## Slide 1: SAFE CNC MACHINE
Design Review VI
Team 514: Samuel Byers, Amanda Garcia-Menocal, Shelby Gerlt, Malik Grant, Carlton Walker
April 1, 2025
Notes: Good evening, this is Team 514 presenting our design review 5 for the safeguard for the cnc router machine

## Slide 2: Team 514
Shelby Gerlt
Samuel Byers
Amanda Garcia-Menocal
Malik Grant
Carlton Walker
Supply Chain Engineer
Structural Engineer
Test Engineer
Electrical Engineer
Design Engineer
Malik Grant
Notes: Here displayed is Team 514 you have Sam, Amanada, Shelby, Myself, and Carlton

## Slide 3: Guidance and Sponsorship
Dr. Eric Hellstrom
Advisor
Dr. Shayne McConomy
Sponsor
Malik Grant
Notes: For this project we are being sponsored by Dr. McConomy and we are being advised by faculty Dr. Hellstorm

## Slide 4: Project Objective
The objective of this project is to design safeguards for the Senior Design Lab’s CNC router to protect students and staff from hazards and mitigate the need for PPE.
Shapeoko 3 CNC Router
Malik Grant
Notes: The objective of this project is to make the Senior Design Labs CNC router safe for student use without requiring additional supervision. This will be achieved by developing machine safeguards that limit the need for Personal Protective Equipment (PPE) in the room while the machine is in operation.

## Slide 5: Hazards
Moving Parts
Projectiles
Impalement
Particles
Amanda Garcia-Menocal
Notes: To start brainstorming ideas wanted to first start establishing our main hazards our users could encounter. First, the CNC machine has multiple moving parts that could cause pinch hazards or potential clothing or hair being pulled into the machine. Next we have the projectiles, Sharp objects have potential to to harm our users so we want to ensure our enclusire prevents materials like plastics, aluminum, or wood to not be able to harm anyone. Next, the CNC has a drill bit that can cut off someones finger if it interacts with the machine. That is major hazard and we want to prioritize no acess to the machine at anytime it is running. Finally, we want to control the amount of particles that could be produced in the air. The enclusre will be sealed just enough to ensure no partilces like dust will escape into the air.

## Slide 6: Critical Targets and Metrics
Function
Halt projectiles
Limit access while running
Create no interference
Target
 4,000 N
Fully operable
2 ± 0.2mm
Metric
Impact force
Clearance
User observation
Amanda Garcia-Menocal
Notes: Based on our central hazards we wanted to address regarding the objective, we developed our critical targets and metrics based on these hazards. First we want our safeguard to halt projectiles from our users. The enclosure will able to withstand a projectile that is equal to or more than 4000 N. Next, our enclosure will create no interference with the cnc machine as it is running. We will be basing this off user observation and the machine being fully operable. And finally our last target we want to limit any access to the machine. For our target of plus or minus 2.02 mm we want it to be sealed but not fully sealed for pressure issues while using the vaccum attachment.

## Slide 7: Assessed Hazards
Moving Parts
Projectiles
Impalement
Particles
Amanda Garcia-Menocal
Notes: The objective of this project is to make the Senior Design Labs CNC router safe for student use without requiring additional supervision. This will be achieved by developing machine safeguards that eliminate the need for Personal Protective Equipment (PPE) in the room while the machine is in operation.

## Slide 8: Implemented Safety Functions
Moving Parts
Projectiles
Impalement
Particles
Enclosure
Amanda Garcia-Menocal
Notes: The objective of this project is to make the Senior Design Labs CNC router safe for student use without requiring additional supervision. This will be achieved by developing machine safeguards that eliminate the need for Personal Protective Equipment (PPE) in the room while the machine is in operation.

## Slide 9: Implemented Safety Functions
Moving Parts
Projectiles
Impalement
Particles
Enclosure
Automatic Shutoff
Automatic Shutoff
Amanda Garcia-Menocal
Notes: The objective of this project is to make the Senior Design Labs CNC router safe for student use without requiring additional supervision. This will be achieved by developing machine safeguards that eliminate the need for Personal Protective Equipment (PPE) in the room while the machine is in operation.

## Slide 10: Implemented Safety Functions
Moving Parts
Projectiles
Impalement
Particles
Enclosure
Automatic Shutoff
Emergency Shutoff
Amanda Garcia-Menocal
Notes: The objective of this project is to make the Senior Design Labs CNC router safe for student use without requiring additional supervision. This will be achieved by developing machine safeguards that eliminate the need for Personal Protective Equipment (PPE) in the room while the machine is in operation.

## Slide 11: Safety Logic
Amanda Garcia-Menocal

## Slide 12: Enclosure Design
Carlton Walker
37 in
38 in
25 in

## Slide 13: Enclosure Design
Front view:
Side view:
Carlton Walker

## Slide 14: Enclosure Design
Front view:
Side view:
Carlton Walker

## Slide 15: Door Catch
Carlton Walker

## Slide 16: Door Design
Carlton Walker
18.35 in
24in

## Slide 17: Door Design
Carlton Walker
Symmetrical
Table clearance

## Slide 18: Electrical Design – Components
Shelby Gerlt
E-Stop and Power Switch always active
Limit Switches in parallel with Key Switch
Notes: The way the system would be powered is displayed in this diagram with the essential parts including limit switches on the doors, power source relay on/off switch, and emergency shut off button. The doors will have two limit switches on each side of the door to ensure for contact with the frame. The limit switches will be powered directly from the power source of the machine which is being powered from the room outlet. If the door is not fully in tack then the machine will not be powered. But now if the machine wants to be in use while the doors are open that is when you would use the power source relay on/off button to send the current directly to the machine. And finally, the emergency stop button will cut all power through the series of wire for the whole machine. We are using 12 gauge wiring to feed the current throughout the system

## Slide 19: Electrical Design – Limit Switches
Cable Lug Adapters
1
2
3
Terminal Diagram
1: Common
2: Normally Open
3: Normally Closed

## Slide 20: Electrical Design – Placement
Shelby Gerlt
Wiring to components runs through 80/20 frame
Secondary outlet inside of enclosure
Notes: The way the system would be powered is displayed in this diagram with the essential parts including limit switches on the doors, power source relay on/off switch, and emergency shut off button. The doors will have two limit switches on each side of the door to ensure for contact with the frame. The limit switches will be powered directly from the power source of the machine which is being powered from the room outlet. If the door is not fully in tack then the machine will not be powered. But now if the machine wants to be in use while the doors are open that is when you would use the power source relay on/off button to send the current directly to the machine. And finally, the emergency stop button will cut all power through the series of wire for the whole machine. We are using 12 gauge wiring to feed the current throughout the system

## Slide 21: Cable Management
Dust cover to hide wiring
CNC plugs directly into the secondary outlet
Shelby Gerlt

## Slide 22: Vacuum Collection Design
Dust Separator
Festool Shop-vac
Samuel Byers
Dust Sweeper

## Slide 23: Vacuum Hose Design
Samuel Byers
2.0”

## Slide 24: Vacuum Hose Design
Samuel Byers
2.0”
1.8”

## Slide 25: Project Cost Breakdown
Samuel Byers
Chart: 
| Budget | Spent | Remaining
 | 2000 | 1896.1862 | 103.8138
Electrical
$60
Base
$59
Metal
$700
Hardware
$437
Polycarbonate
$428
Notes: The next item is the budget for this project. We have a budget of $2,000. The total projected cost listed here is $1600. However, due to a very recent change in suppliers, the total projected cost is closer to $1500.
We are using two different suppliers. The first supplier is Grainger because they offer an academic discount to FSU. Whatever we could source from Grainger, we are ordering from McMaster-Carr.
We also took inventory of the materials available in the senior design lab. Whatever materials we could use, we set aside and this has been taken into account for our projected costs.
Projected costs have also taken into account taxes, shipping, and any cutting and assembly fees.

## Slide 26: Aluminum Extrusion Material Selection
Modular
Good strength-to-weight ratio
Long-term solution
Simple assembly
Corrosion resistant
1.50”
1.50”
Samuel Byers
Notes: Next, we want to go into more detail about why we chose the materials that we did.
For the frame, we will be using aluminum extrusions, 1.5” by 1.5”, hollow interior, ultra-lightweight, and smooth-sided.
Compared to other materials we considered, such as wood, aluminum extrusion has a number of pros.
It is modular, allowing us to easily make changes as we go along. It also allows the professor, TAs, and even future teams to easily change or make additions to the enclosure.
It has great strength-to-weight ratio, especially compared to wood, and is a long-term solution.
It is also very easy to assemble. It has T-slots on each side allowing for items to easily slide in and out.
And it is corrosion resistant.

## Slide 27: Polycarbonate Material Selection
Pros
Impact resistance
Durability
Heat tolerance
Samuel Byers
Notes: For the siding, we will be using polycarbonate, a quarter of an inch sheets.
Compared to other materials we considered, such as acrylic, polycarbonate has a number of pros.
It is much more impact resistant and durable than acrylic. And is heat tolerant for any heat that might be generated by the machine.

## Slide 28: Polycarbonate Material Selection
Pros
Impact resistance
Durability
Heat tolerance
Cons
Scratch sensitivity
UV degradation
Chemical sensitivity
Samuel Byers
Notes: However, polycarbonate does have some cons.
Polycarbonate is scratch sensitive. To mitigate this, we want to potentially test using a clear coating over the polycarbonate, similar to what they use on polycarbonate safety goggle lenses.
Polycarbonate is also prone to UV degradation. However, because the enclosure is located in a room with no windows and only artificial lighting, this will not be an issue.
And finally, polycarbonate is sensitive to certain chemicals. To clean the siding, you can use mild dish detergent soap diluted with water.
But you cannot use solvents (such as acetone), strong acids or bases, ammonia-based cleaners, or abrasive cleaners.
To mitigate this, we plan to include this in the operation manual and potentially include a sticker on the side of the enclosure with a warning.

## Slide 29: Hazard Communication
Samuel Byers
Operation Manual
Subsystem descriptions
Operation of safety system
Troubleshooting
Maintenance Guidelines

## Slide 30: Hazard Communication
Samuel Byers
Operation Manual
Machine Hazard Signage

## Slide 31: Future Work
Design Review 6
Finish installing electrical parts and mounts
Print final version of operation manual
Test all safety functions
Install and level base
Samuel Byers
Notes: For future work, we will finish ordering all materials. At this point, we have ordered almost everything except for the base and electrical components.
Once the materials come in, we will begin to assemble the enclosure hopefully right after spring break.
From there, we can install and level the enclosure in its designated location in the senior design lab, install the vacuum hose, and complete the electrical wiring.
Finally, we will test the design and verify risk reduction to make sure the safety functions are working properly.
Thank you, this concludes our presentation. And we will open it now up to any questions.

## Slide 32: Lessons Learned
Samuel Byers
Trust but verify
Document, document, document (and organize)
Make parts as easy to replace as possible
Hold people accountable to the timeline
Communicate, communicate, communicate
Notes: For future work, we will finish ordering all materials. At this point, we have ordered almost everything except for the base and electrical components.
Once the materials come in, we will begin to assemble the enclosure hopefully right after spring break.
From there, we can install and level the enclosure in its designated location in the senior design lab, install the vacuum hose, and complete the electrical wiring.
Finally, we will test the design and verify risk reduction to make sure the safety functions are working properly.
Thank you, this concludes our presentation. And we will open it now up to any questions.

## Slide 33: Project Objective
Implement safeguards for the CNC router to:
Mitigate the need for PPE
Protect students and staff from hazards
Shapeoko 3 CNC Router
Shelby Gerlt
Notes: The objective of this project is to make the Senior Design Labs CNC router safe for student use without requiring additional supervision. This will be achieved by developing machine safeguards that limit the need for Personal Protective Equipment (PPE) in the room while the machine is in operation.

## Slide 34: Stakeholders
FAMU-FSU COE
Tripp Lappalainen
Jacob Schmitt
Elias Haase
FAMU-FSU COE
Shelby Gerlt

## Slide 35: Critical Target: Halt Projectiles
Target | 3000 N
Metric | Impact force
Testing | Impact test
Shelby Gerlt
Notes: To test the ability of a selected barrier to halt projectiles, an impact test will be performed.

## Slide 36: Critical Target: Create No Interference
Target | Pass
Metric | Pass/Fail
Testing | Observation
Shelby Gerlt
Notes: To test whether the design creates no interference, the machine will be tested with the safeguards in place to check that it can successfully complete a cycle.

## Slide 37: Critical Target: Limit Access When On
Target | True
Metric | Pass/Fail
Testing | Observation
Shelby Gerlt
Notes: To test whether the machine prevents the user from accessing it, the machine will be turned on and a subject will attempt to access it. In the case that the access is overridden, the machine will have a limit switch to shut it down.

## Slide 38: Hierarchy of Functions
CNC Safeguard
Protection
Non-mechanical hazards
Mechanical hazards
Interface
Communication
Control
Collect dust
Dampen noise
Halt projectiles
Prevent contact with point of operation
Prevent contact with power transmission
Create no interference
Communicates hazards
Communicates proper use
Stops use of incorrect materials
Limit machine access when running
Shelby Gerlt
Notes: Hierarchy of functions outlines the goals we have for our design. The primary functions are to halt projectiles, create no interference, and limit machine access while running

## Slide 39: Hierarchy of Functions
CNC
Protection
Non hazards
M hazards
Interface
Comm
Control
Collect
Dampen
Halt
Prevent
Prevent
Create
Comm
Comm
Stops
Limit
Non-mechanical hazards
Mechanical hazards
Collect dust
Dampen noise
Halt projectiles
Prevent contact with point of operation
Prevent contact with power transmission
Create no interference
Protection
CNC Safeguard
Shelby Gerlt
Notes: One of the main hazards is projectiles, in case of this our design has to be able to counter or stop projectiles from hitting anyone near the machine.
The safeguard design must also not prevent the machine from functioning as intended.

## Slide 40: Hierarchy of Functions
Interface
Communication
Control
Communicates hazards
Communicates proper use
Stops use of incorrect materials
Limit machine access when running
CNC Safeguard
CNC
Protection
Non hazards
M hazards
Interface
Comm
Control
Collect
Dampen
Halt
Prevent
Prevent
Create
Comm
Comm
Stops
Limit
Shelby Gerlt
Notes: Final critical target, the design will prevent anyone from accessing the router while it is on. This means the user will not be able to come into contact with the machine at all while it is running.

## Slide 41: Targets: Mechanical
Samuel Byers
Function | Target | Metric
Prevent contact w/ point of operation | Particle levels < 5 mg/m3 | Clearance
Prevent contact w/ power transmission | Noise levels < 85 dB | Clearance

## Slide 42: Targets: Non-Mechanical
Samuel Byers
Function | Target | Metric
Collect Dust | Particle levels < 5 mg/m3 | Particulates
Dampen Noise | Noise levels < 85 dB | Decibel

## Slide 43: Targets: Interface
Samuel Byers
Function | Target | Metric
Prevent use of incorrect materials | Customer uses proper materials | User opinion

## Slide 44: Targets: Beyond the Functions
Samuel Byers
Function | Target | Metric
Manage Cables | Visibility of wires/aesthetics | Sponsor opinion
Disassemble Quickly | < 1 day | Time
Limit Vibrations | 5 ± 0.5 mm | Displacement

## Slide 45: Assumptions to Guide the Design
The user will understand how to use the machine
The machine will be properly maintained
The user will not be using PPE
Only compatible materials will be used in the machine
Samuel Byers

## Slide 46: Medium Fidelity Concepts
Malik Grant
Horizontal sliding door
Vertical sliding door
Double sliding door
Top-hinge door
Bifold door
Notes: For our concept selection, we first started with generating 100 different ideas centered around our critical targets. After developing these ideas from each member of the team we came together to narrow down our concepts to 5 medium fidelity concepts and 3 high fidelity concepts. We used different processes to rank these concepts. For our 5 medium fidelity concepts, we were able to get real life comparisons and were able to pull different features that would be best for our prototype.

## Slide 47: High Fidelity Concepts
Malik Grant
Roll cover
Hatch
Oven door
Notes: Here is our 3 high fidelity concepts,

## Slide 48: Concept Selection
Samuel Byers
Concepts

## Slide 49: Concept Selection
Samuel Byers
Impact force
Clearance
Limited access
Disassembly time
Displacement due to vibration
Characteristics
Concepts

## Slide 50: Concept Selection
Samuel Byers
Selection
Impact force
Clearance
Limited access
Disassembly time
Displacement due to vibration
Characteristics
Concepts

## Slide 51: Final Selection
Samuel Byers
Horizontal sliding door
Vertical sliding door
Double sliding door
Top-hinge door
Bifold door

## Slide 52: Changes from Initial Concepts
Carlton Walker
Front Opening Doors
Auto-Off Hinge
Back Door
Preliminary Designs CAD
Updated Design

## Slide 53: Electrical Design
Power Source
Breaks Series
Amanda Garcia-Menocal
Breaks Series
Notes: The way the system would be powered is displayed in this diagram with the essential parts including limit switches on the doors, power source relay on/off switch, and emergency shut off button. The doors will have two limit switches on each side of the door to ensure for contact with the frame. The limit switches will be powered directly from the power source of the machine which is being powered from the room outlet. If the door is not fully in tack then the machine will not be powered. But now if the machine wants to be in use while the doors are open that is when you would use the power source relay on/off button to send the current directly to the machine. And finally, the emergency stop button will cut all power through the series of wire for the whole machine. We are using 12 gauge wiring to feed the current throughout the system