## Slide 1: Green Propellant Thrust Stand
Team 517
Jeffrey Hill, Aidan Hoolihan, Ryan Kaczmarczyk,
Nicholas Jensen, Edward Zapert
02/20/2025

## Slide 2: Team Sponsors & Advisors
Nicole Vaughn
Liquid Propulsion Engineer
Alexandre Berger, Ph.D.
Assistant Professor
Shayne McConomy, Ph.D.
Professor
Ebony Bland
Aerospace Engineer
Aidan Hoolihan
Marshall Space Flight Center
Sponsors:
Advisors:

## Slide 3: Team Introductions
Jeffrey Hill
Thermal Fluids Engineer
Ryan Kaczmarczyk
Controls Engineer
Aidan Hoolihan
Materials Engineer
Nicholas Jensen
Manufacturing Engineer
Edward Zapert
Design Engineer
Aidan Hoolihan
Presenter
Presenter
Presenter

## Slide 4: Objective
The objective of this project is to develop a thrust stand that can take accurate measurements of a 0.1N green propellant thruster.
Aidan Hoolihan

## Slide 5: Project Background
Aidan Hoolihan
Green Propellant
Current Uses
GPIM Tech demonstration Mission
Cheaper and safer than hydrazine
Requires less fuel onboard
Lunar Flashlight CubeSat mission to map ice on the moon
Notes: new alternative to typical rocket fuel SA hydrazine
Of interest because it is cheaper and safer than what is currently used
This new propellant has only been part of a few missions those being:
Lunar south pole

## Slide 6: What Makes a Good Thrust Stand?
Aidan Hoolihan
To answer this question lets first look at an example:
Pictured on the right is what NASA-MSFC currently uses for micro thrust measurement
Thrust stand is fired in vacuum
The 0.1N thruster collects data that is small and easily skewed
Thruster pushes upward to rotate see-saw, pushing into force sensor
Wires/piping through stand power sensors and provide propellant
Flame bucket diverts heat away from stand
Current stand is made of aluminum
Notes: To achieve our objective, we first took a look at what is currently used by the folks at MSFC

## Slide 7: What Makes a Good Thrust Stand?
Aidan Hoolihan
What does this tell us about our sponsors needs?
NASA-MSFC
Gathered Insights
Meetings
Lab Visit
Improvement Areas
Defined Needs
Refined Details
Notes: It took many meetings and even a visit to the NASA-MSFC laboratory in Huntsville Alabama for Team 517 to learn these details about the current thrust stand
After more communication with sponsors, Team 517 learned that not all these characteristics are positive, and others have significant room for improvement
The next task was interpreting our conversations to lay out groundwork for our customers needs
This involved many team meetings, along with many zoom calls with our sponsors to iron out details of the design

## Slide 8: What Makes a Good Thrust Stand?
Pictured previously is what NASA-MSFC currently uses for micro thrust measurement
Thrust stand is fired in vacuum
The 0.1N thruster collects data that is small and easily skewed
Thruster pushes upward to rotate see-saw, pushing into force sensor
Wires/piping through stand power sensors and provide propellant
Flame bucket diverts heat away from stand
Current stand is made of aluminum
Aidan Hoolihan
Team 517’s Interpreted Needs
Design must be able to take measurements of a micro thruster
Thrust stand must be capable of enduring and functioning in a high vacuum environment, where it cannot be reached by users
Collected data must be precise, and account for environmental and computational error to ensure precision
If a see-saw mechanism is used, it must be able to lock to prevent unwanted movement during transport
Thrust stand should have good wire management and spacious enough to include the propellant piping
Design must have a mechanism that diverts heat to an empty region of the vacuum
Aluminum is a material concern due to corrosion; another material must be selected for the design that is non-corrosive

## Slide 9: Design Process: Ideation
Ideas
Aidan Hoolihan
Key Features
Calibrates Remotely
Easy to clean
Precise measurement
Error calculation
Locking mechanism
Lightweight
non-corrosive material
No larger than 12x18 in
Key characteristics for the thrust stand were identified through ideation and selection.
Methods used: Binary Pairwise, Pugh Charts, and House of Quality.
The process helped determine essential vs. flexible features.
Key features shaped the original design and its iterations.

## Slide 10: Design Iteration #1
Nicholas Jensen
Calibration Mechanism
Flame Bucket
Terminal Blocks
Vibrational Damping
Pros
Cons
Low resonant frequency
Low cost
Easy to clean
High visibility
Moment induced on linkage
Unrealistic proportions
Minimalistic

## Slide 11: Design Iteration #2
Nicholas Jensen
Calibration Linkage
Calibration Weight Module
Thruster Linkage Mount
Structural Components
Sensor Mount
Pros
High resonant frequency
Cons
Hard to manufacture
Calibration setup with heavy linkage
Modular
Low visibility
No link pivot integration
Limited room near thruster to work

## Slide 12: Final Design
Nicholas Jensen
Updates
Redesigned structure
Thruster
Calibration weight
Bearings
Improved calibration method
Interchangeable sensor mounts
Bolt design
Machinability
Optimized mounts

## Slide 13: Final Design
Nicholas Jensen
Solenoid Valve
Thruster
Thruster Link Mount
Thruster Block

## Slide 14: Final Design
Nicholas Jensen
WIKA Force Sensor
Calibration Weight Hook
Bearing Mount
Preload Weight

## Slide 15: Final Design
Nicholas Jensen
Modular Terminal Blocks
Calibration Weight
Stepper Motor Calibration Lift

## Slide 16: Design Validation: Modal Analysis
Design Goal: Create stand with resonant frequencies around 700Hz
Edward Zapert
Initial Design
Run Modal Analysis
Once
f ≈ 700 Hz
Final Results

## Slide 17: Design Validation: Thermal Analysis
Design Goal: Model heat transfer from thruster to validate sensor placement
Edward Zapert
Dual Heat Sources
  Thruster and Solenoid
30 Second Steady Thruster Fire
Key
- Tungsten Core
- Rhenium Body
- Titanium Mount
- 304 S.S. Block
Results after 30 seconds
Maximum Contact Temp of 20ºC

## Slide 18: Current Budget
Edward Zapert
Chart: 
| Budget | Spent | Remaining
 | 2000 | 667.8009 | 1332.1991
Supplied by Sponsor
FAMU-FSU Engineering
WIKA Model F2221 Force Transducer ($1500)

## Slide 19: Current Expenses
Raw Material
Hardware
Bearings
$493.49
$68.07
$105.24
Edward Zapert
304 Stainless Steel Plating
Screws, Hooks, Standoffs
Ceramic Bearings

## Slide 20: Future Work
Edward Zapert
Machining and Assembly
Documentation
Send purchased parts to machine shop and assemble final stand
Create CAD drawings and begin assembly manual
Test WIKA sensor using 3D printed test equipment
Sensor Testing

## Slide 21: Future Work: Roadblocks
Potential budget issues with next trip to NASA-MSFC in Huntsville
Machining times
Error analysis coding
  Trial and error needed to process sensor data and filter noise.
  Debugging the uncertainty model may delay accurate thrust validation.
Edward Zapert

## Slide 22: Quick Recap
Vacuum Conditions
Remote Calibration
ASCENT
    NASA MSFC
    FAMU-FSU COE
Edward Zapert
Background
Green propellant is safer and more efficient than hydrazine
Design Validation
Modal analysis ran to verify natural frequency
Accurately measure the thrust of a 0.1N green propellant thruster
Key Goals
Minimize uncertainty
Remotely calibrate under vacuum
Thermal analysis ran to verify temperature output near sensor

## Slide 23: Slide Headline
Try to keep text at 16 pt minimum.
Try to put as few words as possible on the slide if you’re using for a presentation.
Mix and match the backgrounds as shown in this template or just use one throughout.
You can put department/unit logos in slide master at Horizontal 0.89” Vertical 6.44” From top left corner

## Slide 24: Font Check
This is 10-point
This is 15–point Times
This is 20–point
This is 25–point
This is 30–point
This is 35–point
This is 40–point
This is 50–point
This is 60–point
This is 72–point
Notes: Use at least 20-point font in Room A105, B134, and B136
Use at least 25-point font in Room B135

## Slide 25: College of Engineering Color Palette
Fang
Orange
RGB: 238, 118, 36
Hex: #EE7624
CMYK:2, 66, 99, 0
1 2 3 4
1 2 3 4
White
Pantone: PMS 000C
RGB: 255, 255, 255
Hex: #FFFFFF
CMYK: 0, 0, 0, 0
1 2 3 4
Black
Pantone: Black C
RGB: 0, 0, 0
Hex: #000000
CMYK:0, 0, 0, 100
Garnet
Pantone: PMS 195 C
RGB: 120, 47, 64
Hex: #782F40
CMYK:19, 90, 50, 55
1 2 3 4
Notes: Avoid 75% Black in B135

## Slide 26: Accent Color Palette
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
1 2 3 4
Turquoise
RGB: 64, 224, 208
Hex: #40E0D0
CMYK:
1 2 3 4
American Orange
RGB: 255, 139, 0
Hex: #FF8B00
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Asagi-iro
RGB: 72, 146, 155
Hex: #48929b
CMYK:
1 2 3 4
Gainsboro
RGB: 220, 220, 220
Hex: #DCDCDC
CMYK:
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Imperial
RGB: 104, 40, 96
Hex: #682860
CMYK:
1 2 3 4
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Notes: Remove American orange add hyperlink grey
Make corn the last for b135
All work in 134 imperial move later
Tardis doesn’t work in b136

## Slide 27
https://color.adobe.com/create/color-wheel
Analogous
F7AB19
D67F15
EE7624
D64615
F73119
Monochromatic
6E3610
F0A16C
EE7624
6E4931
BASB1C
Triad
A14508
4BED3B
EE7624
250CED
2010A1
Complementary
FF8C40
EE7624
0098A1
24E2ED
A1470C
Split Complementary
28A164
2FED8D
EE7624
0848A1
1871ED
Double Split Complementary
3BED93
EE7624
0C6AED
ED2F18
EDAC2F
Square
C7ED3B
EE7624
0CE1ED
A418ED
ED660C
Compound
87724A
EE7624
60EFCF
09BA61
BA7E09
Shades
6E3610
EE7624
FA7625
D46820
AD551A
Notes: These are the variants that work well with Fang Orange. The bolded items show well on the projectors.

## Slide 28
https://color.adobe.com/create/color-wheel
Analogous
85412D
8F3831
782f40
8F3176
792D85
Monochromatic
C44D69
8E626D
782F40
C48796
451B25
Triad
C43959
78743B
782F40
236178
43A2C4
Complementary
C46078
782F40
25C43D
2F783A
C43959
Split Complementary
93C460
577835
782F40
39C49D
297861
Double Split Complementary
5A783B
782F40
237860
6E2978
784435
Square
78683b
782F40
237830
293978
782337
Compound
DEBAAF
782F40
5D8555
70AB32
AB4D32
Shades
C44D69
782F40
853447
5E2532
38161E

## Slide 29
B135 Stage Right
A105
A105
B135 Stage Left
B135
B134, A105
B136

## Slide 30
Border Line
Middle of Slide
Middle of White Space
Border Line
Border Line
Center of White Space
Center of Slide
Border Line
Edge of Branding
Notes: Vertical lines from top down.
Borderline and top of title. (0.5 inch)
Center of Slide (0 inch y-direction for the entire slide)
Center of Design Content (0 inch y-direction considering the title, footer, and negative space)
Bottom of Design Content (0.25 in gap to the footer. 0.75 to the bottom of the screen)
Horizontal lines from left to right
Borderline (0.5 inch)
Center of design content.
Center of slide (0 inch y-direction for the entire slide)
Borderline (0.125 inch all around)