## Slide 1: Manufacturing for STEM Engagement
DR 5 – Team 521
Carlos Aceituno, Tristian Belardo, Leah Bergman, and Xavier Hammond
1/23/25

## Slide 2: Team Members
Carlos Aceituno
Mechanical Engineer 1
Presenter
Xavier Hammond
Mechanical Engineer 2
Tristian Belardo
Electrical Engineer 1
Presenter
Leah Bergman
Electrical Engineer 2
Carlos Aceituno
Notes: This is our team

## Slide 3: Sponsors & Advisors
Tajaey Young
Digital Services
Sales Manager
Camilo Ordóñez, Ph.D.
Teaching Faculty I
Carlos Aceituno
Shayne McConomy, Ph.D.
Teaching Faculty II
Shayla George
Software & Control Technology Consultant
Cliff Rice
Automotive,
Electric Vehicle,
and Battery Industry Consultant
James Fadool
Global OEM
Technical Consultant
Notes: Here we have our sponsors and advisors for our project. Our sponsor is Rockwell Automation and their team consists of Tajaey Young, Shayla George, Cliff Rice, and James Fadool. Next we have our advisors from the FAMU-FSU College of Engineering. Our project advisor is Dr. Camilo Ordonez and our senior design professor Dr. Shayne McConomy

## Slide 4: Objective
Educate and foster engagement in manufacturing engineering through an automated demonstration.
Carlos Aceituno
Notes: The objective of this project is to educate and foster K-12 engagement in manufacturing engineering through an automated demonstration.

## Slide 5: Project Overview
Carlos Aceituno
Rockwell Automation is a global leader in industrial automation and Control Systems
Create a button pin machine that uses automation and manufacturing concepts
Increase K-12 interest in Manufacturing Engineering and STEM in general

## Slide 6: Project Impact
Carlos Aceituno
Chart: Percentage of U.S. students at or above proficient by subject area (2018-2019)
| Mathematics | Science | Technology/Engineering
Grade 4 | 41 | 36
Grade 8 | 34 | 35 | 46
Grade 12 | 24 | 22
Source: U.S. Department of Education, Institute of Education Sciences, National Center for Education Statistics, National Assessment of Educational Progress (NAEP) 2018-2019
Notes: Rockwell Automation tasked our team with creating a device to assist with STEM engagement
The overall goal of this device is to find a way to introduce students to the world of manufacturing and engage them in a way such that they would want to pursue such a career in this field.
Mention “BRIDGING THE GAP BETWEEN K-12 STUDENTS AND MANUFACTURING”
Important: all percentages below 50 and decreasing as grade level increases

## Slide 7: Project Background
Carlos Aceituno
Move pin bottom dye under press.
Move pin bottom dye to ejection.
Return dye home.
Lower entry
ramp.
Raise entry
ramp.
1
2
Move pin top dye under press.
Move pin dye top to orientator.
1
2
3
4
5
6
7
Press linear actuator down.
On
Notes: This is the run through of the CURRENT process
Note that the numbers are out of order on purpose (Wiring technique used by old team)

## Slide 8: Key Goals
Carlos Aceituno
Number of Update Messages: ≥ 4
Production Rate:
60 < x < 90 seconds
Failure Rate: < 2%
Teach the audience about automated manufacturing.
Improve reliability of the system.
Produce a tangible item for the user to keep.
Notes: To ensure quality products
Showcase to students the manufacturing process
An item that students can take with them is critical to the learning process and we want to continue this trend
This slide is used to connect our key goals to our targets and metrics
Old team was not able to make a fully automated system
Target audience are K-12 students // Rockwell wants to make an engagement device to teach this audience
An item that students can take with them is critical to the learning process and we want to continue this trend

## Slide 9
Carlos Aceituno
Final Selected Design
User-controlled claw
Human machine interface
Notes: Our final selected design includes
Human machine interface // User controlled claw

## Slide 10: SolidWorks Study
Carlos Aceituno
Gravity
Actuator press and component weight
Forces
Fixed linear actuator
Notes: RECAP: Major issue of frame bending upon actuation
Goal: see if the bowing we see happening can be virtually replicated to test different solutions before any purchasing or physical modifications are made.
240 lbs for actuator press (200 static, 40 dynamic) and ~ 25 lbs for actuator and mount weight

## Slide 11: SolidWorks Study
Carlos Aceituno
Gravity
Actuator press and component weight
Forces
Notes: RECAP: Major issue of frame bending upon actuation
Goal: see if the bowing we see happening can be virtually replicated to test different solutions before any purchasing or physical modifications are made.
240 lbs for actuator press (200 static, 40 dynamic) and ~ 25 lbs for actuator and mount weight

## Slide 12: SolidWorks Study
Carlos Aceituno
Gravity
Actuator press and component weight
Forces
Fixed linear actuator
Notes: RECAP: Major issue of frame bending upon actuation
Goal: see if the bowing we see happening can be virtually replicated to test different solutions before any purchasing or physical modifications are made.
240 lbs for actuator press (200 static, 40 dynamic) and ~ 25 lbs for actuator and mount weight

## Slide 13: Displacement
Carlos Aceituno
Table
Notes: Click to add arrows!!
Fixed linear actuator = low displacement (must have a fixed component to run SolidWorks study, no table in the workspace)
High displacement on the ends (will displace more on left side in reality because SolidWorks study does not include the weight of all the components of the right side)

## Slide 14: Frame Bending Solutions
Carlos Aceituno
Notes: This is to relate what we’re doing to provide support compared to what other people are already doing to increase support

## Slide 15: 1st Iteration Frame Solution
Carlos Aceituno
Notes: All force is on the two inner bars (that the actuator is fixed to), adding the top bar distributes the weight among the outside bars as well. The bottom bars serve the same purpose, and the frame is mechanically shortened without any actual reduction of length.

## Slide 16: 2nd Iteration Frame Solution
Carlos Aceituno
Notes: All force is on the two inner bars (that the actuator is fixed to), adding the top bar distributes the weight among the outside bars as well. The bottom bars serve the same purpose, and the frame is mechanically shortened without any actual reduction of length.

## Slide 17: PLC Implementation
Programmable Logic Controller
  Hard real-time system
Two Ethernet ports
Analog I/O card
Tristian Belardo
Single-box
Modular
Notes: Hard real-time system: output results are produced in response to input condition within a limited time or else failure
Single-box: brick, fit all units and interfacing into one compact casing
Modular: rack, space for modules with different functions (i.e. power supply, processor, I/O modules)
Ethernet ports: Connects system to a computer and enables Human Machine Interface (HMI)
Analog I/O card (Local expansion module): Individually configure channels, enable/disable channels individually, auto calibration of inputs, high accuracy rating

## Slide 18: Code Flowchart
Tristian Belardo
Start
Load Materials (Manual)
Check Safety Sensor
Start Button Pressed (machineState = RUNNING)
Move Conveyor to TOP_DIE Position
Actuator Down
Actuator Up
Move Conveyor to BOTTOM_DIE Position
Actuator Down
Actuator Up
Move Conveyor to FINISH Position
Reset Button Pressed (machineState = IDLE)
Move Conveyor to START Position
End
NO
YES
t == LIMIT
t == LIMIT

## Slide 19: Code Flowchart
Tristian Belardo
Start
Load Materials (Manual)
Check Safety Sensor
Start Button Pressed (machineState = RUNNING)
NO
YES

## Slide 20: Code Flowchart
Tristian Belardo
Move Conveyor to TOP_DIE Position
Actuator Down
Actuator Up
Move Conveyor to BOTTOM_DIE Position
Actuator Down
Actuator Up
Move Conveyor to FINISH Position
t == LIMIT
t == LIMIT

## Slide 21: Code Flowchart
Tristian Belardo
Reset Button Pressed (machineState = IDLE)
Move Conveyor to START Position
End

## Slide 22: Ladder Logic Pseudocode
Tristian Belardo
Power Rail
Ground Rail
+

## Slide 23: Ladder Logic Pseudocode
Tristian Belardo
Power Rail
Ground Rail
+
SAFETY_SENSOR
START_BTN
( RUNNING )
Inputs
Outputs
1

## Slide 24: Ladder Logic Pseudocode
Tristian Belardo
SAFETY_SENSOR
START_BTN
( RUNNING )
STOP_BTN
( PAUSED )
RESET_BTN
( IDLE )
RUNNING
CONVEYOR_SWITCH: START
( CONVEYOR_MOTOR )
( MOVE_TO_TOP_DIE)
CONVEYOR_SWITCH: TOP_DIE
( ACTUATOR_DOWN )
ACTUATOR_DOWN
( ACTUATOR_UP )
TOP_TIMER.EXPIRED
( TOP_TIMER.EXPIRED)
RUNNING
CONVEYOR_SWITCH: TOP_DIE
( CONVEYOR_MOTOR )
( MOVE_TO_BOT_DIE)
CONVEYOR_SWITCH: BOT_DIE
( ACTUATOR_DOWN )
ACTUATOR_DOWN
( ACTUATOR_UP )
BOT_TIMER.EXPIRED
( BOT_TIMER.EXPIRED)
PAUSED
( MOVE_TO_START)
RESET_BTN
Power Rail
Ground Rail
+
1
2
3
4
5
6
7
8
9
10

## Slide 25: Former Wiring Diagram
Tristian Belardo
y-axis of gantry
input ramp
conveyor motor
actuator w/ motor driver
2 DM442
microstep
drivers
3 power supplies + 9-volt battery
1 DM542
microstep
drivers
Notes: 1st click- Power supplies: 2 variable, 1 9-volt, and a 9-volt battery
2nd click – Microstep drivers (control three motors)
3rd click – conveyor motor , y-axis for extraction, input ramp
4th click – Actuator with motor driver and Arduino UNO

## Slide 26: Cost of Industrializing
Tristian Belardo
Chart: 
| Proposed Costs | Actual Budget
Stepper Motor | 1188 | 0
Motor Driver | 4898.92 | 0
Actuator | 6501.48 | 0
Acutal Budget | 2000
Calculated using the cost of Allen-Bradley Components, which Rockwell Automation produces

## Slide 27: Updated Wiring Diagram
Tristian Belardo
y-axis of gantry
x-axis of gantry
2 power supplies + 9-volt battery
Notes: 1st click- Power supplies: All motor drivers controlled by one power supply (use of voltage divider), 24-volt PLC, and 9-volt battery
2nd click –y-axis on claw, x-axis on claw

## Slide 28: New Components
Tristian Belardo
Contact Sensor
Round Electromagnet
Limit Switches
Start/Stop/Reset Buttons
Notes: 1st click- Start/Stop/Reset Buttons
2nd click –y-axis on claw, x-axis on claw

## Slide 29: Arduino to Industrial Sensors
Carlos Aceituno
Limit Switch
Contact Sensor
Buttons

## Slide 30: Budget Update
Carlos Aceituno
Purchase History
Bolts & Brackets
Electromagnet
Ethernet Cord & Adapter
Polycarbonate
Chart: 
| Budget | Spent | Remaining
 | 2000 | 537.0359 | 1462.9641

## Slide 31: Future Work
Tristan Belardo
Receive Materials & Test Frame Support
Redesign Gantry for User-Controlled Claw
PLC Dummy
Code
PLC/Sensor Integration
Ladder Logic Updates

## Slide 32: References
https://www.pewresearch.org/short-reads/2024/04/24/most-americans-think-us-k-12-stem-education-isnt-above-average-but-test-results-paint-a-mixed-picture/#:~:text=In%20science%2C%20the%20U.S.%20ranked,and%20Mexican%20students%20ranked%20lowest.
https://buymagnets.com/product/round-electromagnets-flat-faced/?product_sku=BDE-0515-12
https://www.digikey.com/en/products/detail/omron-electronics-inc-emc-div/SS-3GL13PT/664729
https://www.digikey.com/en/products/detail/adafruit-industries-llc/3942/9658069
https://www.digikey.com/en/products/detail/sparkfun-electronics/COM-10302/5775291
Tristian Belardo
Notes: Auto-scrolls to next slide

## Slide 33: Stay tuned for more!
“Working together, we'll drive better outcomes and achieve results.”
- Rockwell Automation
Tristian Belardo

## Slide 34: Sensor Transition: Arduino to Industrial
Showcase Machine
Accurate Representation
Tristan Belardo

## Slide 35: Ladder Logic Pseudocode
Leah Bergman
STOP_BTN
( PAUSED )
RESET_BTN
( IDLE )
RUNNING
CONVEYOR_SWITCH: START
( CONVEYOR_MOTOR )
( MOVE_TO_TOP_DIE)
CONVEYOR_SWITCH: TOP_DIE
( ACTUATOR_DOWN )
ACTUATOR_DOWN
( ACTUATOR_UP )
TOP_TIMER.EXPIRED
( TOP_TIMER.EXPIRED)
RUNNING
CONVEYOR_SWITCH: TOP_DIE
( CONVEYOR_MOTOR )
( MOVE_TO_BOT_DIE)
CONVEYOR_SWITCH: BOT_DIE
( ACTUATOR_DOWN )
ACTUATOR_DOWN
( ACTUATOR_UP )
BOT_TIMER.EXPIRED
( BOT_TIMER.EXPIRED)
PAUSED
( MOVE_TO_START)
RESET_BTN

## Slide 36: Budget Update
Leah Bergman
Purchase History | 
Part Description | Quantity
Corner Brackets | 30
M6 Head Cap Screws (25 Pack) | 2
M6 Drop-In Nut | 80
Chart: 
| Budget | Spent | Remaining
 | 2000 | 537.0359 | 1462.9641

## Slide 37: Timeline
Importance of project
Reiterate key goals / major issues
Current design breakdown
Final selected design
Wiring breakdown (electronic components)
Introduce biggest change: PLC (add in slides about the labs?)
Code flowchart (what we need PLC to do)
New sensors
Frame bending solution

## Slide 38: Code Flowchart
Leah Bergman

## Slide 39: Planned Component Integration
Limit Switches
Ultrasonic Proximity Sensors
Round Electromagnet
Buttons
Leah Bergman

## Slide 40: Cost of Industrializing
Allen Bradley stepper motor: $2,219.08
Actuator cost
Potential Driver cost
https://plc-direct.com/collections/motors?srsltid=AfmBOorllvfW6e1xjDAjRnOCSKAM7E5V21vqU_Y6JKXGOQNKbRgDe9uk
Leah Bergman

## Slide 41
Leah Bergman

## Slide 42: Concept Selection
Carlos Aceituno
Binary Pairwise Comparison
House of Quality
Pugh Chart
Analytical Hierarchy Process
Final Selection
Notes: For this iteration of the project our group decided to highlight 4 targets and metrics we deemed as critical.
1.

## Slide 43
Carlos Aceituno
Analytical Hierarchy Process
Compare each concept to every engineering characteristic
Normalize the chart:
Normalize the chart: (𝐸𝑎𝑐ℎ 𝑉𝑎𝑙𝑢𝑒)/(𝐶𝑜𝑙𝑢𝑚𝑛 𝑆𝑢𝑚)
Consistency Check:
Consistency Check: 𝑊_𝑠=[𝐶]×{𝑃_𝑖}
Compare each concept to every engineering characteristic
Concept # | Alternative Value
1 | 0.33
3 | 0.36
7 | 0.31
Notes: For this iteration of the project our group decided to highlight 4 targets and metrics we deemed as critical.
1.

## Slide 44: Concept Selection
Xavier Hammond
Binary Pairwise Comparison
House of Quality
Pugh Chart
Analytical Hierarchy Process
Final Selection
Notes: For this iteration of the project our group decided to highlight 4 targets and metrics we deemed as critical.
1.

## Slide 45: Stress
Xavier Hammond
Notes: Fixed linear actuator = low displacement (must have a fixed component to run SolidWorks study, no table in the workspace)
High displacement on the ends (will displace more on left side in reality because SolidWorks study does not include the weight of all the components of the right side)

## Slide 46: Concept Generation
Xavier Hammond
Brainstorming
Biomimicry
Morphological Chart
Notes: Given that our design must manufacture button pins. Our concept generation consisted of creating different ways of manufacturing button pins. For generating our concepts who mainly used these three techniques
Brainstorming: threw ideas out there
Biomimicry: used a claw like structure like a crab's claw to increase user engagement
Morphological Chart: used this make combinations between our ideas.
Used these techniques to generate 100 design concepts for the button bin maker
Combination of the 3 gave us our best designs

## Slide 47: Medium Fidelity Concepts
Touch-screen interface for users to select button color, graphic, and add text before printing their design. (4)
Consists of puzzle-style metal pieces to be easily broken down for storage. (5)
User-controlled claw and a dual axis conveyor belt. (6)
Heat-shrinkable mylar and load sensor beneath the frame to detect uneven pressure distribution and adjust the actuator’s position in real-time. (7)
Easily collapsible frame and touchscreen interface for status display and a vacuum-based arm for extraction and dispensing. (8)
Xavier Hammond
Notes: Include the purpose for doing Medium Fidelity Concepts

## Slide 48: Concept Selection
Carlos Aceituno
Binary Pairwise Comparison
House of Quality
Pugh Chart
Analytical Hierarchy Process
Final Selection
Notes: For this iteration of the project our group decided to highlight 4 targets and metrics we deemed as critical.
1.

## Slide 49
Carlos Aceituno
Binary Pairwise Comparison
Customer Requirements
Completes a cycle in 60-90s.
Contains simple, useful safeguards for errors.
Clearly explained for solo use.
Captures key components of manufacturing and educates user.
Poses no risk to non-technical users.
Expands upon the results of the previous team.
Functions with minimal human intervention.
Easily transported.
Understandable and safe for all ages.
Reliable and realistic as a manufacturing process.
Notes: For this iteration of the project our group decided to highlight 4 targets and metrics we deemed as critical.
1.

## Slide 50
Carlos Aceituno
Binary Pairwise Comparison
High to Low Importance Weight Factor (IWF)
Customer Requirements
Completes a cycle in 60-90s.
Contains simple, useful safeguards for errors.
Clearly explained for solo use.
Captures key components of manufacturing and educates user.
Poses no risk to non-technical users.
Expands upon the results of the previous team.
Functions with minimal human intervention.
Easily transported.
Understandable and safe for all ages.
Reliable and realistic as a manufacturing process.
Notes: For this iteration of the project our group decided to highlight 4 targets and metrics we deemed as critical.
1.

## Slide 51: Concept Selection
Carlos Aceituno
Binary Pairwise Comparison
House of Quality
Pugh Chart
Analytical Hierarchy Process
Final Selection
Notes: For this iteration of the project our group decided to highlight 4 targets and metrics we deemed as critical.
1.

## Slide 52
Carlos Aceituno
House of Quality
Receives Button Pin Materials
Assembles Button Pin
Output Button Pin
Engage User
Realistic Manufacturing Environment
Displays Manufacturing Process
Actuates Upon User Input
Receives Sensor Information
Stops Upon Completion
Maintains Rigidity
Aligns Materials Accurately
Operates by Given Computer Data
Assembles with Ease
Halts in Response to Error or User Input
Engineering Characteristics
Critical Engineering Characteristics
Notes: For this iteration of the project our group decided to highlight 4 targets and metrics we deemed as critical.
1.

## Slide 53: High Fidelity Concepts
Xavier Hammond
Triangular support frame
User-controlled claw
Shock-absorbent material
Gravity-fed storage
Visual alignment marks
Human machine interface
1
2
3
Notes: All high-fidelity concepts contain a user-controlled claw, like a prize claw machine, chosen for its ability to entertain and engage a wide range of ages. As the product is showcased to an audience ranging from 5-18 years old, our team focused on how to maintain engagement for a kindergartener and upperclassmen in high school
Concept 1: Triangular-based support frame, shock-absorbent material mounted linear actuator, user-controlled claw for output of final product
Concept 3:User interface to convey the current manufacturing step, user-controlled claw for output of final product
Concept 7:Heat-shrinkable mylar to cover button design, load sensor beneath the frame that adjusts the actuator in real-time

## Slide 54
Carlos Aceituno
Pugh Chart
1
3
7
User-controlled claw
Triangular support frame
Shock-absorbent material
User-controlled claw
Human machine interface
Load cell
Heat-shrinkable mylar
Notes: For this iteration of the project our group decided to highlight 4 targets and metrics we deemed as critical.
1.

## Slide 55: Concept Selection
Carlos Aceituno
Binary Pairwise Comparison
House of Quality
Pugh Chart
Analytical Hierarchy Process
Final Selection
Notes: For this iteration of the project our group decided to highlight 4 targets and metrics we deemed as critical.
1.

## Slide 56
Carlos Aceituno
Pugh Chart
Critical Engineering Characteristics
Assembles Pin Button
Realistic Manufacturing Environment
Operates by Given Computer Data
Receives Sensor Information
Displays Manufacturing Process
Halts in Response to Error or User Input
Output Button Pin
Critical Engineering Characteristics
Design Concepts
1
2
3
4
5
6
7
8
Datum
Senior Design Team 522:
High School Learning Tool
Not a realistic manufacturing process.
Risk of being too fast to follow.
Notes: CLARIFY WHAT CONCEPTS ARE.
1.

## Slide 57
Carlos Aceituno
Pugh Chart
Critical Engineering Characteristics
Assembles Pin Button
Realistic Manufacturing Environment
Operates by Given Computer Data
Receives Sensor Information
Displays Manufacturing Process
Halts in Response to Error or User Input
Output Button Pin
Critical Engineering Characteristics
Design Concepts
1
2
3
4
7
8
Datum
Not a realistic manufacturing process.
Does not improve output of button.
Easily collapsible frame
Touchscreen interface for status display
Vacuum-based arm for extraction and dispensing
Notes: CLARIFY WHAT CONCEPTS ARE.
1.

## Slide 58: Sponsor Background
Leah Bergman
Philanthropy
Industrial Automation
&
Digital Transformation
Emulate3D Digital Twin
Notes: Rockwell is the largest company in the world dedicated to industrial automation and digital transformation
Emulate3D: software to help design, test, and optimize automation projects
In 2021, 49% (dark blue segment) was donated towards STEM education  Manufacturing for STEM engagement!

## Slide 59: Introduction to Manufacturing and Automation
Manufacturing Process
A series of steps that converts raw materials into finished goods
Mass production of a product
Can range from manual to fully automated
Leah Bergman
Notes: Automation is an ever-growing part of manufacturing, with the continuous development of new technologies. The most common way K-12 schools teach manufacturing is with manual assembly lines. Our goal is to expand into automated demonstrations to promote STEM engagement.

## Slide 60: Current Design
Leah Bergman
Button Top
Design
Mylar
Button Back
Notes: Current design: 3 motors, 3 microstep drivers, Arduino Mega, Arduino UNO
Metal frame with a conveyor belt on the bottom, gantry on top with the die mold
Linear actuator fixed above with the top of the die mold

## Slide 61: Major Issues
Leah Bergman
Malfunctioning conveyor belt
Weak supporting frame
Buttons not working
Notes: When linear actuator presses, the entire frame bends and lifts from the table
Conveyor belt doesn’t move to proper locations because the movement was hard coded without limit switches, so one power supply must be disconnected in between steps
4/9 buttons force a step in the process to start when pressed

## Slide 62: Key Goals
Leah Bergman

## Slide 63: Key Goals
Leah Bergman
Improve reliability of the system
Notes: - As of brief testing we completed last week, the system successfully made three buttons in a row and failed on the fourth.

## Slide 64: Key Goals
Leah Bergman
Teach the audience about automated manufacturing
Improve reliability of the system
Notes: - As it operates now, the system requires a large amount of user interaction to successfully make a button. It lacks successful automation in the design.

## Slide 65: Key Goals
Leah Bergman
Produce a tangible item for the user to keep
Teach the audience about automated manufacturing
Improve reliability of the system
Notes: - In producing a physical item, the audience is more engaged and excited about the process.

## Slide 66
Leah Bergman
Who will the achievements of these goals impact?
Notes: - This leads into the question of “who will the achievements of these goals impact?”

## Slide 67: Markets
Tristian Belardo
Primary/Secondary Markets
After School STEM Clubs
Colleges/Universities
K-12 Institutions
Notes: This brings us to our markets. Our primary market is K -12 Institutions, as that is the target audience of this project. Our secondary markets include after-school STEM clubs and College and Universities where STEM curriculum is also present

## Slide 68: Stakeholders
Tristian Belardo
Rockwell Automation & FAMU-FSU College of Engineering
  Dr. Camilo Ordóñez
Dr. Shayne McConomy
Notes: Our stakeholders for this project include Rockwell Automation and FAMU-FSU College of Engineering. Rockwell Automation would be able to use this product to showcase what exactly their company does in manufacturing world on a small scale, and the FAMU-FSU College of Engineering could use this to promote manufacturing interests for students

## Slide 69: Assumptions
Leah Bergman
System operates with some level of user input
User does not need any prior knowledge to operate the system
System is provided space and power for operation
Notes: - To assure the completion of the product is successful, a few assumptions had to be made.
The goal is automation, not autonomy.
The product is targeted at K-12 schools, which are not filled with people familiar with manufacturing engineering.
The system will be reasonably sized but requires a flat surface and outlets to operate.

## Slide 70: Customer Needs
Industrial
Uses Rockwell technology and hardware when possible
Utilizes more industrial hardened devices
Manufacture
Resembles a realistic manufacturing environment
Completes a cycle in roughly one minute
Automated
Builds upon last years design with focus on automation
Takes user input but completes a cycle on its own
Control
Includes start/stop buttons and pause input
Simple enough for use by a non-technical user
Leah Bergman
Notes: INDUSTRIAL: Currently no Rockwell technology/hardware is in use as it operates with Arduinos right now, ideally it uses PLC’s, I/O Blocks, and Sensors
MANUFACTURE: Ensure the audience is engaged and properly educated
AUTOMATED: Focus on moving forwards instead of backwards, more reliable automation built off their design
CONTROL: We don’t want any confusion or safety hazards in the operation of the design

## Slide 71: Functional Decomposition
Tristian Belardo
Rockwell Automation
Manufacturing for STEM Engagement
Manufacture
Educate
Control
Support
Notes: This brings us to our functional decomposition of the Manufacturing for STEM engagement device

## Slide 72: Functional Decomposition
Tristian Belardo
Rockwell Automation
Manufacturing for STEM Engagement
Manufacture
Educate
Control
Support
Notes: We were able to identify 4 subsystems that align with the goals of this project. The subsystems identified are manufacture, Educate, Control, and Support

## Slide 73: Functional Decomposition
Tristian Belardo
Manufacture
Assembles Button Pin
Outputs Completed Button
Receive Button Pin Materials
Notes: The first sub-system is Manufacture, which has three functions. The first function being Receive button materials. The pin buttons are made out of three pieces which is considered our raw materials. The next function is the Assembly of the pin button. The raw materials are then pressed to together to form a completed button. This brings us to the last function where the completed button is outputted to be safely retrieved by the user

## Slide 74: Functional Decomposition
Tristian Belardo
Rockwell Automation
Manufacturing for STEM Engagement
Manufacture
Educate
Control
Support

## Slide 75: Functional Decomposition
Tristian Belardo
Educate
Resembles Realistic Manufacturing Environment
Displays Manufacturing Process
Engage User
Notes: The second subsystem is Educate. Our first function is to engage the user. We want our audience to learn and remember about the manufacturing process. This brings us to our next function that we want to resemble a realistic manufacturing environment. We want to showcase what you would find in a manufacturing environment to spark interest to our audience. Our last function is to display the manufacturing process. We want to ensure that our audience can see each step in the process of making a pin button

## Slide 76: Functional Decomposition
Tristian Belardo
Rockwell Automation
Manufacturing for STEM Engagement
Manufacture
Educate
Control
Support

## Slide 77: Functional Decomposition
Tristian Belardo
Control
Actuates upon User Input
Receives Sensor Information
Stops upon Completion
Halts in Response or Human Override
Notes: Our third subsystem is control. Our first function is Actuates upon user input. The user should be able to give the product input and the product does something. Our next function is to receive sensor information. Once the product starts operating we want to ensure functions are performing accurately. The next function is halts in response or human override. If something gets stuck we want the system to be able to recognize it and stop. This should also happen from user input as well. The last function is stops upon completion. The product should cycle through a completion of 1 pin button then stop.

## Slide 78: Functional Decomposition
Tristian Belardo
Rockwell Automation
Manufacturing for STEM Engagement
Manufacture
Educate
Control
Support

## Slide 79: Functional Decomposition
Tristian Belardo
Support
Aligns Materials Accurately
Assembles with Ease
Maintains Rigidity
Notes: The last subsystem is support. The first function is maintains rigidity. As the product is moving and forming a button we want to ensure that its shell keeps it shape. The next function is aligns materials accurately. We want to ensure that when the button is being formed that it is in the correct position to prevent mistakes. The last function is assembles with ease. The product is expected to travel and should be able to be assembled by anyone. And this concludes our functional decomposition

## Slide 80: Future Work
Tristian Belardo
Emulate3D
Component Research
PLC Learning Course
Notes: Moving forward, we would like to start bringing our current design and ideas into Emulate 3D. Emulate3D will allow us to design, test, and optimize our project in a digital space. We would also like to do some component research. Some parts of the current design, such as the linear actuator and conveyor gantry, are missing vital sensors that prevent the completion of certain tasks. Lastly, we are in the process of completing a PLC Learning Course. Our current design uses Arduino boards, which are not found in real manufacturing, and we are potentially going to switch to PLCs.

## Slide 81: References
Smart Manufacturing Industrial Automation | Rockwell Automation | US
Types of Manufacturing Processes: A Detailed Guide (deskera.com)
https://mx.pinterest.com/pin/711005859956621471/

## Slide 82: Stay tuned for more!
“Working together, we'll drive better outcomes and achieve results.”
- Rockwell Automation

## Slide 83: Functional Decomposition
Tristian Belardo
Function | Manufacture | Educate | Control | Support
Receive pin button materials | X |  |  | 
Assembles pin button | X |  |  | 
Outputs Completed button | X |  |  | 
Engage User | X | X |  | 
Displays Manufacturing Process | X | X |  | 
Resembles realistic manufacturing process | X | X |  | 

## Slide 84: Functional Decomposition
Tristian Belardo
Function | Manufacture | Educate | Control | Support
Actuates upon user input | X | X | X | 
Receives Sensor Information |  |  | X | 
Operates by Given Computer Data | X |  | X | 
Halts in response to error or user override |  | X | X | 
Stops upon completion | X |  | X | 
Maintains rigidity |  |  |  | X

## Slide 85: Functional Decomposition
Tristian Belardo
Function | Manufacture | Educate | Control | Support
Aligns Materials Accurately |  |  | X | X
Assembles with Ease |  |  |  | X

## Slide 86
Analytical Hierarchy Process
Assembles Pin Button
Realistic Manufacturing Environment
Operates By Given Computer Data
Receives Sensor Information
Displays Manufacturing Process
Halts In Response to Error or User Input
Output Button Pin
Critical Engineering Characteristics
Notes: For this iteration of the project our group decided to highlight 4 targets and metrics we deemed as critical.
1.

## Slide 87
Carlos Aceituno
Binary Pairwise Comparison
Customer Requirements
Completes a cycle in roughly 60-90s
Contains simple, useful safeguards for errors
Clearly explained for solo use
Poses no risk to non-technical user
Expands upon the results of the previous team
Functions with minimal human intervention
Easily transported
Understandable and safe for all ages
Reliable and realistic as a manufacturing process
Captures key components of manufacturing and educates user
Importance Weight Factor (IWF)
1
3
1
3
4
2
2
0
5
4
Notes: For this iteration of the project our group decided to highlight 4 targets and metrics we deemed as critical.
1.

## Slide 88: Back Up Slides

## Slide 89: Slide Headline
Try to keep text at 16 pt minimum.
Try to put as few words as possible on the slide if you’re using for a presentation.
Mix and match the backgrounds as shown in this template or just use one throughout.
You can put department/unit logos in slide master at Horizontal 0.89” Vertical 6.44” From top left corner

## Slide 90: Font Check
This is 10-point
This is 15–point Times
This is 20–point
This is 25–point
This is 30–point
This is 35–point
This is 40–point
This is 50–point
This is 60–point
This is 72–point
Notes: Use at least 20-point font in Room A105, B134, and B136
Use at least 25-point font in Room B135

## Slide 91: College of Engineering Color Palette
Fang
Orange
RGB: 238, 118, 36
Hex: #EE7624
CMYK:2, 66, 99, 0
1 2 3 4
1 2 3 4
White
Pantone: PMS 000C
RGB: 255, 255, 255
Hex: #FFFFFF
CMYK: 0, 0, 0, 0
1 2 3 4
Black
Pantone: Black C
RGB: 0, 0, 0
Hex: #000000
CMYK:0, 0, 0, 100
Garnet
Pantone: PMS 195 C
RGB: 120, 47, 64
Hex: #782F40
CMYK:19, 90, 50, 55
1 2 3 4
Notes: Avoid 75% Black in B135

## Slide 92: Accent Color Palette
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
1 2 3 4
Turquoise
RGB: 64, 224, 208
Hex: #40E0D0
CMYK:
1 2 3 4
American Orange
RGB: 255, 139, 0
Hex: #FF8B00
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Asagi-iro
RGB: 72, 146, 155
Hex: #48929b
CMYK:
1 2 3 4
Gainsboro
RGB: 220, 220, 220
Hex: #DCDCDC
CMYK:
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Imperial
RGB: 104, 40, 96
Hex: #682860
CMYK:
1 2 3 4
1 2 3 4
Tardis Blue
RGB: 0, 59, 111
Hex: #003B6F
CMYK:
Rubine Red
RGB: 206, 0, 88
Hex: #CE0058
CMYK: 0, 100, 43, 12
1 2 3 4
1 2 3 4
Corn
RGB: 251, 236, 93
Hex: #FBEC5D
CMYK:
1 2 3 4
Timberwolf
RGB: 219, 215, 210
Hex: #DBD7D2
CMYK:
Notes: Remove American orange add hyperlink grey
Make corn the last for b135
All work in 134 imperial move later
Tardis doesn’t work in b136

## Slide 93
https://color.adobe.com/create/color-wheel
Analogous
F7AB19
D67F15
EE7624
D64615
F73119
Monochromatic
6E3610
F0A16C
EE7624
6E4931
BASB1C
Triad
A14508
4BED3B
EE7624
250CED
2010A1
Complementary
FF8C40
EE7624
0098A1
24E2ED
A1470C
Split Complementary
28A164
2FED8D
EE7624
0848A1
1871ED
Double Split Complementary
3BED93
EE7624
0C6AED
ED2F18
EDAC2F
Square
C7ED3B
EE7624
0CE1ED
A418ED
ED660C
Compound
87724A
EE7624
60EFCF
09BA61
BA7E09
Shades
6E3610
EE7624
FA7625
D46820
AD551A
Notes: These are the variants that work well with Fang Orange. The bolded items show well on the projectors.

## Slide 94
https://color.adobe.com/create/color-wheel
Analogous
85412D
8F3831
782f40
8F3176
792D85
Monochromatic
C44D69
8E626D
782F40
C48796
451B25
Triad
C43959
78743B
782F40
236178
43A2C4
Complementary
C46078
782F40
25C43D
2F783A
C43959
Split Complementary
93C460
577835
782F40
39C49D
297861
Double Split Complementary
5A783B
782F40
237860
6E2978
784435
Square
78683b
782F40
237830
293978
782337
Compound
DEBAAF
782F40
5D8555
70AB32
AB4D32
Shades
C44D69
782F40
853447
5E2532
38161E

## Slide 95
B135 Stage Right
A105
A105
B135 Stage Left
B135
B134, A105
B136

## Slide 96
Border Line
Middle of Slide
Middle of White Space
Border Line
Border Line
Center of White Space
Center of Slide
Border Line
Edge of Branding
Notes: Vertical lines from top down.
Borderline and top of title. (0.5 inch)
Center of Slide (0 inch y-direction for the entire slide)
Center of Design Content (0 inch y-direction considering the title, footer, and negative space)
Bottom of Design Content (0.25 in gap to the footer. 0.75 to the bottom of the screen)
Horizontal lines from left to right
Borderline (0.5 inch)
Center of design content.
Center of slide (0 inch y-direction for the entire slide)
Borderline (0.125 inch all around)