## Slide 1: Smart Streetlight Proof of Concept
Group 9
10/22/15
Thor Cutler
Tucker Russ
Anthony Giordano
Brandon Berry

## Slide 2: Overview
Introduction
Current/Future System
Raspberry Pi SSLS User Interface
XBee Communication
LED Lighting Specifications
DC Power Supply Specifications
Smart Meter Incorporation
Group 9
Tucker

## Slide 3: Entrepreneurial Project
Project is fully funded by the Entrepreneurial Senior Design Department under Dr. Devine
Funding for the project is covered up to $1,500
Designed with special entrepreneurial characteristics
  Show the cost/benefits of implementation on FSU’s campus
  Create a real-time SSLS demo model proving this concept
  Have the potential to bring the demo to other campuses demonstrated
Group 9
Tucker

## Slide 4: Introduction
Fully working Smart Streetlight System Demo Model
Give exposure to new Smart Grid Technology
Build design using our design and programs
Minimum of two Streetlights, a Smart Meter, and a User Interface Device
Show advantages of implementing Street Lights on our Campus
Group 9
Tucker

## Slide 5: Todays Scenario
When a Streetlight, House, or Campus Building looses power
The only way the utility company knows of the outage is if a customer calls in to report the outage and the its location
Group 9
Tucker

## Slide 6: Smart Streetlight System Scenario
When a Streetlight, House, or Campus Building looses power
The utility company is immediately notified of the outage and the location
Group 9
Tucker
Notes: This allows them to not only know the exact time of the outage but also if other devices are effected (Ill talk more about that) and the exact location so they can pinpoint the problem which leads to less troubleshooting

## Slide 7: Mesh Network on Campus
Group 9
Tucker
Notes: Each Streetlight now becomes a Node to the entire mesh network. The more streetlights the stronger the mesh network becomes. Now any Buildings can now be connected to these nodes by the Smart Meters on the building. This strengthens the mesh network and now brings the same functionality to buildings. With the number of streetlights on our campus this picture would be a good representation of Smart Streetlights being implemented on campus.

## Slide 8: Benefits
Time since outage
Location of outage
More information leads to less troubleshooting to find where fault is located
Potential to do research, estimate costs of power saving ideas, etc.
Change existing streetlight bulbs to LEDs
Group 9
Tucker

## Slide 9: System Requirements
Requirement Code | Requirement Statement | Need Mapping | Explanation
R_S1 | The SSLS shall alert a user within 10 seconds of a monitored device losing power. | N_S1 N_S2 | The purpose of this requirement is to document one of the basic functions of our project. When a street light or smart meter loses power, the system user, by looking at the system’s monitor, will be alerted of the power loss.
R_S2 | The SSLS shall constantly show the status of all monitored devices, updating every 10 seconds. Status consists of: -Powered on or off -last updated -voltage -current -power | N_S3 N_S4 N_S8 N_Want1 N_Want3 N_want4 | The purpose of this requirement is to ensure that the system will constantly be updating data on a set time interval and not just when a monitored device loses power.
R_S3 | The SSLS shall receive status signals from monitored devices wirelessly. | N_S5 N_S6 N_S7 | The purpose of this requirement is to simulate that street lights are far enough apart that a wired connection isn’t practical
R_S4 | The SSLS shall be able to differentiate between different monitored devices by the signal that they send. | N_S7 | The purpose of this requirement is to ensure that each light sends a slightly different signal as to allow the user to know which light has lost power.
Group 9
Thor

## Slide 10: System Requirements Example Test
Test R_S1:
A monitored device on the SSLS Demo Model will be turned off and a timer will be started.
  _____ In 10 Seconds or less the SSLS Demo Model monitor needs to have updated information.
  _____ The updated information must accurately show which monitored device has lost power.
  _____ The updated information must show how long ago the monitored device lost power accurate to +- 10 seconds.
Group 9
Thor

## Slide 11: Components
Streetlight
Transmit Data
Receive Data
Smart Meter
Raspberry Pi
Receive
Data
Transmit Data
Receive Data
Group 9
Thor

## Slide 12: Raspberry Pi 2
900MHz quad-core Cortex-A7 CPU
1GB RAM
4 USB ports
Full HDMI port
40 GPIO pins
Micro SD card slot
Linux Raspbian loaded
XBee functionality using GPIO pins
Group 9
Thor

## Slide 13: SSLS User Interface
Real-time status notifications every 10 seconds or less
Touchscreen UI for simplicity
  Configurable using EVTest to find screen bounds
  Input these bounds in Rasbian root file:
    Sudo/nano/FILE/ ->
    Usr/share/X11/xorg.config.d/10-evdev.conf
UI will most likely be written in Python
  Chosen to easily interact with the Rapberry Pi’s GPIO pins
Group 9
Thor

## Slide 14: XBee Series 1
2.4GHZ using IEEE 802.15.4
P2P and multi-point Mesh Network
3.3V, 50mA Input
300ft max outdoor range
1mW Output
6 10-bit ADC input pins
65536 Channels
Local or over-air configuration
Group 9
Thor

## Slide 15: Configuration
XBee devices will be configured using X-CTU, a free multi-platform application by Digi
It is generally used for simple designs and test conditions
In the future we will need to develop code to receive signals from the monitored devices
Group 9
Thor

## Slide 16: Demonstration
We are currently able to send signals using two XBee devices, allowing communication between two computers
Group 9
Thor

## Slide 17: Model Requirements
Requirement Code | Requirement Statement | Need Mapping | Explanation
R_M1 | The SSLS Demo Model shall be built on a cart making it mobile. | N_M3 | Our whole demo will be built on a cart allowing presentations to be held in multiple locations and making working on the Demo easier.
R_M2 | The SSLS Demo Model shall have a monitor to display the status of all monitored devices. | N_M2 N_Want6 | The Demo will have the screen that displays the SSLS information for each light covered in R1 and R2.
R_M3 | The SSLS Demo Model shall have at least 1 street light and 1 smart meter that can be shut off to represent power loss. | N_M1 | This part of the model will be used to represent power loss in a light allowing us to display how the system reacts to power loss in a monitored device.
Group 9
Brandon

## Slide 18: Model Design
Model will be on a mobile cart
Plexiglass will display electric components
Model buildings will represent buildings of a city or campus
Group 9
Brandon

## Slide 19: LEDs for Model
5050 SMD (Surface Mount Diode)
Dimensions: 5.0mm X 5.0mm
Power Draw: 60mA @ 2.8 - 3.4 Volts
Lumen Flux: 16-22 lumens
Group 9
Brandon

## Slide 20: Benefits of LED’s
LEDs provide whiter light
LEDs – 5500K vs. HPS(High Pressure Sodium) – 2200K
Group 9
Brandon

## Slide 21: Angle of the lighting
Light from LEDs can be directed
Better light distribution, eliminating dark spots
Less street lights are needed
Improved vertical lighting, better visibility for drivers
Group 9
Brandon

## Slide 22: Lower Cost & Environmentally Friendly
At 10 hours per night:
HPS - 290 watts | 1058 kwh per year
LED - 125 watts | 456 kwh per year
Less power means less CO2 emissions
Less maintenance mean less overall operation cost
Group 9
Brandon

## Slide 23: Street Light
3D Printed model street lights
XBee and LEDs will be built into the street light
They will be connected in parallel with the XBee connected to a backup battery
Group 9
Brandon

## Slide 24: Power Schematic for XBee & LEDs
Group 9
Brandon

## Slide 25: While DC Power is Connected
Group 9
Brandon

## Slide 26: LED Input Current and Voltage
Group 9
Brandon

## Slide 27: Battery and XBee Input Voltage
Three Diodes are used to reduce the voltage from 5 to 3.4 volts
Group 9
Brandon

## Slide 28: While DC Power is Disconnected
Diodes are used to prevent the backflow of current when the DC power supply goes down
This allows the XBeeCheck to see that the DC power supply has stopped working while the XBee itself still receives power
Group 9
Brandon

## Slide 29: LED is off when the DC Power goes down
Group 9
Brandon

## Slide 30: What Will Be Powered?
3 XBee: 3.3V each 50mA
3 LEDs: 2.8-3.4V, 60mA-80mA
                -Two on cart
            -One far away
Digi XBee Smart Plug running at 120V
Raspberry Pi 2: Running at 5V
Group 9
Anthony

## Slide 31: Power Supply
Three 5 Volt 1 Amp DC power supplies
Individual power source per streetlight in order to recognize which power source is out
Group 9
Anthony

## Slide 32: Toggle Switches
1 switch per Streetlight (3 total)
1 switch for Smart Meter
1 Main Turn Off switch
Group 9
Anthony

## Slide 33: Lithium Ion Battery
3.3V Supply
Will supply power to XBee in the case of a power loss
Not using a capacitor due to the required time the XBee needs to stay on
Group 9
Anthony

## Slide 34: Digi XBee Smart Plug
Functions as a household Smart Meter
Ability to communicate with all XBees in the network
Enables users to measure and control connected electrical devices, maximizing energy efficiency and reducing cost
Runs off of 120V, 8A rated socket
Group 9
Anthony

## Slide 35: Power Layout
5V DC
5V DC
120 V
Smart Meter
w/XBee
Streetlight 1
Streetlight 2
120 V
5V DC
Streetlight 3
5V
5V
120V
5V
5V DC
Raspberry Pi
5V
Group 9
Anthony
LED

## Slide 36: Questions?
Group 9

## Slide 37
Group 9