## Slide 1: Smart Streetlight Proof of Concept
Group 3
03/26/16
Tucker Russ
Thor Cutler
Brandon Berry
Anthony Giordano

## Slide 2: Overview
Introduction
Solution
3D Printing Progress
XBee Configuration
XBee Frame Comprehension
Model Design
Battery Backup System
Circuit Design
Shark Tank Progress
Group 3
Tucker

## Slide 3: Introduction
Fully working Smart Streetlight System Demo Model
Give exposure to new Smart Grid Technology
Build system using our design and code
Three complete Streetlights and a User Interface Device
Show advantages of implementing Streetlights on our Campus
Participate in Engineering Shark Tank
Group 3
Tucker

## Slide 4: Smart Streetlight System Scenario
When a Streetlight, House, or Campus Building loses power
The utility company will be immediately notified of the outage and the location through the User Interface Device
Group 3
Tucker
User
Notes: This allows them to not only know the exact time of the outage but also if other devices are effected (Ill talk more about that) and the exact location so they can pinpoint the problem which leads to less troubleshooting

## Slide 5: Top-level Model Hardware Design
Group 3
Tucker
802.15.4 P2P protocol

## Slide 6: 3D Printing Progress
Each Streetlight is printed in 3 parts in order to make up the entire dimensions of the Streetlight
3D Printer MAX printing dimensions: 130 x 96 x 139 (mm)
Part 1: Part 2: Part 3:
85 x 55 x 5 (mm) 87 x 57 x 127 (mm) 20 x 20 x 127 (mm)
Group 3
Tucker

## Slide 7: Scaled Model on Cart
Group 3
Tucker

## Slide 8: XBee Series 1
2.4GHZ using IEEE 802.15.4
P2P and multi-point Mesh Network
3.3V, 50mA Input
300ft max outdoor range
1mW Output
6 10-bit ADC input pins
65536 Channels
Local or over-air configuration
Group 3
Thor

## Slide 9: Configuration
XBee devices are configured using X-CTU, a free multi-platform application by Digi
X-CTU allows each XBee device to be flashed with personal settings, such as using a certain pin as a digital input.
Group 3
Thor

## Slide 10: User Interface XBee Device Design
Group 3
Thor

## Slide 11: User Interface XBee Device Properties
The Raspberry Pi will be connected to its own XBee device that is set up to receive data packets (frames) from the Xbee devices attached to monitored devices
The Raspberry Pi will use the data from the frames to determine the status of each monitored device
The status of each monitored device will be viewable on the LCD screen,
Group 3
Tucker

## Slide 12: User Interface Software Solution
2 Step Process
  Step 1: Information Recording
    Device would be left in recording mode overnight to determine the status of each streetlight in the network and record the data
    After a set amount of time the device would stop recording (Normally in the morning when streetlights are turned off)
  Step 2: Visual Representation of Data
    Currently being developed
    Opens text file created by Step 1 and displays the status of streetlights that need fixing
Group 3
Tucker

## Slide 13: User Interface Step 1 Code
Group 3
Tucker

## Slide 14: User Interface Step 1 Output
Group 3
Tucker

## Slide 15: Power Layout of Model
5V DC
5V DC
120 V
Smart Meter
w/XBee
Streetlight 1
Streetlight 2
120 V
5V DC
Streetlight 3
5V
5V
120V
5V
5V DC
User Interface
5V
Group 3
Brandon
LED

## Slide 16: Why is a backup battery needed?
If the power supplied to the streetlight fails, the backup battery will provide enough power to allow the XBee to still transmit for 6+ hours for the model
The battery capacity would be scaled up with a full size design
This will allow for the ability to notify the user interface when the power to a streetlight has gone out
Once the system regains outside power, the battery will begin to charge back to its full capacity
Group 3
Brandon

## Slide 17: Original Node Power Circuit for XBee & LEDs
Group 3
Brandon

## Slide 18: Updated Node Circuit While DC Power is Connected
Group 3
Brandon

## Slide 19: Updated Node Circuit While DC Power is Disconnected
Group 3
Brandon

## Slide 20: While DC Power is Disconnected
Group 3
Brandon
Diodes are used to prevent the backflow of current when the DC power supply goes down
This allows the XBeeCheck to see that the DC power supply has stopped working while the XBee itself still receives power
A second check for when the LED goes out has been added to the circuit

## Slide 21: XBee Check Readings
The voltage required to cause a “high” or “low” reading on the XBee:
Low < 0.9V
High > 0.9V
Each XBee check will be supplied over 0.9 volts to insure a high reading when needed
When the main power is lost or the LED goes out, the XBee checks will receive an insignificant voltage resulting in a low reading
Group 3
Brandon

## Slide 22: Actual Schematic for each Streetlight Node
Group 3
Brandon

## Slide 23: Supplies List for each Streetlight Node
1 XBee
5 Rectifier diodes
1 4V Lithium-ion battery
3 24Ω Resistors
20 Gauge Wire
2 Toggle switches (for model purposes only)
Group 3
Brandon

## Slide 24: Shark Tank
Group 3
Anthony

## Slide 25: Target Market
Established lighting manufacturers
Utility companies
Group 3
Anthony

## Slide 26: Potential Consumers
Who
College campuses
  -Walkway lights
Neighborhood associations
  -Street lights
Recreational sports complexes
  -Field lights
Airports
  -Runway lights
Why
Efficient lighting
Safety (well lit walkways)
Fast response to outages
Group 3
Anthony

## Slide 27: Material Cost
User Interface
Raspberry Pi 2 - $35
Python software - $0
SSL software code - $0
Individual Device
XBee Pro - $40
Circuit board - $4
Wires - $2
Lithium Ion Battery - $20
Voltage Controller - $2
Group 3
Anthony

## Slide 28: Competition
General Electric’s LightGrid
Uses wireless nodes to relay information obtained from an individual streetlight
Requires internet connection to communicate lighting performance
Contains GPS chips to locate the exact location of each light
Group 3
Anthony

## Slide 29: Competitors Vs. SSL
General Electric’s LightGrid
Multiple wireless features to monitor and control lights
Requires Internet Access
Up to$400 per light
Addition software license costs
Smart Streetlights
Single wireless feature to check status of lights
No internet access required
Approximately $68.00 per light
One time purchase (no contract)
Group 3
Anthony

## Slide 30: Competitive Advantage
Simple solution for monitoring the status of each individual streetlight
Cost efficient alternative to replacing full streetlight
Does not require internet connection
Group 3
Anthony

## Slide 31: Selling Points
Provides quick response to streetlight outages
Increases safety providing reliable lighting
Inexpensive compared to competitors
Group 3
Anthony

## Slide 32
Group 3
Anthony

## Slide 33: Questions?
Group 3