HW4 part D. [20]  Sample exam problem  – Floating-Point Representations (CIO 4 aeo)

Suppose you are looking at a memory dump of a program that works exclusively with floating-point data, and you see that a word of memory representing a particular program variable contains the hexadecimal value 0x3e256fd4.  You want to know what actual numeric value (floating-point number) is contained in that program variable.

(a)   Identify the engineering problem.

(i) What is the name of the engineering standard that specifies the most common format for floating-point representations?

(ii) Does this particular hex value represent a single-precision or a double-precisison number?  How do you know?  Explain briefly.

(b)  Formulate the engineering problem.  Show how to break up the binary word into the appropriate constituent bit fields, and write an algebraic expression giving the value of the floating-point number in terms of the integer value of each field.

(c)  Solve the engineering problem.  Calculate and write in ordinary decimal scientific notation the value of the specific floating-point number being represented.

HW5 Part C (CIO 6 / POs a,o) – Multipliers and Dividers

The following MIPS subroutine takes a 4-bit unsigned multiplicand and multiplier in registers $a0 and $a1 respectively, and returns their 8-bit unsigned product in $v0.

line#

1    MULT4:	li	$v0,0		# Clear product register

2		li	$t0,0x08	# mask = Mask for initial bit position (bit 3).

3    LOOP:	sll	$v0,$v0,1	# prod = prod << 1; (shift product left 1 place).

4		and	$t1,$a1,$t0 	# bit = multiplier & mask;

5		beq	$t1,$0,ENDIF 	# if (bit != 0)

6		addu	$v0,$v0,$a0  	#	product += multiplicand;

7    ENDIF:	srl	$t0,$t0,1 	# mask = mask >> 1; (shift mask right 1 place)

8		bne	$t0,$zero,LOOP	# if (mask != 0) goto LOOP;

9 		jr	$ra 		# $v0 now contains complete product; return it.

Hand-simulate the execution of this code given the initial values $a0=11, $a1=5.

a) [10] First, write out the given input numbers as full 32-bit binary register values.

| bit #: | 31 |  |  | MSB |  |  | 24 | 23 |  |  |  |  |  |  | 16 | 15 |  |  |  |  |  |  | 8 | 7 |  |  | LSB |  |  | 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| $a0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| $a1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

b) [25] Next, fill in the table through all four iterations of the loop.  Indicate each line of code executed, and each value written back to a register.  We have filled in the initial values and the first six lines of the table for you.  Also record the branch behavior.

| Iter. No. | Line No. | $a0 | $a1 | $t0 | $t1 | $v0 | Branch behavior, taken v. not | Branch dest (if taken) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Initially: | 11 | 5 | ? | ? | ? |  |  |
| 1 | 1 |  |  |  |  | 0 |  |  |
| 1 | 2 |  |  | 8 |  |  |  |  |
| 1 | 3 |  |  |  |  | 0 |  |  |
| 1 | 4 |  |  |  | 0 |  |  |  |
| 1 | 5 |  |  |  |  |  | taken | ENDIF (7) |
| 1 | 7 |  |  | 4 |  |  |  |  |
| 1 | 8 |  |  |  |  |  | taken | LOOP (3) |
| 2 | 3 |  |  |  |  | 0 |  |  |
| 2 | 4 |  |  |  | 4 |  |  |  |
| 2 | 5 |  |  |  |  |  | Not taken |  |
| 2 | 6 |  |  |  |  | 11 |  |  |

Similar problem to HW6 part C (CIO 5 / POs a,e,o) – Control and dataflow

Below is the single-cycle MicroMIPS datapath from the textbook (fig. 13.3, p. 248).  Suppose you are told that the LW instruction on a certain test chip is malfunctioning.  You suspect that the problem might be that one of the connections (wires or multi-wire buses) in the below high-level wiring diagram could be broken or disconnected.  You want to determine which lines might be broken without opening up the chip package.

a) [10] Identify the scope of the diagnostic problem to be solved.  Which connections in the above diagram (including both data and control wires/buses) are required for successful functioning of the LW instruction?  Using a highlighter pen (if you have one), highlight all the lines, or sections of lines, that are required.  (Assume that any broken control wires would behave as all-0 signals.)

b) [10] Formulate a testing strategy for diagnosing the problem.  For each of the wires/buses that you highlighted in part (a), identify at least one other instruction in the MicroMIPS instruction set (table 13.1, p.244) that would also fail to work properly if the indicated connection were entirely broken.  (If it’s a multi-wire bus, assume all wires in the bus would be broken.)  We have started writing a table of answers for you… you can use a 2nd column and the top of the next page if necessary.

Label of		An instruction that could

Wire or bus	be used to test it

rs 			add

c) [10] Solve the diagnostic problem.  Suppose that after some experimenting, you discover that SW is also malfunctioning, but that all other instructions are working correctly.  Assuming that only a single segment of a given wire or bus in the top-level schematic is broken, which one must it be?  How do you know?

d) [5] Assuming your answer to part (c) is correct, if any broken wires (including data wires) manifest themselves as “stuck-at-0” signals, then what are the LW and SW instructions actually doing in the malfunctioning chip  (instead of the thing that they are supposed to be doing)?