|  | Table showing which instructions use which lines in figure 13.3. | :Line Category | and,or,xor,nor,slt | add,sub | addi | slti,andi, ori,xori | lui | lw | sw | beq,bne | bltz | j | jal | jr | syscall |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Instruction category: |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 |
| IF | Next PC, (PC), (PC)(IC, inst | a | x | x | x | x | x | x | x | x | x | x | x | x | x |
| RF | rs, (rs) | b | x | x | x | x |  | x | x | x | x |  |  | x |  |
|  | rt | c | x | x | x | x |  | x | x | x |  |  |  |  |  |
|  | (rs)(ALU | d | x | x | x | x |  | x | x |  |  |  |  |  |  |
| Rtype | fn | e | x | x |  |  |  |  |  |  |  |  |  | x | x |
|  | rd | f | x | x |  |  |  |  |  |  |  |  |  |  |  |
|  | rt(Reg file, (rt)(ALUSrc mux | g | x | x |  |  |  |  | x |  |  |  |  |  |  |
|  | (rt) | h | x | x |  |  |  |  | x | x |  |  |  |  |  |
| IJType | op | i |  |  | x | x | x | x | x | x | x | x | x |  |  |
|  | imm, SE out, ALUSrc ctl | j |  |  | x | x | x | x | x |  |  |  |  |  |  |
|  | rt(RegDst mux | k |  |  | x | x | x | x |  |  |  |  |  |  |  |
| ALU | ALUSrc out, ALUFunc ctl, ALU out | l | x | x | x | x | x | x | x |  |  |  |  |  |  |
|  | ALUout(RegInSrc | m | x | x | x | x | x |  |  |  |  |  |  |  |  |
|  | ALUOvfl | n |  | x | x |  |  |  |  |  |  |  |  |  |  |
| Ld/St | Data in, DataWrite ctl | o |  |  |  |  |  |  | x |  |  |  |  |  |  |
|  | Data addr | p |  |  |  |  |  | x | x |  |  |  |  |  |  |
|  | DataRead ctl, Data out | q |  |  |  |  |  | x |  |  |  |  |  |  |  |
| Next PC calc | jta | r |  |  |  |  |  |  |  | x | x | x | x |  |  |
|  | Br&Jump ctl | s |  |  |  |  |  |  |  | x | x | x | x | x | x |
|  | (rs)(Next addr | t |  |  |  |  |  |  |  | x | x |  |  | x |  |
|  | (rt)(Next addr | u |  |  |  |  |  |  |  | x |  |  |  |  |  |
|  | (PC)(Next addr | v | x | x | x | x | x | x | x | x | x |  |  |  | x |
|  | 31, IncrPC | w |  |  |  |  |  |  |  |  |  |  | x |  |  |
| WB | RegDst ctl | x | x | x |  |  |  |  |  |  |  |  | x |  |  |
|  | RegDst out, Register input, RegWrite ctl | y | x | x | x | x | x | x |  |  |  |  | x |  |  |
|  | RegInSrc ctl | z | x | x | x | x | x |  |  |  |  |  | x |  |  |

An optimal strategy for debugging a broken SLTI instruction, assuming that only one line (wire or bus) is broken:

Any of the following line categories might be broken (SLTI uses all these):

a. Next PC, (PC), (PC)(IC, inst

b. rs, (rs)

c. rt

d. (rs)(ALU

i. op

j. imm, SE out, ALUSrc ctl

k. rt(RegDst mux

l. ALUSrc out, ALUFunc ctl, ALU out

m. ALUout(RegInSrc

v. (PC)(Next addr

y. RegDst out, Register input, RegWrite ctl

z. RegInSrc ctl

1. Test BEQ

If BEQ fails also, this suggests the broken wire is one of {a,b,c,i,v}.

1.1. Test LUI

If LUI fails also, the broken wire is {a,i,v}

1.1.1. Test JAL

JAL Fails ( {a,i}

1.1.1.1 Test AND

AND Fails({a}

AND Works({i}

JAL Works ( {v}

If LUI works, the broken wire is {b,c}

1.1.2. Test BLTZ

BLTZ Fails ( {b}

BLTZ Works ( {c}

If BEQ works, this eliminates these, and leaves {d,j,k,l,m,y,z}

1.2. Test SW

SW fails ( {d,j,l}

1.2.1. Test AND

AND fails ( {d,l}

1.2.1.1. Test LUI

LUI fails ( {l}

LUI works ( {d}

AND works ( {j}

SW works ( {k,m,y,z}

1.2.2. Test LW

LW fails ( {k,y}

1.2.2.1. Test ADD

ADD fails ( {y}

ADD works ( {k}

LW works ( {m,z}

1.2.2.2. Test JAL

JAL fails ( {m}

JAL works ( {z}

I.e., here are the possible sequences of tests and outcomes:

BEQ	LUI	JAL	AND		a. Next PC, (PC), (PC)(IC, inst

BEQ	LUI	JAL	AND		i. op

BEQ	LUI	JAL			v. (PC)(Next addr

BEQ	LUI	BLTZ			b. rs, (rs)

BEQ	LUI	BLTZ			c. rt

BEQ	SW	AND	LUI		l. ALUSrc out, ALUFunc ctl, ALU out

BEQ	SW	AND	LUI		d. (rs)(ALU

BEQ	SW	AND			j. imm, SE out, ALUSrc ctl

BEQ	SW	LW	ADD		y. RegDst out, Register input, RegWrite ctl

BEQ	SW	LW	ADD		k. rt(RegDst mux

BEQ	SW	LW	JAL		m. ALUout(RegInSrc

BEQ	SW	LW	JAL		z. RegInSrc ctl

Note that the maximum number of tests needed is 4.  This is optimal, since note there are 12 possible sets of wires that could be to blame, and (log212( = 4, so at least 4 binary tests are needed in order to narrow down the set of options from 12 possibilities to 1.