FAMU-FSU COLLEGE OF ENGINEERING

EEL-3705 Digital Logic Design

Individual Assessment = Fall 2005

09/16/2005

Name:______KEY_______________                      Last 3 digits of SSN:_____________

# Note: This assessment is closed book closed notes. No help can be obtained and need to be done individually.

# Problem 1

| A. |  | Convert the following decimal numbers into Hex and Binary. Assume unsigned binary numbers. Hint: Find the hex representation first. |
| --- | --- | --- |

| # | Decimal | Hex (2 digits) | Binary (8 bits) |
| --- | --- | --- | --- |
| 1) | 7 | = $07 | %00000111 |

| B. |  | Calculate the 2’s complement of the following signed binary numbers. Give the decimal equivalent of the original binary number. |
| --- | --- | --- |

| # | Original Binary Number (A) | 2’s Complement (8 bits) | Decimal Equivalent of Original Binary Number (A) |
| --- | --- | --- | --- |
| 1) | 10111111 | %01000001 | -65 |

| C. | 5pts | Given a binary number A=100100102 , determine |
| --- | --- | --- |
| # | Type of representation | Result |
| 1) | BCD equivalent of A | 92 |

| D. | 10pts | Perform the following arithmetic operations. Give the result in the indicated form. Assume signed binary numbers. |
| --- | --- | --- |
| # | Problem | Result Form | Result |
| 1) | 01101101 -00110001 | Binary (8 bits) | Show work here ( |

Problem  2

|  | Given the three variable function: |
| --- | --- |

| A |  | Evaluate the function using the truth table given below (Write all possible combinations of the variable and then evaluate F) |
| --- | --- | --- |

| A | B | C | F |
| --- | --- | --- | --- |
| 0 | 0 | 0 | 0 |
| 0 | 0 | 1 | 0 |
| 0 | 1 | 0 | 1 |
| 0 | 1 | 1 | 0 |
| 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 1 |
| 1 | 1 | 1 | 0 |

| B |  | Write the function in canonical Sum of Products form (using the truth table above). You may use the shorthand notation for your answer. |
| --- | --- | --- |

| D |  | Evaluate the following function using the Venn Diagram given below |
| --- | --- | --- |