## Slide 1: Home Energy Management
Senior Design Final Presentation

## Slide 2: Our Goal
With the implementation of our Home Energy Management System and the advantage of Real-Time Pricing (RTP) provided by electric utility companies, consumers have the ability to adjust their energy usage in order to reduce their electricity bill.
Sponsored by FEEDER – Foundation for Engineering Education for Distributed Energy Resource
Who are we?
Dillon Wiggins – EE – Project Manager
Pablo Aguirre – EE – Systems Engineer
Juan Ospina – CE & EE – Hardware Engineer
Michael Garcia-Rivas – CE – Software Engineer
Ivan Remete – EE – Electrical Engineer

## Slide 3: Background
According to Brattle Group, a leading consulting firm, during the power crisis in the Western U.S. in 2000/01, a demand response program would have helped contain the energy crisis in California.
If real‐time pricing had been offered to large commercial and industrial customers, peak demand would have fallen by 2.5 percent, resulting in a drop of 18 percent in wholesale market prices.
SOURCE: BENEFITS OF DEMAND RESPONSE IN ELECTRICITY MARKETS AND RECOMMENDATIONS FOR ACHIEVING THEM
Notes: http://energy.gov/sites/prod/files/oeprod/DocumentsandMedia/DOE_Benefits_of_Demand_Response_in_Electricity_Markets_and_Recommendations_for_Achieving_Them_Report_to_Congress.pdf
THESE 7 SLIDES SHOULD BE COMPRESSED INTO, AT MOST, 3
TOO WORDY
Pablo

## Slide 4
Load Response from Critical Peak Pricing and Demand Response Enabling Technologies
Background cont.
SOURCE: BENEFITS OF DEMAND RESPONSE IN ELECTRICITY MARKETS AND RECOMMENDATIONS FOR ACHIEVING THEM
Figure 1
Notes: http://energy.gov/sites/prod/files/oeprod/DocumentsandMedia/DOE_Benefits_of_Demand_Response_in_Electricity_Markets_and_Recommendations_for_Achieving_Them_Report_to_Congress.pdf
THESE 7 SLIDES SHOULD BE COMPRESSED INTO, AT MOST, 3
Pablo

## Slide 5
Real-time pricing (RTP) enables customers to pay for electricity at the wholesale price during a predetermined period of time, paying for energy at a rate that is linked to the hourly market price for electricity.
This is often viewed as the purest form of price-based demand response, as the much smaller price-responsive interval periods lead to a closely linked cost/price ratio.
Background cont.
Result
The cost of generating electricity does not always match the price the end user pays for electricity, RTP allows customers to base their energy usage on the energy market price.
Renewable energy can become a viable source through a normalized demand curve
Notes: Source: Faruques PDF
THESE 7 SLIDES SHOULD BE COMPRESSED INTO, AT MOST, 3
TOO WORDY
Pablo

## Slide 6
Source: Florida Public Service Commission, Dec.2012
PV: Pecan Street Research Institute (Not to scale)
TYSP(Ten Year Site Plan) Utilities: Example Daily Load Curve (FL)
Figure 4
Ivan Remete
Notes: IVAN

## Slide 7
Chart: Real Time Pricing Monday Feb. 8 –Friday Feb. 12
| 11:00 PM-12:00 AM | 12:00 AM-1:00 AM | 1:00 AM -2:00 AM | 2:00 AM -3:00 AM | 3:00 AM -4:00 AM | 4:00 AM -5:00 AM | 5:00 AM -6:00 AM | 6:00 AM -7:00 AM | 7:00 AM -8:00 AM | 8:00 AM -9:00 AM | 9:00 AM -10:00 AM | 10:00 AM -11:00 AM | 11:00 AM -12:00 PM | 12:00 PM - 1:00 PM | 1:00 PM -2:00 PM | 2:00 PM -3:00 PM | 3:00 PM -4:00 PM | 4:00 PM -5:00 PM | 5:00 PM -6:00 PM | 6:00 PM -7:00 PM | 7:00 PM -8:00 PM | 8:00 PM -9:00 PM | 9:00 PM -10:00PM | 10:00 PM -11:00 PM
M | 4.6 | 4.6 | 4.5 | 4.6 | 4.6 | 4.7 | 4.8 | 5.2 | 5.1 | 5 | 4.9 | 4.8 | 4.7 | 4.7 | 4.7 | 4.6 | 4.7 | 4.9 | 5.4 | 5.2 | 5 | 4.9 | 4.7 | 4.5
Tue | 4.3 | 4.2 | 4.2 | 4.2 | 4.3 | 4.4 | 4.8 | 5.5 | 5.1 | 4.9 | 4.8 | 4.7 | 4.6 | 4.6 | 4.5 | 4.5 | 4.5 | 4.8 | 5.6 | 5.2 | 5 | 4.8 | 4.6 | 4.5
W | 4.4 | 4.3 | 4.3 | 4.3 | 4.3 | 4.4 | 4.6 | 5.3 | 5.1 | 5 | 4.8 | 4.8 | 4.7 | 4.6 | 4.6 | 4.5 | 4.6 | 4.9 | 5.4 | 5.2 | 5 | 4.9 | 4.7 | 4.5
Thu | 4.5 | 4.4 | 4.4 | 4.4 | 4.4 | 4.6 | 5 | 5.9 | 5.4 | 5.4 | 5.1 | 5 | 4.8 | 4.7 | 4.7 | 4.6 | 4.6 | 5 | 6 | 5.7 | 5.3 | 5 | 4.6 | 4.5
F | 4.4 | 4.4 | 4.3 | 4.3 | 4.4 | 4.7 | 5.2 | 5.6 | 5.4 | 5.2 | 5 | 4.8 | 4.6 | 4.5 | 4.5 | 4.4 | 4.4 | 4.6 | 5.3 | 5 | 4.8 | 4.6 | 4.5 | 4.3
Source: Power Smart Pricing, Ameren Illinois
Ivan Remete
Notes: IVAN

## Slide 8
Chart: Real Time Pricing Saturday Feb. 13 – Sunday Feb. 14
| 11:00 PM-12:00 AM | 12:00 AM-1:00 AM | 1:00 AM -2:00 AM | 2:00 AM -3:00 AM | 3:00 AM -4:00 AM | 4:00 AM -5:00 AM | 5:00 AM -6:00 AM | 6:00 AM -7:00 AM | 7:00 AM -8:00 AM | 8:00 AM -9:00 AM | 9:00 AM -10:00 AM | 10:00 AM -11:00 AM | 11:00 AM -12:00 PM | 12:00 PM - 1:00 PM | 1:00 PM -2:00 PM | 2:00 PM -3:00 PM | 3:00 PM -4:00 PM | 4:00 PM -5:00 PM | 5:00 PM -6:00 PM | 6:00 PM -7:00 PM | 7:00 PM -8:00 PM | 8:00 PM -9:00 PM | 9:00 PM -10:00PM | 10:00 PM -11:00 PM
Sat | 4.3 | 4.3 | 4.3 | 4.2 | 4.3 | 4.3 | 4.5 | 4.8 | 4.9 | 5.1 | 5.1 | 4.7 | 4.5 | 4.4 | 4.4 | 4.4 | 4.5 | 4.7 | 5.2 | 5.1 | 5 | 4.9 | 4.7 | 4.6
Sun | 4.6 | 4.6 | 4.5 | 4.5 | 4.4 | 4.5 | 4.6 | 4.7 | 4.7 | 4.7 | 4.6 | 4.4 | 4.3 | 4.2 | 4.2 | 4.2 | 4.2 | 4.4 | 4.6 | 4.6 | 4.5 | 4.4 | 4.3 | 4.2
Source: Power Smart Pricing, Ameren Illinois
Average monthly utility: $87 for Illinois, $123 for FL. <Electricity Local>
Ivan Remete
Notes: IVAN

## Slide 9
Chart: 
| EV | A/C | Water Heating | Appliances
Average residential load per kW | 22 | 14 | 10 | 54
Reference: CentralMaineDiesel
Projected residential loads per kW
Figure 2 displays the power you need when all appliances have started and are running. Loads are based on the U.S average. Assuming total house continuous rating is 47.860 kW
Figure 2
Notes: Ivan
THESE 7 SLIDES SHOULD BE COMPRESSED INTO, AT MOST, 3
Mention Tesla

## Slide 10
Unit | Continuous Rating (W)
Electric Vehicle | 10000
Central Air (40k BTU)-for a 1,500sqft home | 6000
Electric Water Heater | 4000
Refrigerator (1/4 HP) | 500
Freezer (1/4 HP) | 600
Dehumidifier | 650
Computer System: CPU, Monitor, Laser Printer | 1500
UPS System | 2000
CD Player | 100
Radio | 100
Television | 300
Microwave | 800
Blender | 300
Coffee Maker | 1500
Electric Range (1 element) | 1500
Toaster (2-slice) | 1000
Dishwasher (Hot Dry) | 1500
Electric Oven | 3410
Reference: CentralMaineDiesel
Continuous Load Rating Per Average Household
Notes: IVAN
THESE 7 SLIDES SHOULD BE COMPRESSED INTO, AT MOST, 3

## Slide 11
Unit | Continuous Rating (W)
Washing Machine | 1150
Electric Clothes Dryer | 5400
Security System | 500
Hair Dryer | 1200
Garage Door Opener (1/3 HP) | 750
Iron | 1200
Total Load (W) | 
47,860 | 
Reference: CentralMaineDiesel
Continuous Load Rating Per Average Household Cont.
Notes: IVAN
THESE 7 SLIDES SHOULD BE COMPRESSED INTO, AT MOST, 3

## Slide 12
Source: U.S Energy information Administration
Average Energy Consumed (Residential)
More than a quarter (27%) of the energy consumed in Florida homes is for air conditioning, which is more than four times the national average. Half of energy consumed by Florida households is for appliances, electronics, and lighting.
Figure 3
Notes: Ivan
THESE 7 SLIDES SHOULD BE COMPRESSED INTO, AT MOST, 3

## Slide 13
Internet
Router
Web Application
Main Controller
Electric
Vehicle
Water Heater
Thermostat
Design
Web Server
Load Controller
Load Controller
Load Controller

## Slide 14: House Design

## Slide 15: Main Controller Section
Beagle Bone Black (Main Controller)
Connected to Internet using Ethernet Connection.
NRF24L01+ Transceiver
Characteristics | Specification
Processor | AM335x 1GHz ARM® Cortex-A8
RAM | 512MB DDR3 RAM
Storage | 4GB 8-bit eMMC on-board flash
Connectivity | Specification
 | Ethernet
 | SPI (Serial Peripheral Interface)
 | HDMI
 | GPIO
Characteristics | Specification
RF Technology | 2.4 GHz ISM Band Operation
Modulation | 1 or 2 MHz Bandwidth
Information | Dynamic Payload 1 to 32 bytes
Notes: Michael

## Slide 16: Load Section
MSP432P401R
Direct communication with main controller using a NRF24L01+ Transceiver.
NRF24L01+ Transceiver
5[V] Relay – Rated 10[A] 250 [V] AC
Characteristics | Specification
MCU | 48 MHz 32-bit ARM Cortex M4F
Power | 95 [uA]/MHz Active Operation
 | 850 [nA] Standby Operation
Memory | 
Flash | 256 KB
RAM | 64 KB
Notes: Michael
10 Amp relay

## Slide 17: Main Controller

## Slide 18: Load Controller

## Slide 19: Combination of Collected Data
The Main Controller was on the third floor therefore the direct distance on other floors had to be calculated using the height.
There is about 25ft between floors
Building B has 4 large rooms
Building A has more open space

## Slide 20: System Testing
Testing Results |  |  | 
Command | Component |  | 
 | Main Controller | Load Controller | Main Controller
 | Task |  | 
 | Sent | Received | Returned
Decrease Temperature | Pass | Pass | N/A
Increase Temperature | Pass | Pass | N/A
Turn Loads Off | Pass | N/A | N/A
Turn Loads On | Pass | N/A | N/A
RefreshTemp | Pass | Pass | Pass
CheckStatus | Pass | Pass | Pass
UpdateLoads | Pass | Pass | Pass
UpdateTemps | Pass | Pass | Pass
holdOrSched | Pass | Pass | Pass
Max Price Set | Pass | Pass | Pass
Testing Price | Pass | Pass | Pass
Loads(Deletion) | Pass | Pass | Pass

## Slide 21
Algorithm

## Slide 22
Algorithm

## Slide 23
Algorithm

## Slide 24
Algorithm

## Slide 25
Start
Time > x min ?
Calculate Cost [₵]
Σ Total Cost Load 1
Σ Total Cost
(Consumption)
Check status of Load
No
Yes
OFF
ON
Calculate Cost [₵]
Calculate Cost [₵]
…
Load 1
Load 2
Load N
Σ Total Cost Load 2
Σ Total Cost Load N
Algorithm
Consumption Cost [₵]= RTP [₵/Wmin] * Load Rating [W] * Elapsed Time [min]

## Slide 26
Web-Application   Main Controller
Socket Connection
Main Controller
IP: 192.168.1.3
Information Exchange:
ON/OFF Event
Check Status of the loads (if they are active)
Update each load’s information or save new load
Set Temperature Event
Set hold or schedule option
Check thermostat temperature reading
Update temperature schedule
Set User preferred monthly maximum price
(During testing) Send current Real Time Price
Via nRF24L01+
Load Controller
Notes: MGR

## Slide 27: Simulation
Chart: Load Consumption vs. Time
| 0 | 4.1666666666666664E-2 | 8.3333333333333301E-2 | 0.125 | 0.16666666666666699 | 0.20833333333333301 | 0.25 | 0.29166666666666702 | 0.33333333333333298 | 0.375 | 0.41666666666666702 | 0.45833333333333298 | 0.5 | 0.54166666666666696 | 0.58333333333333304 | 0.625 | 0.66666666666666696 | 0.70833333333333304 | 0.75 | 0.79166666666666696 | 0.83333333333333304 | 0.875 | 0.91666666666666696 | 0.95833333333333304
RTP*kWh | 61.56 | 47.872 | 63.272 | 44.792 | 0.828 | 20.9 | 0 | 0.972 | 0.936 | 0.9 | 0.9 | 0.864 | 0.846 | 0.828 | 0.828 | 0.9 | 6.49 | 27 | 15.576 | 15.048 | 8.692 | 8.036 | 23.644 | 0.81
SP*kWh | 91.656 | 72.896 | 96.346 | 68.206 | 1.206 | 28.006 | 0 | 1.206 | 1.206 | 1.206 | 1.206 | 1.206 | 1.206 | 1.206 | 1.206 | 1.206 | 7.906 | 30.15 | 17.688 | 17.688 | 10.988 | 10.988 | 34.438 | 1.206
RTP | 4.5 | 4.4 | 4.4 | 4.4 | 4.6 | 5 | 5.9 | 5.4 | 5.2 | 5 | 5 | 4.8 | 4.7 | 4.6 | 4.6 | 5 | 5.5 | 6 | 5.9 | 5.7 | 5.3 | 4.9 | 4.6 | 4.5
Standard Price (SP) | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7 | 6.7

## Slide 28: Future Development
Later versions of this project could have the following features
  Metering
  Renewable Energy Generation
    Priority on solar
  Algorithm Machine Learning (AI)
  Security

## Slide 30
Budget Cont.

## Slide 31
Budget Cont.

## Slide 32: Thank you for your time!

## Slide 33: For more information please visit: www.eng.fsu.edu/~ospinju/

## Slide 34: Reference Slides

## Slide 35: Testing Results

## Slide 36: Testing Results

## Slide 37
Testing Results