## Slide 1: Home Energy Management
EML 4911C-Senior Design- Spring 2016 Presentation I

## Slide 2: Our Goal
With the implementation of our Home Energy Management System and the advantage of Real-Time Pricing (RTP) provided by electric utility companies, consumers have the ability to adjust their energy usage in order to reduce their electricity bill.
Sponsored by FEEDER – Foundation for Engineering Education for Distributed Energy Resource
Who are we?
Dillon Wiggins – EE – Project Manager
Pablo Aguirre – EE – Systems Engineer
Juan Ospina – CE & EE – Hardware Engineer
Michael Garcia-Rivas – CE – Software Engineer
Ivan Remete – EE – Electrical Engineer

## Slide 3
Internet
Router
Web Application
Main Controller
Electric
Vehicle
Water Heater
Thermostat
Design
Web Server
Load Controller
Load Controller
Load Controller

## Slide 4: House Design

## Slide 5: Thermostat
LM74 Temperature Sensor
  SPI
  0.0625°C Temperature Resolution
  −55°C to +150°C (-66°F to 302°F)
  Accuracy: −10°C to 65°C, ±1.25°C (max)

## Slide 6
Current sensor turns: 100
Current Detector
Detecting Active Loads Zero Cross Detect Utilizing LM139 Comparator

## Slide 7
Scale (V/div)
2
2
50m (A)
2
Current Detector: Zero Cross Detect Waveform

## Slide 8
Current sensor turns: 100
Current Detector: Adjusting Reference Voltage

## Slide 9
Sensor Current = 100mA
Sensor Current = 10mA
Current Detector: Adjusting Reference Voltage Negative Reference = 500mV

## Slide 10
Source: Florida Public Service Commission, Dec.2012
PV: Pecan Street Research Institute (Not to scale)
TYSP(Ten Year Site Plan) Utilities: Example Daily Load Curve (FL)
Figure 4
Ivan Remete

## Slide 11
Chart: Real Time Pricing Monday Feb. 8 –Friday Feb. 12
| 11:00 PM-12:00 AM | 12:00 AM-1:00 AM | 1:00 AM -2:00 AM | 2:00 AM -3:00 AM | 3:00 AM -4:00 AM | 4:00 AM -5:00 AM | 5:00 AM -6:00 AM | 6:00 AM -7:00 AM | 7:00 AM -8:00 AM | 8:00 AM -9:00 AM | 9:00 AM -10:00 AM | 10:00 AM -11:00 AM | 11:00 AM -12:00 PM | 12:00 PM - 1:00 PM | 1:00 PM -2:00 PM | 2:00 PM -3:00 PM | 3:00 PM -4:00 PM | 4:00 PM -5:00 PM | 5:00 PM -6:00 PM | 6:00 PM -7:00 PM | 7:00 PM -8:00 PM | 8:00 PM -9:00 PM | 9:00 PM -10:00PM | 10:00 PM -11:00 PM
M | 4.6 | 4.6 | 4.5 | 4.6 | 4.6 | 4.7 | 4.8 | 5.2 | 5.1 | 5 | 4.9 | 4.8 | 4.7 | 4.7 | 4.7 | 4.6 | 4.7 | 4.9 | 5.4 | 5.2 | 5 | 4.9 | 4.7 | 4.5
Tue | 4.3 | 4.2 | 4.2 | 4.2 | 4.3 | 4.4 | 4.8 | 5.5 | 5.1 | 4.9 | 4.8 | 4.7 | 4.6 | 4.6 | 4.5 | 4.5 | 4.5 | 4.8 | 5.6 | 5.2 | 5 | 4.8 | 4.6 | 4.5
W | 4.4 | 4.3 | 4.3 | 4.3 | 4.3 | 4.4 | 4.6 | 5.3 | 5.1 | 5 | 4.8 | 4.8 | 4.7 | 4.6 | 4.6 | 4.5 | 4.6 | 4.9 | 5.4 | 5.2 | 5 | 4.9 | 4.7 | 4.5
Thu | 4.5 | 4.4 | 4.4 | 4.4 | 4.4 | 4.6 | 5 | 5.9 | 5.4 | 5.4 | 5.1 | 5 | 4.8 | 4.7 | 4.7 | 4.6 | 4.6 | 5 | 6 | 5.7 | 5.3 | 5 | 4.6 | 4.5
F | 4.4 | 4.4 | 4.3 | 4.3 | 4.4 | 4.7 | 5.2 | 5.6 | 5.4 | 5.2 | 5 | 4.8 | 4.6 | 4.5 | 4.5 | 4.4 | 4.4 | 4.6 | 5.3 | 5 | 4.8 | 4.6 | 4.5 | 4.3
Source: Power Smart Pricing, Ameren Illinois
Ivan Remete

## Slide 12
Chart: Real Time Pricing Saturday Feb. 13 – Sunday Feb. 14
| 11:00 PM-12:00 AM | 12:00 AM-1:00 AM | 1:00 AM -2:00 AM | 2:00 AM -3:00 AM | 3:00 AM -4:00 AM | 4:00 AM -5:00 AM | 5:00 AM -6:00 AM | 6:00 AM -7:00 AM | 7:00 AM -8:00 AM | 8:00 AM -9:00 AM | 9:00 AM -10:00 AM | 10:00 AM -11:00 AM | 11:00 AM -12:00 PM | 12:00 PM - 1:00 PM | 1:00 PM -2:00 PM | 2:00 PM -3:00 PM | 3:00 PM -4:00 PM | 4:00 PM -5:00 PM | 5:00 PM -6:00 PM | 6:00 PM -7:00 PM | 7:00 PM -8:00 PM | 8:00 PM -9:00 PM | 9:00 PM -10:00PM | 10:00 PM -11:00 PM
Sat | 4.3 | 4.3 | 4.3 | 4.2 | 4.3 | 4.3 | 4.5 | 4.8 | 4.9 | 5.1 | 5.1 | 4.7 | 4.5 | 4.4 | 4.4 | 4.4 | 4.5 | 4.7 | 5.2 | 5.1 | 5 | 4.9 | 4.7 | 4.6
Sun | 4.6 | 4.6 | 4.5 | 4.5 | 4.4 | 4.5 | 4.6 | 4.7 | 4.7 | 4.7 | 4.6 | 4.4 | 4.3 | 4.2 | 4.2 | 4.2 | 4.2 | 4.4 | 4.6 | 4.6 | 4.5 | 4.4 | 4.3 | 4.2
Source: Power Smart Pricing, Ameren Illinois
Average monthly utility: $87 for Illinois, $123 for FL. <Electricity Local>
Ivan Remete

## Slide 13
Algorithm
Ivan Remete

## Slide 14
Algorithm
Ivan Remete

## Slide 15
Algorithm
Ivan Remete

## Slide 16
Algorithm
Ivan Remete

## Slide 17
Start
Time > 1 min ?
Calculate Cost [Cents]
Σ Total Cost Load 1
Σ Final Cost (Running Sum for that Month)
Check status of Load
No
Yes
OFF
ON
Calculate Cost [Cents]
Calculate Cost [Cents]
…
Load 1
Load 2
Load N
Σ Total Cost Load 2
Σ Total Cost Load N
Algorithm
Ivan Remete

## Slide 18
Priority 1-4 : Turn off loads at 45% of the maximum price set by the user
Priority 5-7 : 75% of the maximum price set
Priority 8-10: 95% of the maximum price set
Ivan Remete

## Slide 19: Testing Protocols
Test Completed:
1. Inner Mesh: Main Controller  Load Controllers
Line of Sight/Open Air Test
  Outside the Center of Advanced Power (CAPS) building
Indoor Test
  Inside the College of Engineering
2. Network/Socket Connection: Web/Server Application  Main Controller

## Slide 20: Testing Protocols
Inner Mesh: Main Controller  Load Controllers
Line of Sight/Open Air Test
  Outside the Center of Advanced Power (CAPS) building over 2,000 ft
Indoor Test
  Testing was done in the Atrium of the 3rd floor of the COE
  Main controller was connected to a power source while the Load Controller was connected to a computer and taken to different testing points across all three floors of the COE
  A set of bytes was continuously sent from Main Controller to Load Controller
Main Controller
Load Controller
Via nRF24L01

## Slide 21: Testing Results

## Slide 22: Testing Results

## Slide 23
Testing Results

## Slide 24: Combination of Collected Data
The Main Controller was on the third floor therefore the direct distance on other floors had to be calculated using the height.
There is about 25ft between floors
Building B has 4 large rooms
Building A has more open space

## Slide 25
Socket Connection
Real-Time Control of Loads
Real-Time Price Change on Server
Algorithm Response
AC Temperature Control
Website Performance
LAN (Local Area Network)
Main Controller
2. Router
3. Server – Web App
4. CellPhone
IP: 192.168.0.125
IP: 192.168.0.119
Items on Graph:
Main Controller
Router = Internet
Server = Webserver where website will be hosted. (A computer will be used to simulate as server).
Cellphone used to access the Web server.
Load Controllers
5. Load Controllers
Network Connection Tests

## Slide 26
Demo: Web-Application   Main Controller
Socket Connection
Main Controller
IP: 192.168.0.125
Information Exchange:
1. ON/OFF Event
2. Set Temperature Event
3. Set User preferred monthly maximum price
4. Send current Real Time Price

## Slide 27: Real Time Price Example
Max. Monthly Price = $ 100.00
Max. kW/h Price = $ (100.00/30 days)/24 Hours = 0.138 = $13.8 Cents per kWh
Algorithm:
  45 % of Max. kWh Price - Turn OFF Loads w/ Priority 1-4 = 0.062 = $6.2 Cents per kWh
  75 % of Max. kWh Price - Turn OFF Loads w/ Priority 5-7 = 0.103 = $10.3 Cents per kWh
  95 % of Max. kWh Price - Turn OFF Loads w/ Priority 8-10 = 0.131 = $13.1 Cents per kWh
  Pool Pump Priority = 1
  Tesla Car Priority = 9

## Slide 28: Objectives

## Slide 29: Objectives

## Slide 30: Current and Future Development
Algorithm Development
  Priority settings are currently grouped into only three (3) categories with little resolution
  Testing for current and comparing real-time pricing
  Threshold Calculation
    What percentage of the max price amount should turn off certain loads?
    Storing a weeks worth of data on the device to calculate the day’s value
Hardware cases and pricing custom acrylic
  Pricing custom acrylic
  Developing CAD files
Notes: priority settings:
--This does not take advantage of the 1-10 priority setting
--Little resolution when deciding which loads to cut off
Testing for current:
--Used to compare current load usage with real-time pricing
--Current sensor information will tel us which loads are being used. After calculating the power each load is drawing, the algorithm should determine which loads should be off.
Threshold calculation:
--Keeping the constant value of 45% of max price is simple but does not take full advantage of the system

## Slide 32
Budget Cont.

## Slide 33: Questions?

## Slide 34: Thank you for your time!