## Slide 1
Steam Engine
Sliding valve
Steam enters chamber from
left, leaving from right
both valves closed, piston moves to the right
Steam enters from right,
leaving from left
piston moves back to the left

## Slide 2
Simple steam power plant cycle
Heat in
Work out
Condensing back to iquid
form for easy transportation
Heat in
Work out
Heat out to cooling water
Work in
by pump

## Slide 3
Superheated steam
Saturated water
liquid+vapor
Compressed
(subcooled)
liquid
Phase Change
Above critical point,
there is no clear
distinction between
liquid and vapor phases
Melting
vaporization
sublimation
Constant pressure process

## Slide 4
p
v
p
T
T
V
Constant
temperature
lines
Constant
pressure
line

## Slide 5
(a) P-v diagram: Along the constant temperature line, increasing vapor pressure
will lead to higher density (lower specific volume) due to compression.
After it reaches the saturation pressure at that temperature, the vapor will condense
into liquid while the pressure remains constant until all vapor condense into liquid.
(b) T-v diagram: Along the constant pressure line, increasing liquid temperature
will lead to lower density (higher specific volume) due to thermal expansion.
At the saturation temperature, the liquid will vaporize into gaseous form at a constant
pressure until all liquid vaporize.

## Slide 6
p
T
P-T phase diagram
solid
liquid
vapor
Melting/freezing
Substances that contract
on freezing
Substances that expand
on freezing ex. Water.
Higher pressure makes
it more difficult to freeze, thus requiring
lower freezing temperature. The reverse is true for substances that contract on freezing
Critical point
Vaporization/condensation
Sublimation
Triple point: all three phases
coexist in equilibrium
Critical point: A limiting state above which there is no clear distinction between
liquid and vapor phases.