## Slide 1: Objectives
Introduce the thermodynamic property entropy (S) using the Clausius inequality
Recognize the fact that the entropy is always increasing for an isolated system (or a system plus its surroundings) based on the increase of entropy principle
Analysis of entopy change of a thermodynamic process (how to use thermodynamic table, ideal gas relation)
Property diagrams involving entropy (T-s and h-s diagrams)
Entropy balance: entropy change = entropy transfer + entropy change

## Slide 2: Entropy
Entropy: a thermodynamic property, can be used as a measure of disorder. The more disorganized a system the higher the entropy.
Defined using Clausius inequality
This inequality is valid for all cycles, reversible and irreversible.
Consider a reversible Carnot cycle
Define a thermodynamic property entropy (S), such that

## Slide 3: Entropy-2
Since entropy is a thermodynamic property, it has fixed values at a fixed thermodynamic states.
1
2
reversible
process
any
process
T
S
The entropy change during an irreversible process is greater than the integral of Q/T during the process. If the process is reversible, then the entropy change is equal to the integral of Q/T. For the same entropy change, the heat transfer for a reversible process is less than that of an irreversible. Why?

## Slide 4: Entropy Increase Principle
A process can take place only in the direction that complies with the increase of entropy principle, that is, Sgen0.
Entropy is non-conservative since it is always increasing. The entropy of the universe is continuously increasing, in other words, it is more disorganized and is approaching chaotic.
The entropy generation is due to the existence of irreversibilities. Therefore, the higher the entropy generation the higher the irreversibilities and, accordingly, the lower the efficiency of a device since a reversible system is the most efficient system.

## Slide 5: Entropy Generation Example
Example: Show that the heat can not transfer from the low-temperature sink to the high-temperature source based on the increase of entropy principle.
Source
800 K
Sink
500 K
Q=2000 kJ
S(source) = 2000/800 = 2.5 (kJ/K)
S(sink) = -2000/500 = -4 (kJ/K)
Sgen= S(source)+ S(sink) = -1.5(kJ/K) < 0
It is impossible based on the entropy increase principle
Sgen0, therefore, the heat can not transfer from low-temp. to high-temp. without external work input
If the process is reversed, 2000 kJ of heat is transferred from the source to the sink, Sgen=1.5 (kJ/K) > 0, and the process can occur according to the second law
If the sink temperature is increased to 700 K, how about the entropy generation? S(source) = -2000/800 = -2.5(kJ/K)
S(sink) = 2000/700 = 2.86 (kJ/K)
Sgen= S(source)+ S(sink) = 0.36 (kJ/K) < 1.5 (kJ/K)
Entropy generation is less than when the sink temperature is 500 K, less irreversibility. Heat transfer between objects having large temperature difference generates higher degree of irreversibilities