## Slide 1: EML 3015C Sample Test #3 Fall 1999
boiler
high-P
turbine
Low-P
turbine
pump
condenser
1
2
4
5
6
1
2
3
3
4
5
6
T
s
Problem 1: A superheat, reheat Rankine cycle will be designed based on the following conditions: (1) the pressure of the boiler is 8 MPa, (2) The pressure of the reheater at state 4 is 0.8 MPa, (3) The condenser is evacuated to a constant pressure of 0.01 MPa, (4) The qualities of the steam mixture exiting from the high pressure and low pressure turbines are 100% and 90%, respectively. Determine (a) the turbine work (per kg steam), (b) the pump work (per kg), (c) the total heat transfer (per kg), (d) the thermal efficiency, (e) the mass flow rate of the steam if the power output is 80 MW.

## Slide 2: Sample-test-3 Solution (1)

## Slide 3: Sample-test3-solution (2)
A-5

## Slide 4: Sample Test #3(2)
A cylinder/piston assembly contains 1 kg of air undergoes a thermodynamic cycle consisting of the following three reversible processes in series. The initial volume of the assembly is unknown. R=0.287(kJ/kg K), Cp=1.003(kJ/kgK), Cv=0.717(kJ/kgK), k=Cp/Cv=1.4
Process 1-2: isothermal compression from P1=0.1 MPa to P2=0.5 Mpa
Process 2-3: constant pressure expansion to T3=400 K
Process 3-1: adiabatic expansion to the initial state
Using the ideal gas model and Tds equation,
(a) sketch the cycle on P-v and T-s diagrams
(b) determine the net work done by the system
(c) determine the net heat transfer into the system

## Slide 5: Sample Test #3(2) solution
T
s
P
v
1
2
3
1-2, isothermal compression
2-3, constant pressure expansion
3-1, adiabatic expansion (isentropic)
First, establish a thermodynamic state table:
From the equation of the state
1-2, isothermal, T1=T2, P2=500 kPa
v2=(P1/P2)v1=(100/500)v1
2-3, constant pressure expansion
P3=P2=500 kPa, T3=400K, v3=0.23(m3/kg)
3-1, adiabatic expansion
T1=T3(P1/P3)(k-1)/k=400(1/5)0.287=252.6(K)
v1=RT1/P1=(0.287)(252.6)/100=0.725(m3/kg)
v2=v1/5=0.145 (m3/kg)
1
2
3

## Slide 6: Sample Test #3(2) solution (cont.)

## Slide 7: Sample Test #3(3)
A water container is partitioned into two regions as shown. One side contains 10 kg of hot water at 80°C while the other side contains 8 kg of cold water at 20°C. The specific heat of water is 4.2 (kJ/kg K) and it can be considered as incompressible. The partition is suddenly removed and allow the water to mix thoroughly. Assume the container is well insulated from the surroundings and the properties of the water do not change significantly with respect to its temperature, (a) Is this a reversible process? (b) What is the final equilibrium temperature? (c) Entropy generation during the process.
Water, 80°C
Water, 20°C

## Slide 8: Sample Test #3 solution (3)