## Slide 1
Ideal Gas Model
For many gases, the ideal gas assumption is valid and the P-v-T relationship can be simplified by using the ideal gas equation of state: Pv=RT (Compressibility factor Z=1)
For an ideal gas, it can be shown that the specific internal energy u is a function of temperature only, u=u(T)
Accordingly, specific enthalpy is a function of temperature only, since h(T)=u(T)+pv=u(T)+RT
Physically, a gas can be considered ideal only when the intermolecular forces are weak. This usually happens in low pressure and high temperature ranges.

## Slide 2
Ideal Gas Model(cont.)
Specific ratio k=cp/cv, cp=cv+R
In some cases, the temperature dependence of the specific heat can be written in polynomial form, see Table A-2, p. 845
Otherwise, ideal gas tables are also available. They are easier to use compared to the thermodynamic tables since temperature is the only parameter.

## Slide 3
Example: Two tanks filled with air are connected by a valve as shown. If the valve is opened and the gases are allowed to mix while receiving heat from the surrounding. The final temperature is 227°C. Determine (a) the final pressure of the mixture, (b) the amount of heat transfer during the mixing process. Assume ideal gas model is valid.
Air, 1 kg,
127°C
0.05 MPa
Air, 2 kg
247°C
0.02 MPa
Assume: little change of KE & PE
Both the initial and the final states are in equilibrium
From table A-1, Tc=132.5 K, Pc=3.77 Mpa
Tr=3, Pr=0.0133 for tank 1
From Figure A-13, compressibility factor Z=1, good ideal gas assumption