## Slide 1
Basic Fluid Properties and Governing Equations
Density (): mass per unit volume (kg/m3 or slug/ft3)
Specific Volume (v=1/): volume per unit mass
Temperature (T): thermodynamic property that measures the molecular activity
of an object. It is used to determine whether an object has reached thermal
equilibrium.
Pressure (p):pressure can be considered as an averaged normal force exerted
on a unit surface area by impacting molecules.
( , N/m2 or pascal; lb/in2 or psi)
Pascal law: (under static condition) pressure acts uniformly in all directions. It also
acts perpendicular to the containing surface.
If a fluid system is not in motion, then the fluid pressure is equal its thermodynamic
pressure.
Atomspheric pressure (patm): pressure measured at the earth’s surface.
1 atm = 14.696 psi = 1.01325 x 105 N/m2 (pascal)
Absolute pressure: pressure measured without reference to other pressures.
Gage pressure: pgage= p absolute - patm

## Slide 2
Atmospheric pressure can be measured using a barometer:
Vacuum
p=0
Patm=1.01x105 Pa
p=0
p=patm
L

## Slide 3
p
p+dp
h
Free surface, p=p
Example: If a container of fluid is accelerating
with an acceleration of ax to the right as shown below,
what is the shape of the free surface of the fluid?
ax
p
p+dp

dx
dy
x
y

## Slide 4
Buoyancy of a submerged body
h1
h2
p2=p+Lgh2
p1=p+Lgh1
free surface
Net force due to pressure difference
dF=(p2-p1)dA=Lg(h2-h1)dA
The principle of Archimedes:
The buoyancy acting on a submerged object is equal to the weight of the
displaced fluid due to the presence of the object.
This law is valid for all fluid and regardless of the shape of the body. It can
also be applied to both fully and partially submerged bodies.

## Slide 5
Example: Titanic sank when it struck an iceberg on April 14, 1912. Five
of its 16 watertight compartments were punctuated when it collides with
the iceberg underwater. Can you estimate the percentage of the iceberg that
is actually beneath the water surface? It is known that when water freezes
at 0 C, it expands and its specific gravity changes from 1 to 0.917.
buoyancy
weight
When the iceberg floats, its weight balances
the buoyancy force exerted on the iceberg by
the displaced water.

## Slide 6
Properties (cont.)
Viscosity: Due to interaction between fluid molecules, the fluid flow
will resist a shearing motion. The viscosity is a measure of this resistance.
Moving Plate
constant force F
constant speed U
Stationary Plate
From experimental observation, F  A(U/H)=A(dV/dy)
H

## Slide 7
Boundary Layer Concept
Immediately adjacent to a solid surface, the fluid particles are slowed
by the strong shear force between the fluid particles and the surface.
This relatively slower moving layer of fluid is called a “boundary layer”.
Laminar
Turbulent
Question: which profile has larger wall shear stress?
In other words, which profile produces more frictional
drag against the motion of the solid surface?

## Slide 8
Partial Differential Equations (PDE): Many physical phenomena are
governed by PDE since the physical functions involved usually depend on two
or more independent variables (ex. Time, spatial coordinates). Their variation with
respect to these variables need to be described by PDE not ODE (Ordinary
Differential Equations).
Example: In dynamics, we often track the change of the position of an object
in time. Time is the only variable in this case. X=x(t), u=dx/dt, a=du/dt.
In heat transfer, temperature inside an object can vary with both time and space.
T=T(x,t). The temperature varies with time since it has not reach its thermal
equilibrium.
The temperature can also vary in space as according to the Fourier’s law:

## Slide 9: Basic equations of Fluid Mechanics
Mass conservation (continuity equation):
  The rate of mass stored = the rate of mass in - the rate of mass out
Within a given time t, the fluid element with
a cross-sectional area of A moves a distance of
L as shown.
The mass flow rate can be represented as
Area A

## Slide 10
Keep density constant,
volume changes with time
ex: blow up a soap bubble
Keep volume constant,
density changes with time
ex: pump up a basketball
For steady state condition: mass flow in = mass flow out

## Slide 11
Examples: filling up an empty tank
Water is fed into an empty tank using
a hose of cross-sectional area of 0.0005 m2.
The flow speed out of the hose is measured
to be 10 m/s. Determine the rate of increase
for the water height inside the tank dh/dt.
The cross-sectional area of the tank is 1 m2.
h(t)
0, no mass out

## Slide 12
Section 2, A2=1 m2
Section 1, A1=5 m2
V1=20 m/s
V2=?

## Slide 13
Momentum Conservation: (Newton’s second law)
Net external forces lead to the change of linear momentum
dx
dz
dL
P
P+dP

First, neglect viscosity
Euler’s Equation

## Slide 14
Euler’s Equation:
First, dz=0 no elevation variation
If dp>0, pressure increases as fluid flows downstream
then dV<0, velocity decreases due to the adverse pressure gradient
and vice versa.
If dp=0, no external pressure gradient
If dz<0, fluid flows to a lower point, dV>0, its velocity increases
and vice versa
If dV=0, no flow
If dz<0, into the lower elevation inside the static fluid system,
dp>0, pressure increases

## Slide 15
Air flows through a converging duct as shown. The areas at sections 1 & 2
are 5 m3 and 1 m3, respectively. The inlet flow speed is 20 m/s and we know
the outlet speed at section 2 is 100 m/s by mass conservation. If the pressure
at section 2 is the atmospheric pressure at 1.01x105 N/m2, what is the pressure
at section 1. Neglect all viscous effects and given the density of the air
as 1.185 kg/m3.
Section 1
Section 2