## Slide 1
Lab. Assignment 2, part 1: Hot water flows steadily into the water tank with a
constant mass flow rate of 5 kg/s and a constant temperature of 90 C. Initially, the
tank contains cold water of 20 C as shown. The tank has a constant cross-sectional
area of 0.2 m2. (a) Use mass conservation concept, determine and plot the water level
(h) as a function of time, up to 100 second. (b) Use energy balance concept, determine
and plot the water temperature (T) inside the tank as a function of time. Assume the
hot water mix instantaneously with the cold water inside the tank and no heat losses.
0.5 m
Atank = 0.2 m2

## Slide 2
Part 2: If the bottom of the tank is punctuated when the hot water is starting to flow
into the tank and the small hole has an area of 0.00113 m2, determine and plot the
water level as a function of time. It is known that the velocity of flow through the
hole (V) is related to the water level of the tank (h) as V= , where g is the
gravitational constant. This is called the Torricelli’s theorem. We will derive this
relation this week using the famous Bernouuli’s equation.
0.5 m
0.00113 m2

## Slide 3
Subject Review:
Neglect heat transfer
Heat out q=dQ/dt
Work in dW/dt