## Slide 1: Second Law of Thermodynamics
Identify the direction of a process. (ex: Heat can only transfer from a hot object to a cold object, not the other around)
Can be used to determine the “Quality” of the energy. (ex: A high-temperature energy source has a higher quality since it is easier to extract energy from it to deliver useable work.)
Can be used to exclude the possibilities of constructing 100% efficient heat engine and any perpetual-motion machines. (Kevin-Planck statement and Clausius statement)
Reversible processes and irreversibilities.
Determine the theoretical limits for the performance of engineering systems. (ex: A Carnot engine is theoretically the most efficient heat engine and its performance can be used to set as a standard for other practical machines)

## Slide 2: Second Law-cont.
A process can not happen unless it satisfies both the first and second laws of thermodynamics. The first law characterizes the balance of energy which defines the “quantity” of energy. The second law defines the direction which the process can take place and its “quality”.
Define a “Heat Engine”: A device that converts heat energy into work while operating in a cycle. Ex: A steam power plant.
Heat engine
QH
QL
TH
TL
Wnet
Q-Wnet=U, U=0 for a cycle
Wnet=QH-QL
Thermal efficiency
th=Wnet/QH=(QH-QL)/QH
=1-(QL/QH)
Question: Can we produce an 100% heat engine? QL=0?

## Slide 3: Kevin-Planck Statement
It is impossible for any device that operates on a cycle to receive heat from a single reservoir and produces a net amount of work.
This is a statement without proof, but has not been disproved yet.
Therefore, the question from previous slide is “NO”. It is not possible to built a heat engine that is 100%.
Heat engine
QH
TH
Wnet
A heat engine has to reject some energy into a lower temperature sink in order to complete the cycle.
TH>TL in order to operate the engine. Therefore, the higher the temperature, the higher the quality of the energy source since it can produce useable work to more lower-temperature energy sinks.

## Slide 4: Heat Pump
A “heat pump” is defined as a device that transfers heat from a low-temperature source to a high-temperature one. Ex: a heat pump to extract energy from outside cold outdoor air into the warm indoors.
Heat pump
QH
QL
TH
TL
Wnet
Coefficient of Performance (COP): COP=QH/Wnet=QH/(QH-QL)
= 1/(1-QL/QH)
COP>1, ex: a typical heat pump has a COP in the order of 3
Question: can we built a heat pump operating at , that is Wnet=0? QH=QL?

## Slide 5: Clausius Statement
It is impossible to construct a device that operates in a cycle and produces no effect other than the transfer of heat from a lower-temperature body to a higher-temperature body.
Also can not be proved, rather depends on experimental observations.
Heat can not transfer from low temperature to higher temperature unless external work is added.
Heat pump
QH
QL
TH
TL
Therefore, it is not possible to built a heat pump without external work input.

## Slide 6: Equivalence of the Two Statements
It can be shown that the violation of the one statement means the violation of the other statement. They are equivalent.
Heat pump
QH+QL
QL
TH
TL
Wnet
=QH
Heat engine
QH
100% heat engine: against K-P Statement
Heat pump
QL
QL
TH
TL
Heat transfer from low-temp body to high-temp body without work- violation of the C-statement

## Slide 7: Perpetual-Motion Machine
Imagine that if we can extract energy from unlimited low-temperature energy sources such as the ocean or the atmosphere.
Heat engine
Heat pump
QL
QH
QH
QH-QL
Wnet=QL
TH
Ocean TL
It is against the Kevin-Planck statement: it is impossible to build an 100% heat engine.

## Slide 8: Reversible and Irreversibilities
A reversible process means there are no irreversibilities exist when a system is undergoing interaction with its surroundings. Therefore, the process can be reversed without leaving any trace on its surroundings. Both system and the surroundings are returned to their initial states. It is an ideal process that can not happen in reality. However, if the irreversibilities are small enough, some processes can be approximated as reversible. Ex: a frictionless pendulum, quasi-equilibrium expansion and compression of gas in a cylinder/piston assembly (in an idealized Carnot cycle)
Irreversibilities: friction, sudden expansion and compression, heat transfer between two bodies with finite temperature difference.