## Slide 1
The Equations of State
Equations that relate the pressure, temperature, and specific volume
of a substance. They predict the p-v-T relationship of a “gas”
reasonably well within selected regions.
Example: Ideal gas equation:
Note: many gases such as air, oxygen can be treated as ideal gases.
However, dense gases such as water vapor and refrigerant vapor
should not be treated as ideal gas. Use property table instead.

## Slide 2
Ideal Gas Assumption
T
v
Ideal gas behavior( high temp)
Ideal gas behavior(low pressure)
Non-ideal gas
behavior
Note: for most gases
Deviate from ideal gas in the vicinity of the critical point
and saturated vapor line
behaves like ideal gas at high temperature and low pressure
regions

## Slide 3
Compressibility Factor-A measure of deviation from the ideal gas
Z: compressibility factor, Z=1, ideal gas
Pr=P/Pcr
Tr=T/Tcr
Example: steam T=310° C, P=10 MPa, Tcr=647.3K, Pcr=22.09 MPa (From Table A-1, p. 842); Tr=0.9, Pr=0.45, Z=0.75, different from ideal gas
Fig A-3