## Slide 1: Gas Power Cycle - Jet Propulsion Technology, A Case Study

## Slide 2: Ideal Brayton Cycle
Air
Fuel
Products
Compressor
Turbine
Combustor
1
2
3
4
P
v
T
s
1
2
3
4
1
2
3
4
1-2 Isentropic compression
2-3 Constant pressure heat addition
3-4 Isentropic expansion
4-1 Constant pressure heat rejection

## Slide 3: Ideal Brayton Cycle - 2

## Slide 4: Jet Propulsion Cycle
1
2
3
4
5
6
P=constant
P=constant
qout
qin
1-2, inlet flow decelerates in the diffuser; pressure and temperature increase
5-6, outlet flow accelerates in the nozzle section, pressure and temperature decrease
T
s

## Slide 5: Propulsive Power
Jet Engine
Mass flow in
Inlet velocity, Vin
Mass flow out
Exit velocity, Vexit
Action force, FA
Reaction force, FR

## Slide 6: Gas Turbine Improvements
Increase the gas combustion temperature (T3) before it enters the turbine since th = 1 - (T4/T3)
  Limited by metallurgical restriction: ceramic coating over the turbine blades
  Improved intercooling technology: blow cool air over the surface of the blades (film cooling), steam cooling inside the blades.
Modifications to the basic thermodynamic cycle: intercooling, reheating, regeneration
Improve design of turbomachinery components: multi-stage compressor and turbine configuration. Better aerodynamic design on blades (reduce stall).

## Slide 7: PW8000 Geared Turbofan Engine
Twin-spool configuration: H-P turbine drives H-P compressor
L-P turbine drives L-P compressor, on separated shafts
Gearbox to further decrease the RPM of the fan
More fuel efficiency
Less noise
Fewer engine parts
From Machine Design Magazine
Nov. 5, 1998