## Slide 1
EML3015C Thermal-Fluid I Fall 1998 Homework 4
1. A pump transfers water from one reservoir to another as shown. The total frictional
loss of the piping is given as KL(V2/2g) where V is the averaged velocity in the pipe.
The total head provided by the pump ,H, is a function of the volume flow rate, Q, as
given by H=100-50*Q, where H in m of water, Q in m3/s. If the loss coefficient
KL=10 and the pipe diameter is 0.1 m, what is the flow rate pumped to to the upper reservoir.
50 m
pump

## Slide 2
2. Water flows into a hydraulic turbine at 10 m3/s and a pressure of 100 kPa through
a 0.5 m diameter pipe. The turbine discharge into a 0.8 m dia. pipe with a pressure
of 50 kPa. If it is known that the turbine produces 2000 hp, determine the power
loss between the two sections.
2000 hp
Q1=10 m3/s, D1=0.5 m pipe
p1=100 kPa
5 m
D2=0.8 m
P2=50 kPa