## Slide 1
Energy Conservation(cont.)
Example: Superheated water vapor is entering the steam turbine with a mass
flow rate of 1 kg/s and exhausting as saturated steamas shown. Heat loss from
the turbine is 10 kW under the following operating condition. Determine the
power output of the turbine.
P=1.4 Mpa
T=350 C
V=80 m/s
z=10 m
P=0.5 Mpa
100% saturated steam
V=50 m/s
z=5 m
10 kw
From superheated vapor table:
hin=3149.5 kJ/kg
From saturated steam table: hout=2748.7 kJ/kg

## Slide 2
These properties are all dependent: specify one to determine all (because they are in a saturation state)
Liquid and vapor phases coexist, the total mass of the mixture, m, is the sum of the liquid mass and the vapor mass: m=mf+mg, The ratio of the mass of vapor to the total mass is called the quality of the mixture: x=mg/m
f-liquid phase g-vapor phase
Saturated Steam

## Slide 3
Total volume is the sum of liquid volume and vapor volume:
V = Vf + Vg = mfvf + mgvg, where v is the specific volume or 1/
V = m(1/) = mv]
V/m = v = Vf/m + Vg/m = (mf/m)vf + (mg/m)vg
= [(m-mg)/m]vf + (mg/m)vg
= (1-x)vf+xvg= vf + x(vg-vf) = vf + xvfg, where vfg = vg-vf
Similarly, all other saturated thermodynamic properties can be
expressed in the same manner:
Ex: internal energy: u = (1-x)uf+xug= uf + x(ug-uf) = uf + xufg
since U = Uf + Ug = mfuf + mgug

## Slide 4
Saturated Steam Table
hg(p=0.5 Mpa) = 2746.4 + (2758.1-2746.4)/(0.6178-0.4758)*(0.5-0.4758)
=2748.4 kJ/kg for 100% quality saturated vapor
p (Mpa)
hg (kJ/Kg)
Example: If the quality is 50% and the temperature is 150 C
hf = 632.2, hfg = 2114.2, hg = 2746.4
h = (1-x) hf + x hg = (1-0.5)(632.2) + 0.5(2746.4)
= 1689.3 (kJ/kg)
hf (kJ/kg)
hfg (kJ/kg)

## Slide 5
h(p=1.5MPa, T=350C)=3147.4 kJ/kg
h(p=1MPa, T=350C)=3157.7 kJ/kg
Superheated Steam
h(p=1.4MPa, T=350C)=3157.7+(3147.7-3157.7)*(0.4/0.5)
=3149.7 (kJ/kg)

## Slide 6
Compressed Liquid
Similar to the format of the superheated vapor table
In general, properties are not sensitive to pressure, therefore, can treat the
compressed liquid as saturated liquid at the given TEMPERATURE.
Given: P and T:
But not h, since h=u+pv, and it depends more strongly on p. It can be
approximated as