## Slide 1: EML 3015C Thermal-Fluid I Assignment 9 Fall 1999 Part 1. Isentropic Efficiency and Entropy Generation
Assignment 9-1: Steam enters the turbine steadily at 8 MPa and 400C and leaves at a pressure of 1 MPa. Determine (a) the work output if the process is isentropic. If the actual turbine is operating at 70% isentropic efficiency, determine (b) the actual work output, (c) the actual exit temperature of the steam, (d) the entropy generation (assume adiabatic). Base your calculation on 1 kg/s of steady steam flow.
P=1 MPa
P=8 MPa
T=400°C

## Slide 2
Part 2. Gas-Turbine Engine: engine that employs combustion hot-gas flow as the working medium by which heat energy is transformed into rotating mechanical energy. A gas turbine usually includes a compressor that pressurized air into a combustion chamber. The combustion products pass from the chamber through the nozzles to drive the turbine machinery. The rotating turbine drives the compressor and the external load, such as an electrical generator, or produces propulsive power such as an jet engine. A gas-turbine engine can be modeled using idealized thermodynamic cycles such as the Brayton cycle shown below.
Close the loop
adiabatic
reversible

## Slide 3
Fresh air is drawn into the compressor, where its pressure is raised by receiving energy from the rotating compressor blades. Although there is no heat transfer, the temperature is still increased because of the compression (adiabatic compression, isentropic compression). The high pressure air enters the combustion chamber and receives heat at constant pressure. The resulting high-temperature, high-pressure gases drive the turbine and eventually expand into the surrounding. Work output is delivered as turbine rotating mechanical energy. If we assume the exhaust gases expand to the same condition as the inlet air, then we can model the open gas-turbine processes as a closed thermodynamic cycle as described by the Brayton cycle shown earlier. Assume steady-state flow process and we can analyze the cycle based on unit mass flow: From energy balance:

## Slide 5
Assignment 9-2: We would like to design a turbine power plant operating on an ideal Brayton cycle with a specific pressure ratio rp. The air temperature is 300 K (T1) at the compressor inlet and the maximum temperature of the turbine temperature (T3) is limited to 1200 K to avoid material failure of the turbine blades. Assume ideal gas and cp=1.003 kJ/kg K. (a) Plot the thermal efficiency of the power plant as a function of the pressure ratio. (b) Determine the net work output and heat transfer Qin as a function of the pressure ratio. (c) Determine the pressure ratio at which the turbine will produce the maximum work output; also determine the thermal efficiency at this pressure ratio. Discuss your results.