## Slide 1: The Carnot Cycle
Idealized thermodynamic cycle consisting of four reversible processes (any substance):
  Reversible isothermal expansion (1-2, TH=constant)
  Reversible adiabatic expansion (2-3, Q=0, THTL)
  Reversible isothermal compression (3-4, TL=constant)
  Reversible adiabatic compression (4-1, Q=0, TLTH)
1-2
2-3
3-4
4-1

## Slide 2: The Carnot Cycle-2
Work done by gas = PdV, area under the process curve 1-2-3.
1
2
3
3
2
1
Work done on gas = PdV, area under the process curve 3-4-1
subtract
Net work
1
2
3
4
dV>0 from 1-2-3
PdV>0
Since dV<0
PdV<0

## Slide 3: The Carnot Principles
The efficiency of an irreversible heat engine is always less than the efficiency of a reversible one operating between the same two reservoirs. th, irrev < th, rev
The efficiencies of all reversible heat engines operating between the same two reservoirs are the same. (th, rev)A= (th, rev)B
Both Can be demonstrated using the second law (K-P statement and C-statement). Therefore, the Carnot heat engine defines the maximum efficiency any practical heat engine can reach up to.
Thermal efficiency th=Wnet/QH=1-(QL/QH)=f(TL,TH) and it can be shown that th=1-(QL/QH)=1-(TL/TH). This is called the Carnot efficiency.
For a typical steam power plant operating between TH=800 K (boiler) and TL=300 K(cooling tower), the maximum achievable efficiency is 62.5%.

## Slide 4: Example
Let us analyze an ideal gas undergoing a Carnot cycle between two temperatures TH and TL.
1 to 2, isothermal expansion, U12 = 0
QH = Q12 = W12 = PdV = mRTHln(V2/V1)
2 to 3, adiabatic expansion, Q23 = 0
(TL/TH) = (V2/V3)k-1  (1)
3 to 4, isothermal compression, U34 = 0
QL = Q34 = W34 = - mRTLln(V4/V3)
4 to 1, adiabatic compression, Q41 = 0
(TL/TH) = (V1/V4)k-1  (2)
From (1) & (2), (V2/V3) = (V1/V4) and (V2/V1) = (V3/V4)
th = 1-(QL/QH )= 1-(TL/TH) since ln(V2/V1) = ln(V4/V3)
It has been proven that th = 1-(QL/QH )= 1-(TL/TH) for all Carnot engines since the Carnot efficiency is independent of the working substance.

## Slide 5: Carnot Efficiency
A Carnot heat engine operating between a high-temperature source at 900 K and reject heat to a low-temperature reservoir at 300 K. (a) Determine the thermal efficiency of the engine. (b) If the temperature of the high-temperature source is decreased incrementally, how is the thermal efficiency changes with the temperature.
Lower TH
Increase TL

## Slide 6: Carnot Efficiency
Similarly, the higher the temperature of the low-temperature sink, the more difficult for a heat engine to transfer heat into it, thus, lower thermal efficiency also. That is why low-temperature reservoirs such as rivers and lakes are popular for this reason.
To increase the thermal efficiency of a gas power turbine, one would like to increase the temperature of the combustion chamber. However, that sometimes conflict with other design requirements. Example: turbine blades can not withstand the high temperature gas, thus leads to early fatigue. Solutions: better material research and/or innovative cooling design.
Work is in general more valuable compared to heat since the work can convert to heat almost 100% but not the other way around. Heat becomes useless when it is transferred to a low-temperature source because the thermal efficiency will be very low according to th=1-(TL/TH). This is why there is little incentive to extract the massive thermal energy stored in the oceans and lakes.