## Slide 1
Example: Electric heater is often used in houses to provide heating during winter
months. It consists of a simple duct with coiled resistance wires as shown. Consider
a 20 kW heating system such that the air enters at 100 kPa and 17° C with a mass
flow rate of 2 kg/s. If it is known that the air leaves the duct with an exit temperature
of 27° C (same pressure), determine the heat loss from the duct.
dEg/dt=20 kW
Heat loss dQ/dt=?
To=27° C
To=17° C
Assume: steady state, negligible
KE and PE changes, air can be
considered as idea gas

## Slide 2
Transient Energy Balance (Unsteady State)
Heat in q=dQ/dt
Work out dW/dt
E(t) not constant
(4.19), p. 157 in Cengel’s book

## Slide 4
Example: Steam at a pressure of 2 MPa and a temperature of 350° C is exiting
out from a tank through a valve to drive a turbine as shown. The exhausting steam
enters an initially evacuated tank with a volume of 1 m3. The valve is closed when
the second tank is filled with steam at a pressure of 1.4 MPa and a temperature of
500° C. Assume no significant heat transfer and KE and PE changes are also
negligible. Determine the amount of work developed by the turbine.
Steam
2 MPa
350 ° C
V=1 m3
initially
evacuated
control volume
to be analyzed
Assumptions: dQ/dt=0 adiabatic process, KE and PE are negligible
Steam properties at the first tank remains constant
The second tank reaches final equilibrium after the filling process ends

## Slide 5
0
0