## Slide 1: Danny and the Intake Posse
Featuring
Daniel Aronhalt
Marcnell Pierre
Gram Holmes
Dwayne White
Mauricio Ballesteros
Sean Henderson
Thermal Fluids II
April 15, 1999
See Web Site: www.eng.fsu.edu/~hender/project1.html

## Slide 2: OBJECTIVE
Test and Analyze an intake system for the SAE formula car.
Determine relationship between entrance velocities for runners
Find pressure distribution in plenum
Determine velocity profile through out the engine cycle.

## Slide 3: MOTIVATION
Improve engine power and throttle response.
Obtain consistent flow for each runner.
To show even pressure and velocity profiles at runners.

## Slide 4: PLENUM
Fuel injection engines
Improve Uniformity
Improve HP
Throttle response
Sets up for runner resonance

## Slide 5: HOW IT WORKS
Air enters through the throttle body
Flows through restrictor
Plenum accumulates flow volume
Runners retrieve air from plenum volume

## Slide 6: EQUIPMENT
Digital Manometer
Suction pump
Pitot tube
Pressure Taps

## Slide 7: EXPERIMENT PROCEDURE
PRESSURE
Place pressure taps in strategic positions
Supply vacuum for correct flow rate
Register the pressure readings for each runner under suction

## Slide 8: PRESSURE POINTS
21 pressure taps
Pressure taps are located @ 4, 5, 8 in. from the base
.625in apart
Start from the center line to the edge
Only half of plenum: uniform

## Slide 9: PITOT TUBE (VELOCITY)
Pitot tube is moved from left to right to record dynamic pressure.
Compute the velocity profile.
Determine flow characteristics.

## Slide 10: FLOW DISTRIBUTION
Picture shows the entrance flow and no separation

## Slide 11: FLOW PROFILE

## Slide 12: DATA
Velocity from Pitot tube data

## Slide 13: VELOCITY RESULTS
Velocity increases as pitot tube approaches activated runners streamline
Runner velocities were almost identical ( 0.76% difference)
Velocity data indicates possible vortex formation and boundary layers

## Slide 14: PRESSURE for R1
Largest pressure change is blue entrance curve (possible boundary layer)
Largest pressure is near the runner entry (yellow curve)

## Slide 15: PRESSURE RESULTS
Minimum pressure at entrance and maximum pressure near runners
Pressure remains low for points opposite from the activated runner (Vortex?)
Pressure data for runners one and two were similar (7.44% difference)

## Slide 16: CONCLUSIONS
Pressure at each runner is similar (desired)
Data suggests vortex formation (possible negative effect)
Velocity for runners is almost identical (desired)

## Slide 17: FUTURE STEPS
Investigate vortices formation
Investigate transient flow response
Research different plenum shapes
Research different runner shapes