## Slide 1
Superheat Rankine Cycle Example
Turbine
pump
condenser
1
2
3
4
Qout
Qin
Wout
Win
boiler
Consider the same Rankine power cycle as we analyzed before. But this time we are going to superheat the steam in the boiler before allowing it to enter the turbine at 6 MPa. The steam exits from the turbine will be 100% saturated vapor as shown. After condensing, saturated liquid enters the pump at a pressure of 0.1 MPa. Determine (a) the rate of heat transfer into the boiler per unit mass, (b) the net power generation per unit mass. (c) the thermal efficiency,
T
s
1
2
3
4

## Slide 2: solution
A-5
A-5

## Slide 3: Solution(cont.)
A-6

## Slide 4: Discussion
Without going through tedious calculation, can you estimate roughly the thermal efficiency of the first Rankine system (without superheating) will be? Does this estimated value close to the calculated one (35.3%).
By increasing the condensing pressure from 0.01 MPa to 0.1 MPa, what do you think the thermal efficiency of the system will vary based on this change?
Can you estimate the change (order of magnitude estimation) without going through calculation.
Based on our calculation, the thermal efficiency actually decreases from 35.3% to 33.8%. Is this value consistent with your estimation? Why and why not?

## Slide 5: Discussion (cont.)
If we assume the system is operated under a Carnot cycle, then =1-TL/TH, where TL=45.8°C, TH=275.6 °C, both from table A-5. (How?). Therefore, =0.418. The Rankine efficiency should be less than that.
Increase pressure to 0.1 MPa, the condensing temperature increases to 99.6 °C. Therefore, the efficiency based on Carnot cycle should decrease to 0.321.
The percentage change is (0.418-0.321)/0.418=23.2%, a significant drop in thermal efficiency.
However, the real change of the thermal efficiency is very small. Explain why?

## Slide 6: Super- Reheat- Rankine Cycle
boiler
high-P
turbine
Low-P
turbine
pump
condenser
1
2
3
4
5
6
T
s
1
2
3
5
6
4
high-P
turbine
low-P
turbine
We are going to add a low pressure turbine (5-6) to the system we just analyzed. Before going into the L-P turbine, the exit steam from the first turbine (3-4) is reheated in the boiler at a constant pressure. Assume both 4 & 6 are at 100% saturated vapor state and the vapor exiting from the H-P turbine (state 4) expands to a lower pressure of 2 MPa (P4=2 MPa) before it is being reheated at a constant pressure to the state 5. Recalculate (a) the thermal efficiency of the system.

## Slide 7: Solution
A-5
A-6

## Slide 8: Solution(cont.)
A-6