## Slide 1: Entropy of a Pure Substance
Entropy is a thermodynamic property, the value of entropy depends on the state of the system. For example: given T & P, entropy, S, can be obtained from a thermodynamic table just like v, u, h.
If the state is a mixture of liquid and vapor, the entropy can be determined as: s = sf + xsfg, where x is the quality and sf and sfg are saturated values listed in the saturation table.
For compressible liquid, the entropy can be approximated by the entropy of the saturated liquid at the given temperature since it is not a function of pressure: s@T,P  sf@T
T
s (kJ/kg)
P = const.
v = const

## Slide 2: Example
A rigid tank contains 5 kg of refrigerant-134a initially at 20C and 140 kPa. The refrigerant is cooled until its pressure drops to 100 kPa. Determine the entropy change of the refrigerant during this process.
Constant volume process: v1=v2
initial state: P1=140 kPa, T1=20C, from table A-10
s1=1.0532(kJ/kg K), v1=0.1652(m3/kg)
final state: P2=100 kPa, and v2=v1=0.1652 (m3/kg)
from table A-9 vf=0.0007258(m3/kg)
vg=0.1917(m3/kg)
since vf < v2 < vg it is inside the saturation region
x2=(v2-vf)/vfg=(0.1652-0.0007258)/0.191=0.865
from table A-9, sf = 0.0678, sg = 0.9395
s2 =sf + x2(sg-sf)
= 0.0678 + 0.865(0.9395-0.0678) = 0.822
S = m(s2 - s1) = (5)(-0.231) = -1.157 (kJ/kg K)

## Slide 3: Isentropic Process
Isentropic process: entropy is a constant, s=0. A reversible, adiabatic process is always isentropic since no entropy generation due to irreversibilities (sgen=0) and no change of entropy due to heat transfer (ds=Q/T=0).
The reverse is not always true: An isentropic process is not necessary a reversible, adiabatic process. Why?
Carnot cycle consists of two isentropic processes: reversible, adiabatic compression and expansion plus two isothermal processes.
T
s
Isentropic
s=constant
isothermal

## Slide 4: Example
Steam enters an adiabatic turbine at 5 MPa and 450C and leaves at a pressure of 1.4 MPa. Determine the work output of the turbine per unit mass flowing through the turbine if we can assume the process is reversible and neglect all changes of KE and PE.
Wout = m(h1-h2), Wout/m = h1-h2
state 1: P1=5 MPa, T1=450C, from table A-6
h1=3316.2(kJ/kg), s1=6.819(kJ/kg K)
State 2: P2=1.4 MPa, s2=s1=6.819>sg=6.469 @ 1.4 MPa(table A-5),
state 2 is superheated: from table A-6 through interpolation
h2=2927.2+[(3040.4-2927.2)/(6.9534-6.7467)](6.819-6.7467)=2966.8 (kJ/kg). Wout/m = h1-h2 = 349.4 (kJ/kg)
1
2
5 MPa
1.4 MPa
T
s
sg