## Slide 1
EML 3015C Thermal-Fluid I Assignment 7 Fall 1999
Gas-Turbine Engine: engine that employs combustion hot-gas flow as the working medium by which heat energy is transformed into rotating mechanical energy. A gas turbine usually includes a compressor that pressurized air into a combustion chamber. The combustion products pass from the chamber through the nozzles to drive the turbine machinery. The rotating turbine drives the compressor and the external load, such as an electrical generator, or produces propulsive power such as an jet engine. A gas-turbine engine can be modeled using idealized thermodynamic cycles such as the Brayton cycle shown below.
Close the loop
adiabatic
reversible

## Slide 2
Fresh air is drawn into the compressor, where its pressure is raised by receiving energy from the rotating compressor blades. Although there is no heat transfer, the temperature is still increased because of the compression (adiabatic compression, isentropic compression). The high pressure air enters the combustion chamber and receives heat at constant pressure. The resulting high-temperature, high-pressure gases drive the turbine and eventually expand into the surrounding. Work output is delivered as turbine rotating mechanical energy. If we assume the exhaust gases expand to the same condition as the inlet air, then we can model the open gas-turbine processes as a closed thermodynamic cycle as described by the Brayton cycle.
In today’s exercise we are going to examine the adiabatic compression process using a simple experiment: A steel ball is dropped into a tube connected to an enclosed container. If the ball has the same diameter as the inner diameter of the tube, the air inside the container can not escaped and will be compressed due to the added weight of the ball. It can be shown that the compression process can be modeled as a simple dynamical system which relates the pressure change inside the container to the motion of the ball. (a) Derive an ordinary differential equation governing the position of the ball inside the tube x(t) as a function of time (t). (b) From the solution, identify that the process is indeed an adiabatic process. You will need to use the experimental procedures described in the following pages to complete this task. (c ) Estimate the temperature variation inside the container T(t) as a function of time, plot this function.

## Slide 3
x(t)
Po
Patm
W=mg
PatmA+mg=PoA
Po=Patm+(mg/A)
Po: pressure inside the container when the process reaches equilibrium (ball settles down)
x(t): position of the ball away from its equilibrium location
Because of the additional compression, the pressure inside the container will be increased by an amount dP and this will lead to unbalanced force (dF) and an acceleration of the ball (a) according to the Newton’s second law:
It can be assumed that this compression is following a polytropic process, that is the relationship between the pressure (P) and the volume (V) can be expressed by the following relation: PVn=constant, where n is a constant depending on the nature of the process. If the process is adabatic then n=k: specific heat ratio. Therefore, in order to identify that the process is indeed adiabatic, we have to determine n and compare n to the specific heat ratio of the air. If n is close to 1.4, we can assume that the process can be approximated as an adiabatic process.

## Slide 4
Based on the previous discussion, derive an ordinary differential equation governing the motion of the ball, that is to find x as a function of time. Hint: the equation should have the following form:
From the equation it is easily recognized that it is an equation for a simple harmonic oscillator with a circular frequency . The circular frequency is a function of Po(pressure inside the container after equilibrium), A(cross-sectional area of the tube), m(mass of the ball) and Vo(total volume of the trapped air), and n(the exponent defined in the polytropic process). From the simple harmonic analysis, we know that the oscillation period (T) is related to the circular frequency () as T=2/Therefore, the polytropic exponent n can be determined by measuring the oscillation period of the ball inside the tube. Hint: the volume change inside the container (dV) due to the movement of the ball can be related to the distance of the ball away from its equilibrium point (x), that is, dV=Ax. Hint: If derived correctly,
Use the following values for your calculation:
mass of the ball: m=0.01 (kg)
total volume of trapped air: Vo=0.008 (m3)
cross-sectional area of the tube: A= 0.00013 (m2)
Atmospheric pressure: Patm=101300 (Pa)

## Slide 5
1.51