## Slide 1
Superheat Rankine Cycle Example
Turbine
pump
condenser
1
2
3
4
Qout
Qin
Wout
Win
boiler
Consider the superheat Rankine power cycle as we analyzed before. But this time we are going to look at the system at a more practical sense. As before, the steam exits from the turbine will be 100% saturated vapor as shown. After condensing, saturated liquid enters the pump at a pressure of 0.1 MPa. However, both the turbine and the pump are operating at an isentropic efficiency of 80%. Determine (a) the rate of heat transfer into the boiler per unit mass, (b) the net power generation per unit mass. (c) the thermal efficiency,
T
s
1
2s
3
4s
4
2

## Slide 2: Discussion
Irreversibilities and losses are always associated with the operation of a real mechanical system. The existence of these unwanted effects is accompanied by an increase of entropy as required from the second law. (ex: 3 4s isentropic process, 3 4, entropy increases for a real process)
The efficiency of the turbine (t) will decrease as a result of these losses:
The isentropic expansion work (Wt)s = h3-h4s is the ideal process and Wt= h3-h4 is the actual work done in a real process
Similarly, the isentropic pump efficiency can be expressed as
Because of inefficiency, h2-h1 > (h2-h1)s it required more work to pump and compress the liquid.

## Slide 3: Solution
A-5

## Slide 4: Solution (cont.)
A-6