## Slide 1
A
B
0.7 m
0.3 m
0.2 m
1 m
water
water
Liquid X
Homework 1: Given: PA=10 kPa,
PB=9 kPa, (water)=1000 kg/m3,
determine the density of the fluid
X.
1
2
3
4
5

## Slide 2
Homework 2: Calculate the force acting on the underwater gate as shown below. The gate
is square-shaped with 2 m on each side.
5 m
y
2 m x 2m gate
p=p
p=p

## Slide 3
Homework 3: A solid cube made up of an unknown material X, with 1 m on each side, can
float in water with 0.5 m above the water surface. (a) Determine the density of the material X.
(b) If the cube is placed in a different fluid Y, it floats with 0.2 m above the liquid surface,
determine the density of the fluid Y.
0.5 m
1 m
X
0.2 m
X
water
Liquid Y

## Slide 4
Homework 4: Neglecting all losses, determine (a) the mass flow rate of the discharge at this
instant; (b) how time rate of decreasing of the oil level at this instant; © how long will it
take to drain the water. ((water)=1000 kg/m3, (oil)=900 kg/m3)
water
Oil
4 cm dia. Circular hole
1 m
1 m
Circular tank,
dia. 1 m

## Slide 5
Homework 5: A mercury U-tube is used to measure the pressure difference between sections
A and B. The specific gravity of mercury is 13.54. Determine the mercury height h inside
the U-tube if the velocity at A is 8 m/s. Neglect viscous effects.
h
ho
1 m
A
B
2 cm dia.
4 cm dia.
Water flow
x
z

## Slide 6
Homework 6: Water jet flowing out of the bottom of a tank filled to an unknown level, h.
The trajectory of the water jet at this instant is given as shown below. Determine the
water level h at this instant. (Neglect all losses)
2 m
1 m
h