## Slide 1
If the retaining wall shown in Figure 1 is flexible, what will be the lateral force per unit length of the wall (Magnitude, point of action and direction)?
FAMU – FSU College of Engineering
Department of Civil and Environmental Engineering
CEG 4801
Geotechnical Design
If the retaining wall shown in Figure 1 is restrained from movement, what will be the lateral force per unit length of the wall (Magnitude, point of action and direction)?
Figure 1

## Slide 2
Referring to Figure 1, the lateral force per unit length of the wall assuming passive condition (Magnitude, point of action and direction)?
Solve problem 1 with an inclined backfill a = 10o
Refer to the retaining wall shown in Figure 1. Assume that the groundwater level rises to 5 ft below the top of the retaining wall. Given: g = 100 lb/ft3, gsat = 122.4 lb/ft3, f = 30o, and c = 0.
a
W.T.
5 ft
gsat = 122.4 pcf

## Slide 3
If the retaining wall shown in Figure 1 is flexible, what will be the lateral force per unit length of the wall (Magnitude, point of action and direction)?
Figure 1
q=200 psf
The backfill retained by a flexible retaining wall shown in Figure 2 consists of two sand layers, compacted at different densities. The properties of the sand are shown in the figure. Determine the magnitude and location of the lateral load on the wall.
Figure 2

## Slide 4
A retaining wall, having a soft, saturated clay backfill, is shown in Figure 3. For undrained
condition (f = 0) of the backfill, determine:
a. The maximum depth of the tensile crack
b. Pa (Magnitude and point of action)
Figure 3
A retaining wall is shown in Figure 4. Given: height of the wall is equal to 16 ft and
unit weight of the sand backfill is 114 lb/ft3; calculate the active force, Pa (Magnitude, point of action and direction), on the wall using Coulomb’s equation for d = 20o