## Slide 1
1) Find the total active earth pressure per foot of the wall for the following situation. Use Rankine’s method
H = 20 ft
b = 10o
1= 120 lb/ft3 c1=0
1= 35o
85o
H* = 20.31 ft
Homework 4 - Geotechnical Engineering

## Slide 2
2) For the following situation, considering the angle of wall friction between backfill and wall  is 20o, find the active earth pressure per foot of wall by Coulomb theory.
H = 20 ft
b = 10o
1= 120 lb/ft3 c1=0
1= 35o
85o
H* = 20.31 ft
Homework 4 - Geotechnical Engineering

## Slide 3
3‐ Given
A smooth vertical wall is 20 high and retains a cohesionless soil with  = 120 lb/ft3, and  = 28o .
The top of the soil is horizontal and level with the top of the wall.
The soil surface carries a uniformly distributed load of 1000
Required:
Total active earth pressure on the wall per linear foot of wall.
Point of action of the total active earth pressure by Rankine theory.


H
Smooth Surface
 = 0
Vertical Surface
 = 0
q = 1000 lb/ft
Homework 4 - Geotechnical Engineering

## Slide 4
4) For the cantilever retaining wall shown in the following figure, let the following data be given:
Wall dimensions: H = 18 ft, X1=18 in, X2=30 in., X3=4 ft, X4, 6ft, X5=2.75 ft, =10o, D = 4 ft Soil properties: 1 = 117 lb/ft3, 1=34o, 2=110 lb/ft3, 2 =18o, c2= 800 lb/ft2
Calculate the factor of safety with respect to
1- Sliding Failure
2- Overturning Failure
3- Foundation Failure
a = 10o
X1
H
D
X3
X2
X4
1= 117pcf
c1=0
1=
2= 110 pcf
c2= 800 psf
X5
2=18o
Homework 4 - Geotechnical Engineering
gconcrete = 150 pcf