## Slide 1
Home Work Set Number 7 Geotechnical Engineering
Slope Stability Analysis
Homework # 4
Spring 2023
Problem 1
The following figure shows a 15-ft cut through two soil strata. The lower is a highly impermeable cohesive soil. Shearing strength data between the two strata are as follows:
Cohesion=150 psf
Angle of internal friction= 25o
Unit weight of the upper layer= 105 pcf
Find: Driving force and resisting force and factor of safety against sliding
1
1
15’
10’
5’
45o
30o
= 105 pcf
f =25o
C= 150 psf
L =??
Failure Surface

## Slide 2
Problem 1)
Problem 2)
Problem 2
Problem 3

## Slide 3
Problem 4
Refer to Figure 4, Given: b = 20o, g = 18 kN/m3, f = 25o, and c' = 14 kN/m2. Find the height, H, that will have a factor of safety, Fs of 2.5 against sliding along the soil-rock interface.
Figure 4
Problem 5
For the infinite slope shown in Figure 5, find the factor of safely against sliding along the plane AB, given that H = 20 ft. g = 110 pcf, f = 20o, and c' = 500 psf. Note that there is seepage through the soil and that the groundwater table coincides with the ground surface.
Figure 5

## Slide 4
Problem 6
Find the factor of safety for a 20 meter high 2H - l V slope shown in the following figure using ordinary method of slices. Each slice has a width of 5 meters.
g = 16 kN/m3
c = 20 kPa
f = 20O
R = 38.1 m

## Slide 5
Example of how to determine W1 and W5.
1
2
3
4
5
6
7
8
9
10
W1
b1
h1
W1= 0.5x b1 x h1 x g
a1 =
Tangent
a1
Tangent
h5
b5
W5= b5 x h5 x g
a5 =
a5
H=20m
1m
2m
2x20 = 40 m
This is not to scale
= 38.1 m

## Slide 6
H=20m
2x20 = 40 m
1m
2m
Center
Radius