## Slide 1
Stresses in Soil
By
Kamal Tawfiq, Ph.D., P.E.
Spring 2017
Geostatic Stresses
Superimposed Stresses
Lateral Earth Pressure

## Slide 2
Stresses in Soil
Geostatic Stresses
Superimposed Stresses
Lateral Earth Pressure
Geostatic Stress
Added Stress
Due to the
weight of the
house
Total Stress
Effective Stress
Pore Water Pressure

## Slide 3
Geostatic Stresses
Total Stress
Effective Stress
Pore Water Pressure
Total Stress= Effective Stress+ Pore Water Pressure
stotal = seff + u
Bossinisque Equations
Point Load
Line Load
Strip Load
Triangular Load
Circular Load
Rectangular Load
Added Stresses (Point, line, strip, triangular, circular, rectangular)
Stress Distribution in Soils
Influence Charts
Newmark Charts
Stress Bulbs
Westergaard’s Method
(For Pavement)
Approximate Method
1:2 Method
A
By: Kamal Tawfiq, Ph.D., P.E
Added
Stress
Geostatic
Stress
sy
sx
txy

## Slide 10
σz
σx
σz
σx
τxy
σ2
σ1
σ1
σ2
X/R
Z/R
0.95
1
2
3
4
1
2
3
0
0.90
0.80
0.70
0.30
0.50
0.40
0.10
0.20
0.15
qs
Δσ1/qs
0.60
σz
σx
σz
σx
τxy
Circular Load: (Major Principal Stress)/(Surface Stress)
σz = σ1
σz = σ1
σx = σ2
σx = σ2
θ
Δqs
Z
X
R
Stress Bulbs
Circular Load
9 ft
3 ft
A
qs
σz = σ1
σz = σ1
σx = σ2
σx = σ2

## Slide 11
Geostatic Stresses
&
Stress Distribution in Soils
Stresses from the house
Self-weight of the soil
Or
Geostatic Stress

## Slide 12
Point A
11 ft
15 ft
q = 800 lb/ft2
12 ft
Z = 10 ft
Vertical Stress
Find:
Vertical Stress at Point A
Newmark’s Charts

## Slide 13
Influence Value = 0.005
a
b
A
15’
11’
Z= 10’
12’
Steps to determine Vertical Stress Using Newmark’s Charts:
1- Select a scale to draw the shape shown above
2- The scale is
Z = length of line ab
3- Draw the shape using the selected scale
4- Place the shape on Newmark chart so that point A is at the center
5- Count the stress fields n
6- The stress at point A = n x q x 0.005
q = 800 psf
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x

## Slide 14
Influence Value = 0.005
a
b

## Slide 15
Lateral stresses due
to self-weight of soil

## Slide 16
Vertical and Horizontal Stress in Water
sv = d gwater
sh = d gwater = sv
d
Water Table
Hydrostatic Stress or Pressure
Isotropic Stress
By: Kamal Tawfiq, Ph.D., P.E.
.

## Slide 17
By: Kamal Tawfiq, Ph.D., P.E.
sv = d gwater
sh = d gwater = sv
d
Water Table
.
Vertical and Horizontal Stress in Water
Assume a massive wall retaining water. What is the pressure on this wall??
Is the wall stable???
Pw = H gwater
Water pressure on the wall

## Slide 18
Vertical and Horizontal Stress in Soil
sv = d gsoil
sh = (d gsoil ) Ko = sv Ko
d
Ground Surface
Geostatic Stress
Anisotropic Stress
By: Kamal Tawfiq, Ph.D., P.E.
.

## Slide 19
Vertical and Horizontal Stress in Soil
sv = d gsoil
sh = (d gsoil ) ?? = sv ??
d
Ground Surface
By: Kamal Tawfiq, Ph.D., P.E.
.
Soil Displacement = ??
Assume a vertical cut in sand soil. Is this cut safe????

## Slide 20
no movement
AT REST CONDITIONS
The soil remains undisturbed.
Structure is rigid, does not move and can be placed in the soil without allowing any lateral soil movement.
Lateral pressures existing in the soil before installations are still prevailing
D= 0

## Slide 21
Earth Pressure Behind Retaining Wall
Geotechnical Design
CEG 4801
Spring 2014
By: Dr. Kamal Tawfiq
Passive
Active
Active Wedge
Passive Wedge

## Slide 22
Vertical and Horizontal Stress in Soil
sv = d gsoil
sh = (d gsoil ) Ka = sv Ka
d
By: Kamal Tawfiq, Ph.D., P.E.
.
Active Wedge. Exerting pressure on the wall
Stability of a retaining wall.
Deformation

## Slide 23


failure envelope
v’
sh is decreasing until failure
active earth pressure
Rankine’s Active Earth Pressure in f - Soil
f’
h’
f’
v’
=
tan2 (45 – f/2)
1 - sinf
1 + sinf
=
f
Coefficient of active earth pressure
D
q = 45 0+ f/2
f
Pa
F
W
g
f
v’
f’
D
At failure the active wedge will develop in the backfill
By: Kamal Tawfiq, Ph.D., P.E.
Ka = tan2 (45 – f/2)

## Slide 24
sh is increasing until failure
active earth pressure
Rankine’s Passive Earth Pressure in f - Soil
f’
v’
=
tan2 (45 + f/2)
1 + sinf
1 - sinf
=
Coefficient of passive earth pressure
D
q = 45 0- f/2
W
g
f
v’
f’
At failure the passive
wedge will develop in the backfill

f
failure envelope
v’
f’
h’
f
By: Kamal Tawfiq, Ph.D., P.E.
Kp = tan2 (45 + f/2)
Pa
D
passive earth pressure
q = 45 0- f/2

## Slide 25
Rankine’s Active Earth Pressure in f - Soil
v’
f’
a = 0
b = 0
d = 0
1 - sinf
1 + sinf
=
Ka = tan2 (45 – f/2)
Active Wedge

## Slide 26
W.T.
gsoil
f
h1
h2
sh = gsoilh1 + (gsoil + gw)h2
sh = gsoilh1
+
G.S.
sw = gwh2

## Slide 27
By: Kamal Tawfiq, Ph.D., P.E.

## Slide 28
P1
P2
P3
h1
h2
gsoil
gsub
gsoil -gwater
=
1
2
3
=
110 pcf
=
6’
=
4’
Water Table
sh2
sh3
sh1
Point | Depth | Unit Weight (pcf) | Vertical Stress = sv (psf) | Lateral Stress = sh (Psf)
1 | 0 | 110 | 0 | 0
2 | 6 | 110 | 110 x 6 = 660 | 660x0.33 = 217.8
3 | 10 | 110 - 62.4= 47.6 | [(110x6)+(110-62.4)(4)] = 850.4 | 283.18
P1 | = 0.5 x sh2 x 6 = 0.5 x 217.8 x 6 = 653.4 lb/ft
P2 | = sh2 x 4 = 217.8 x 4 = 871.2 lb/ft
P3 | = 0.5 x (sh3 - sh2) x 4 = 0.5 x 65.38 x 4 = 130.76 lb/ft
f = 30o
Ka = 0.33

## Slide 29
By: Kamal Tawfiq, Ph.D., P.E.
Effect of Surcharge Load on Earth Pressure
=
+
+
+
+
q ka
q ka
gHka
q ka
q
Qka + gHka

## Slide 30
By: Kamal Tawfiq, Ph.D., P.E.

## Slide 31


failure envelope
v’
sh is decreasing until failure
active earth pressure
Rankine’s Active Earth Pressure
Case 2: c- f Soil
f’
h’
f’
v’
=
tan2 (45 – f/2) – 2 c tan (45 – f/2)
1 - sinf
1 + sinf
=
f
Coefficient of active earth pressure
v’
f’
D
By: Kamal Tawfiq, Ph.D., P.E.
where Ka = tan2 (45 – f/2)
c
f’
v’
=
Ka – 2 c Ka

-
-2c Ka
-2c Ka
+
+
=
-
+
-2c Ka
g H Ka
g H Ka
-2c Ka
g =
f =
c=
√
√
√

## Slide 32
sh is increasing until failure
active earth pressure
Rankine’s Passive Earth Pressure in c- f Soil

f
failure envelope
v’
f’
h’
f
By: Kamal Tawfiq, Ph.D., P.E.
passive earth pressure
q = 45 0- f/2
v’
f’
D
+
+2c Kp
+
+
=
+2c Kp
g H Kp
+2c Kp
g H Ka
+2c Kp
g =
f =
c=
√
√
√
+
+
f’
v’
=
1 + sinf
1 - sinf
=
Coefficient of passive earth pressure
where Kp = tan2 (45 + f/2)
f’
v’
=
Kp + 2 c Kp

tan2 (45 + f/2) + 2 c tan (45 + f/2)

## Slide 33
a
H
Fig.1
a
Pa = 0.5 g H2 Ka
Rankine’s Active Earth Pressure in f - Soil
Case 1: For Inclined Surface
Ka = cosa
Cosa – (cos2a – cos2 f)1/2
Cosa + (cos2a – cos2 f)1/2

## Slide 34
Coulomb Earth Pressure
Method (1776)

## Slide 35
By: Kamal Tawfiq, Ph.D., P.E.
This active wedge will slide along the failure surface and will exert pressure on the wall. Also, the sliding wedge will push the wall away from the backfill.
Wall Displacement = D
W
Soil-Soil Friction
Soil-Wall Friction
Forces acting on the wall.
Failure surface
Pressure from the sliding wedge
Coulomb Earth Pressure Method (1776)

## Slide 36
By: Kamal Tawfiq, Ph.D., P.E.
Active Wedge. Exerting pressure on the wall
Wall Displacement = D
W
Pa
d
f
F
Normal
Shear
Normal
Shear
q
d
Pa
g
f
b
a
Forces acting on an inclined wall.
Coulomb Earth Pressure Method (1776)
H/3
H

## Slide 37
By: Kamal Tawfiq, Ph.D., P.E.
Active Wedge. Exerting pressure on the wall
Wall Displacement = D
W
Pa
d
f
F
Normal
Shear
Normal
Shear
Forces acting on the wall.
Coulomb Earth Pressure Method (1776)

## Slide 38
a
q
d
Pa
g
f
f
R
W
Coulomb Earth Pressure Method (1776)
R
Pa
W
By: Kamal Tawfiq, Ph.D., P.E.
b - f
90 - q - d
90 + q + d - b +f
b-a
b
H
W = weight of the soil wedge
R = resultant of the shear and normal forces on the failure surface BC
Pa = the active force per unit length of the wall. The direction of Pa is inclined at an angle d to the normal drawn and the face of the wall that supports the soil
D = the angle of friction between the soil and the wall
The force triangle for the wedge is shown in the Figure 2. From the sine law, the forces can be set as follows:
Fig.1
Fig.2
W
=
Sin (90 + q + d - b +f)
Sin (b - f)
Pa
Substitute for W, Eq. 2 can be written as
=
cos2 q sin( b - a) sin (90 + q - d - b + f)
cos (b - f) cos (f - a) sin (b - f)
Pa
0.5 g H2 [
]
To determine the critical value for b for maximum Pa
(dPa/db) = 0
W
=
Sin (90 + q + d - b +f)
Sin (b - f)
Pa
(1)
(2)
(2)
cos2 q cos( d - q)
cos2 (f- q)
sin( d + f) sin (f - a)
cos ( d + q) cos (q - a)
1+
[
]
2
Ka =
Pa = ½ Ka g H2
Where Ka = Coulomb’s active earth pressure coefficient

## Slide 39
g
f
Coulomb’s Earth Pressure
By: Kamal Tawfiq, Ph.D., P.E.
H
cos2 q cos( d - q)
cos2 (f- q)
sin( d + f) sin (f - a)
cos ( d + q) cos (q - a)
1+
[
]
2
Ka =
Pa = ½ Ka g H2
= √
= 0
= 0
a = 0
1 - sinf
1 + sinf
=
Ka
Smooth Surface
a = 0
d = 0
Vertical
Surface
q = 0
Under the given wall and backfill conditions, Ka of Coulomb’s active earth pressure
becomes equivalent to Ka of Rankine’s

## Slide 40
Active Earth Pressure in f - Soil
D
q = 45 0+ f/2
f
Pa
F
W
g
f
D
sh = sv ka
sh = sv ka
Pa=g H ka
1/2
By: Kamal Tawfiq, Ph.D., P.E.
Given:
Vertical retaining wall (flexible)
Wall height (H) = 12 ft
Backfill unit weight (g) = 115 pcf
Angle of soil friction (f) = 30o
Assume wall to be smooth
Find:
Lateral force Pa acting on the wall
Solution:
Example -1
1 - sinf
1 + sinf
=
Ka
Pa = g H0.5 ka
ya = 12/3
Pa = 115 x 122 x 0.5

## Slide 41
+
+
Psoil
Pwater
Pwater
Psoil
By: Kamal Tawfiq, Ph.D., P.E.

## Slide 42
By: Kamal Tawfiq, Ph.D., P.E.
=
+
+
+
+
q ka
q ka
gHka
q ka
Pavement
q

## Slide 43
By: Kamal Tawfiq, Ph.D., P.E.
=
+
+
-
+
-
-2c√ka
-2c√ka
=
+
+
-
+
gHka

## Slide 44
Earth Pre
ssure
&
Retaining W
all Design
By
Kamal Tawfiq,
Ph.D., P.E.

## Slide 45
Types of Earth Retaining Walls
I- Permanent Walls
1- Gravity Wall
2- Semi-gravity wall
3- Cantilever wall
4- Counterfort wall
5-
Sheet pile wall & Braced cuts
I- Permanent Walls
II- Temporary Walls ......
By: Kamal Tawfiq
1
2
3
4
5

## Slide 46
Design of Retaining Wall
1- External Stability
2- Internal Stability
1. External Stability
1- Sliding
2- Overturning
3- Settlement
4- Overall Failure
1
2
3
4
By Kamal Tawfiq, Ph.D., P.E

## Slide 47
Common Proportions of Cantilever Wall
H
Df
B = 0.4 to 0.7 H
Thickness = H/12 to H/10
Minimum batter = 1/50
12 in Preferable minimum
Toe Slab
H/10 to H/8
Thickness
H/12 to H/10
Heel of Slab
Base of footing
Vertical
Stem

## Slide 48
B/3
>1m
H/12 to H/10
H/12 to H/8
B =
0.4 H to 0.7 H
0.25 m to 0.4 m
H
Cantilever Retaining Wall
1
48
D/2 to D
0.3 m to H/12
H
B =
0.5 H to 0.7 H
D = H/8 to H/6
>1m
Gravity Retaining Wall
Approximate Dimensions
Kamal Tawfiq, 2011

## Slide 49
Counterfort Retaining Wall

## Slide 50
a
q
g
f
Coulomb Earth Pressure Method
By: Kamal Tawfiq, Ph.D., P.E.
H
Fig.1
cos2 q cos( d - q)
cos2 (f- q)
sin( d + f) sin (f - a)
cos ( d + q) cos (q - a)
1+
[
]
2
Ka =
Pa = ½ Ka g H2
Where Ka = Coulomb’s active earth pressure coefficient
d
Pa = 0.5 g H2 Ka
d
Angle of Friction between the wall and the soil

## Slide 51
g
f
Rankine’s Earth Pressure
By: Kamal Tawfiq, Ph.D., P.E.
H
Pa = ½ Ka g H2
= √
= 0
= 0
a = 0
1 - sinf
1 + sinf
=
Ka
Smooth Surface
a = 0
d = 0
Vertical
Surface
q = 0
Pa=g H ka
1/2

## Slide 52
a
H
Fig.1
a
Pa = 0.5 g H2 Ka
Rankine’s Active Earth Pressure in f - Soil
Case 1: For Inclined Surface
Ka = cosa
Cosa – (cos2a – cos2 f)1/2
Cosa + (cos2a – cos2 f)1/2

## Slide 53
Active Earth Pressure in f - Soil
D
sh = sv ka
sh = sv ka
Pa=g H ka
1/2
Given:
Vertical retaining wall (flexible)
Wall height (H) = 12 ft
Backfill unit weight (g) = 115 pcf
Angle of soil friction (f) = 30o
Assume wall to be smooth
Find:
Lateral force Pa acting on the wall
Solution:
Example -1
1 - sinf
1 + sinf
=
Ka
Pa = g H0.5 ka
ya = 12/3
Pa = 115 x 122 x 0.5
Pa=g H ka
1/2
Pp= g D kp
1/2
H
D
W

## Slide 54
I. External Stability
1- Sliding
Friction = (∑W) tan d
Factor of Safety Against Sliding =
Resisting Force
Driving Force
FR
=
FD
FD = Pa
FR = Pp + Friction
By: Kamal Tawfiq

## Slide 55
I. External Stability
2- Overturning
Driving Moment
MD
Resisting Moment
MR
Factor of Safety Against Sliding =
Resisting Moment
Driving Moment
MR
=
MD
MD = Pa . ya
MR = Pp.yp + W1 a1 + W2 a2 +W3 a3 +W4 a4
Moment About o
By: Kamal Tawfiq
a1
a2
a4
a3
ya
yp

## Slide 56
Extent of the Passive
Pressure
Friction Surface of along the Base
Using Key at the Base to Improve Sliding Resistance
Key

## Slide 58
qmax
qmin
I. External Stability
3- Bearing Capacity Failure

## Slide 59
qmax
qmin
R
SV
SH
3- Check for Bearing Capacity Failure
e
X
V = sum of all vertical loads
SH = sum of all horizontal loads
R = (SV)2 + (SH)2
Mnet = SMR – SMo
X =
Mnet
SV
e = - X
B
2
q =
SV
A
Mnet y
I
+
-
q
SV
B
6e
B
+
-
1
(
)
max
min
=
B
qmax
qmax
qmax
qmin = 0
qmin = +
qmin = -
+
+
+
-
Factor of Safety Against Bearing Capacity Failure =
qall
qmax
√
√
X

## Slide 60
Retaining Wall Design
Internal Stability
By
Kamal Tawfiq, Ph.D., P.E.

## Slide 64
insulate the footing externally
Masonry wall
Coarse soil
In situ soil
French drain
Geofabric
Geofabric
Plain
concrete
or
4” gravel

## Slide 65
SOLVED EXAMPLES

## Slide 72
Solution
From the figure,
H' = H1 + H2 + T1 = 8 tan 10° + 19.5 + 2 = 22.91 ft
The Rankine active force per unit length of wall =
Example 1
Given
The cross section of a cantilever retaining wall is shown in Figure 1. Calculate the factors of safety with respect to overturning, sliding, and bearing capacity.
10o
H1 = 1.41 ft
q = 120 lb/ft
1 ft
g1 = 115 lb/ft3
f1 = 30o
c1 = 0
H2 = 19.5 ft
Pa2
10o
Ph2
Pv1
2
3
T1 = 2 ft
g2 = 112 lb/ft3
f2 = 20o
c2 = 800 lb/ft2
2.25 ft
2.25 ft
8 ft
4.5 ft
4
6
5
W2
W3
W1
W4
W6
W5
a4
a6
a5
a2
a3
a1
O
av
ya
Pv
Pa1
10o
10o
Ph1
Pv2