## Slide 1: Mechanically Stabilized Earth (MSE) Wall Project
Geotechnical Design
CEG 4801
Kamal Tawfiq, Ph.D., P.E.

## Slide 2
Choices for Bridge Abutments
1
2
3
4

## Slide 3
Earth Pressure Behind Retaining Wall
Geotechnical Design
CEG 4801
Fall 2010
By: Dr. Kamal Tawfiq
Passive
Active

## Slide 4
French architect and engineer Henri Vidal in the early 1960s

## Slide 6
Mechanically Stabilized Earth (MSE) Walls
or Segmental Walls
H = 30 ft
f = 30o
g = 110 pcf

## Slide 7
Mechanically Stabilized Earth Wall (MSE Wall)

## Slide 9
Mechanically Stabilized Earth Wall (MSE Wall)

## Slide 10
Using Galvanized Steel

## Slide 11
Seattle-Tacoma International Airport, WA

## Slide 13
Kamal Tawfiq, Ph.D., P.E.

## Slide 32
Mechanically Stabilized Earth Wall (MSE Wall)

## Slide 41
Using Geogrids

## Slide 44
Tom Landry Highway, TX

## Slide 45
Stability of MSE Walls

## Slide 46
Stability of MSE Walls

## Slide 47
Block Failure

## Slide 48
Mechanically Stabilized Earth Wall (MSE Wall)
Geotechnical Design
CEG 4801
Fall 2004
By: Dr. Kamal Tawfiq

## Slide 49
Mechanically Stabilized Earth Wall (MSE Wall)

## Slide 50
MSE Key Stone Wall

## Slide 51
MSE Key Stone Wall

## Slide 59
Geotextile Walls

## Slide 60
Gabion Walls
Gabion Retaining Wall Design

## Slide 61
Gabion Walls

## Slide 62
Gabion Walls
HESCO CONCERTAINER
Military Accommodation Roofing, Personnel & Material Bunker Sets

## Slide 63
Interior of Fort Sumter with gabions
Petersburg, Virginia. Fort Sedgwick. Gabions

## Slide 65
Rebel fortifications in front of Atlanta, Georgia, in 1863 or 1864

## Slide 66
Gabions with cannon, from a late 16th century illustration.

## Slide 67
MSE Wall
Analysis and Design

## Slide 68
A reinforced earth retaining wall is to be 30 ft high. The properties of the backfill material are g = 110 lb/ft3 and f = 30o. Galvanized steel ties are to be used for the construction of the wall. Design the Reinforcements with FS(B) = 3, FS(p) = 3, fy = 29,000psi and ftie= 20o. The properties of the in-situ soil below the retaining wall are g = 120 lb/ft3, f = 30o, and c = 150 lb/ft2. Design the panels and the ties of the wall.

## Slide 70
A reinforced earth retaining wall is to be 30 ft high. The properties of the backfill material are g = 110 lb/ft3 and f = 30o. Galvanized steel ties are to be used for the construction of the wall. Design the Reinforcements with FS(B) = 3, FS(p) = 3, fy = 29,000psi and ftie= 20o. The properties of the in-situ soil below the retaining wall are g = 120 lb/ft3, f = 30o, and c = 150 lb/ft2. Design the panels and the ties of the wall.

## Slide 71: MSE Wall Project
Geotechnical Design
CEG 4801
Fall 2016
Kamal Tawfiq, Ph.D., P.E.

## Slide 73
A reinforced earth retaining wall is to be 30 ft high. The properties of the backfill material are g = 110 lb/ft3 and f = 30o. Galvanized steel ties are to be used for the construction of the wall. Design the Reinforcements with FS(B) = 3, FS(p) = 3, fy = 29,000psi and ftie= 20o. The properties of the in-situ soil below the retaining wall are g = 120 lb/ft3, f = 30o, and c = 150 lb/ft2. Design the panels and the ties of the wall.
Extend the tie beyond the active wedge to provide enough support against earth pressure of the panel
Kamal Tawfiq, Ph.D., P.E.
Design Concept

## Slide 74
Yield Strength of Steel
t = thickness of tie
Friction angle between steel and soil (given)

## Slide 76
45 + f/2
LR1 = Rankine Length
Le5
LR5
Panel 1
Panel 2
Panel 3
Panel 4
Panel 5
Panel 6
Panel 7
LR1 =
H
Tie 1
45 - f/2
(H- 0.5 Sv) tan (45-f/2)
0.5Sv
W = width of the tie = 4”
Le1=
2.5(sa.Sv.SH)
2 w sv tanf
L1 = LR1 + Le1
Kamal Tawfiq, Ph.D., P.E.
H = 30 ft
f = 30o
g = 110 pcf
Le1 = Effective Length

## Slide 77
LR1 =
H
(H- 0.5 Sv) tan (45 - f/2)
Le1=
2.5(sa.Sv.SH)
2 w sv tanf
L1 = LR1 + Le1
sa4
sa3
sa3
sa4
sa2
sa5
sa6
sa7
sa8
Sv
SH
sv3
sv2
sv1
(sa3 + sa4)/2
sa1
(sa1 + sa2)/2
Kamal Tawfiq, Ph.D., P.E.
Tie width
Tie

## Slide 78
Example:
A reinforced earth retaining wall is to be 30 ft high. The properties of the backfill material are γ = 110 lb/ft3 and φ = 30ο. Galvanized steel ties are to be used for the construction of the wall. Design the Reinforcements with FS(B)= 3, FS(p) = 3, fy= 29,000 psi and φtie= 20ο. The properties of the in-situ soil below the retaining wall are γ = 120 lb/ft3, φ = 30ο, and c = 150 lb/ft2. Design the panels and the ties of the wall.
H
sa3
sa4
sa2
sa5
sa6
sa7
sa8
sv3
sv2
sv1
sa1
g = 110 lb/ft3
f = 30o
LR1 = Rankine Length
Le1 = Effective Length
5’
45 + f/2
sa4
sa3
Sv = 5’
SH = 5’
LR1= 47.6 ft
Le1= 30 ft

## Slide 81
Kamal Tawfiq, Ph.D., P.E.

## Slide 82
Kamal Tawfiq, Ph.D., P.E.

## Slide 83
Kamal Tawfiq, Ph.D., P.E.

## Slide 84
Kamal Tawfiq, Ph.D., P.E.

## Slide 85
H = 30 ft
f = 30o
g = 110 pcf

## Slide 86
Mechanical Stabilized Earth (MSE).
Abutments and Retaining Structures

## Slide 87
MSE Walls
MSE Wall with Horizontal Backslope and Traffic Surcharge
The loading and earth pressure diagram for an MSE wall shall be developed in accordance
with LRFD [11.11.2]
Figure 14.4-2 shows a procedure to estimate the earth pressure. The active earth
pressure for horizontal backslope is computed using a simplified version of Coulomb theory
tan2 (45 / 2)
K a = −φ f
Where:
Ka = Coefficient of active earth pressure
φf = Angle of internal friction of retained earth
MSE Walls Earth Pressure for Horizontal Backslope with Traffic Surcharge
LRFD Figure 11.10.5.2-1

## Slide 90
MSE Wall with Sloping Surcharge
The active earth pressure coefficient Ka is computed using Coulomb’s equation. The force on
the rear of the reinforced soil mass (Ft) and the resulting horizontal (Fh) and vertical (Fv)
forces are determined from the following equations:
FT = 1/2 γfh2Kaf
Fh = Ft cos β
Fv = Ft sin β
Where:
γf = Unit weight of retained fill material
β = Slope angle of backfill behind wall
δ = Angle of friction between retained backfill and reinforced backfill
h = See Figure 14.4-3
Kaf = Use Coulomb’s equation

## Slide 92
Variation of the Coefficient of Lateral Stress Ratio with Depth
(Source AASHTO LRFD Figure 11.10.6.2.1-3)

## Slide 95
Modular Block Gravity Wall with Sloping Surcharge
When designing a “Modular Block Gravity Wall” without setback and with level backfill, the
active earth pressure coefficient may be determined using Rankine theory from the following
formula.
tan2 (45 / 2)
When designing a "Modular Block Gravity Wall" with setback, the active earth pressure
coefficient Ka shall be determined from the following Coulomb formula. The interface friction
angle between the blocks and soil behind the blocks is assumed to be zero.
No live load traffic and live load surcharge shall be allowed on modular block gravity walls
although they are designed for a minimum live load of 100psf. The density of the blocks is
assumed to be 135 pcf and the drainage aggregate inside or between the blocks 120 pcf.
The forces acting on a modular block gravity wall are shown in Figure 14.4-5.

## Slide 115
F* = COEFFICIENT OF FRICTION