## Slide 1
Shallow Foundations
By
Kamal Tawfiq, Ph.D., P.E., F.ASCE

## Slide 2
3- Foundation Design
Differential Settlement

## Slide 5
Structural Foundations are grouped into two main groups.
1- Shallow Foundation
  Spread Footings
  Continuous Footings
  Combined Footings
  Mat Foundation
2- Deep Foundation
  Driven Piles
  Drilled Shaft
  Auger Cat Piles
3- Compensated or floating foundations

## Slide 9
Shallow Foundation
  Spread Footings
  Continuous Footings
  Spread Footings
  Spread Footings

## Slide 10
  Spread Footings
Combined Footings
Combined Footings

## Slide 11
Combined Footings
  Spread Footings

## Slide 12
Mat Foundation

## Slide 13
Mat Foundation

## Slide 14
Deep Foundation
Driven Piles

## Slide 15
Drilled Shafts

## Slide 16
Auger Cast Pile

## Slide 17
Vibro Piers

## Slide 18
I- Bearing Capacity
II- Settlement
Analysis and Design of Shallow Foundation
I- ULTIMATE BEARING CAPACITY THEORIES:
TERZAGHI’S BEARING CAPACITY THEORY
GENERAL BEARING CAPACITY EQUATION

## Slide 19
q = gDf
45o+f/2
45 - f/2
45 - f/2
qult
qult
B
Qdesign
I- Bearing Capacity
TERZAGHI’S BEARING CAPACITY THEORY
Terzaghi's Equation (1943)
Utilizing Prandtl's theory, Buisman (1940) expressed the maximum bearing capacity of soils by superimposing the contribution of cohesion, overburden pressure, and density of the soil, His expression is commonly referred to as Terzaghi's equation. Presumably, it was associated with Terzaghi's in the English speaking countries following the publication of his book (Theoretical Soil Mechanics) in 1943.
- Based on Prandtl's theory of plastic failure, Terzaghi presented a modified system as illustrated below.

## Slide 20
Question:
Name the three zones under the shallow foundation shown in the figure below.
q = gDf
qult
qult
B
Qdesign
FAMU-FSU College of Engineering
Department of Civil and Environmental Engineering
Spring 2019
Quiz # 6
Name:_____________
ID:_____________
1
2
2
3
3
1:_______
2:_________
3:__________

## Slide 21
qu = qc + qq + qg

## Slide 22
Laboratory Testing on Bearing capacity failures of foundations
General shear foundation failure

## Slide 23
Ultimate Bearing Capacity
qu = qc + qq + qg

## Slide 24
1- TERZAGHI’S BEARING CAPACITY THEORY

## Slide 26
1
2
3
4
2
4

## Slide 27
Factors
Factors
Factors

## Slide 28
2- GENERAL BEARING CAPACITY EQUATION

## Slide 32
1- The following bearing capacity equation was used by both Terzaghi and Meyerhof. Describe the three terms in the equation.
qult = cNc + qNq + 0.5 gBNg
ID:_____________
Name:_____________
FAMU-FSU College of Engineering
Department of Civil and Environmental Engineering
Geotechnical Design CEG 4801
Spring 2019
Quiz 7
2- The above equation for bearing capacity of foundation was first developed Terzaghi. Later on, Meyerhof and others improved the equation by adding what factors
qult = cNc + qNq + 0.5 gBNg
lcs
lcd
lci
lqs
lqd
lqi
lgs
lgd
lgi
lcs
lqs
lgs
lcd
lqd
lgd
lci
lqi
lgi
_____________
_____________
_____________
5 min Quiz

## Slide 33
B
Df
1
2
Terzaghi’s bearing capacity equation was based on his assumptions of the plastic zones developed under foundation. On the other hand, the general bearing capacity equation was also developed based on assumptions made by Meyerhof for the plastic zones under foundations.
Indicate od the given figure which of the assumptions are those for Terzaghi or Meyerhof.
1
2