## Slide 1
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
G.S.
gsand = 96 pcf
gclay = 110 pcf
wc = 0.3
3 ft
4 ft
16 ft
Po
Sand
Clay
Po
Soil sample was obtained from the clay layer
Conduct consolidation test [9 load increments ]
Plot e vs. log (p) (Figure 2)
Determine Compression Index (Cc ) & Swelling Index (Cs)
Example:
Figure 2
Figure 1
Soil Sample
Cc
Cs
Dp
Dp7
Dp
Dp1
Dp9
In the lab and after removing
the soil sample from the ground,
the stresses on the soil sample = 0
In the lab the stresses are
added to the soil sample
Dp1
Dp9
5. Determine Po = 3.(96) + 4.(96-62.4) + 8.(110-62.4) = 803.2 lb/ft2
Stress
Increments
eo = 0.795
Dp2
In the ground, the sample was subjected to geostatic stresses.
In the lab and before the consolidation test the stresses on the sample = 0.
During testing, the geostatic stress is gradually recovered
Cc = 0.72
Cs = 0.1

## Slide 2
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
G.S.
gsand = 96 pcf
gclay = 110 pcf
wc = 0.3
3 ft
4 ft
16 ft
Po
Sand
Clay
X
X
Po = Pc
6. Using Casagrande’s Method to determine Pc
Pc = 800 lb/ft2
Overconsolidation Ratio
OCR = = 1
The soil is
Normally Consolidated
N.C. soil
Example:
Dp1
Pc
Po
1
2
3
4
5
6
Point of
maximum curvature
Tangent to point 1
Tangent to point 1
7

## Slide 3
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
X
X
Po = Pc
1
2 Horizontal line
3
4 divide the angle between 2 & 3
Extend the straight line
6 Intersection of 4 & 5
Point of
maximum curvature
Tangent to point 1
Overconsolidation Ratio OCR = = 1
The soil is Normally Consolidated (N.C.) soil
Pc
Po
7
1
Normally Consolidated Soil
Casagrande’s Method to Determine Preconsolidation Pressure (Pc)

## Slide 4
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
X
X
Pc
1
2 Horizontal line
3
4 divide the angle between 2 & 3
5 Extend the stright line
6 Intersection of 4 & 5
Point of
maximum curvature
Tangent to point 1
Overconsolidation Ratio OCR = > 1
The soil is oversonsolidated (O.C.) soil
Pc
Po
7
Po
2
Overconsolidated Soil
Casagrande’s Method to Determine Pc

## Slide 5
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Po
Sand
Clay
Po
A 150’ x 100’ building will be constructed at the site.
The vertical stress due to the addition of the building
qdesign =1000 lb/ft2
The weight of the building Qdesign will be transferred
to the mid height of the clay layer
Qdesign = 15,000,000 lb
The added stress at 15’ from
the ground surface is
Dp =
Example:
Dp1
Building
qdesign
Po
DP1
G.S.
(150+15) x (100+15)
15,000,000 lb
DP = 790.51 lb/ft2
DP + Po =
790.51 + 803 = 1593.51 lb/ft2

## Slide 6
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Po
Sand
Clay
Po
Example:
Dp1
Building
qdesign
Po
DP1
G.S.
Consolidation Settlement
DH = log ( )
Cc H
1 + eO
Po + DP
Po
Po + DP
DP1
DP + Po = 790.51 + 803 = 1593.51 lb/ft2
DH = log ( )
0.72 x 16
1 + 0.795
1593.51
803
DH = 1.9 ft

## Slide 7
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Po
Sand
Clay
Po
Dp1
qdesign
Po
G.S.
Po + DP
DP1
When the building was removed, the soil has become
an overconsolidated clay.
The rebound has taken place through
swelling from pint 1 to point 2
2
1
Demolished

## Slide 8
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Po
Sand
Clay
Po
Dp1
qdesign
Po
G.S.
Po + DP
DP2
New Building
CS
CC
DH = log ( ) +
CS H
1 + eO
PC
Po
C C H
1 + eO
PC
Po + DP
log ( )
Scenario #1
The soil now is overconsolidated Soil:
The new building is heavier in weight
Pc
Constructing a new building
DP2
DP1
eo = 0.61
Assume Po + Dp2 = 2100 psf
DH =
0.1 x 16
1 + 0.61
1593.51
803
log
( )
+
0.72 x 16
1 + 0.61
1593.51
log
( )
2100
=

## Slide 9
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Po
Sand
Clay
Po
Scenario # 2
The soil now is overconsolidated Soil:
The new building is lighter in weight
Dp1
qdesign
Po
G.S.
DH =
CS H
1 + eO
Po + DP
New Building
P0
Po + DP
log ( )
CS
DP2
Constructing a new building
DP2
DP1
eo = 0.61
Assume Po + Dp2 = 1600 psf
DH =
0.1 x 16
1 + 0.61
1600
1593.51
log
( )
=

## Slide 10
Chart: 
| 1 | 1
 | 1000 | 1000
Example of Semi-log Scale