## Slide 1
Soil Settlement
By
Kamal Tawfiq, Ph.D., P.E., F.ASCE
Fall 2010

## Slide 2
Soil Settlement:
Total Soil Settlement = Elastic Settlement + Consolidation Settlement
Stotal = Se + Sc
Load Type (Rigid; Flexible)
Elastic Settlement or Immediate Settlement depends on
Settlement Location (Center or Corner)
{
Theory of Elasticity
Elastic Settlement
Time Depended Elastic Settlement (Schmertman & Hartman Method (1978)
{
By: Kamal Tawfiq, Ph.D., P.E.
Elastic settlement occurs in sandy, silty, and clayey soils.

## Slide 3
Water
Water Table (W.T.)
Voids
Solids
Expulsion of the water
Consolidation Settlement (Time Dependent Settlement)
By: Kamal Tawfiq, Ph.D., P.E.
* Consolidation settlement occurs in cohesive soils due to the expulsion of the water from the voids.
* Because of the soil permeability the rate of settlement may varied from soil to another.
* Also the variation in the rate of consolidation settlement depends on the boundary conditions.
SConsolidation = Sprimary + Ssecondary
Primary Consolidation Volume change is due to reduction in pore water pressure
Secondary Consolidation Volume change is due to the rearrangement of the soil particles
(No pore water pressure change, Δu = 0, occurs after the primary consolidation)
When the water in the voids starts to flow out of the soil matrix due to consolidation of the clay layer. Consequently, the excess pore water pressure (Du) will reduce, and the void ratio (e) of the soil matrix will reduce too.

## Slide 4
Elastic Settlement
Se = (1 - μs) α
2
2
(corner of the flexible foundation)
Se = (1 - μs) α
2
(center of the flexible foundation)
By: Kamal Tawfiq, Ph.D., P.E.
Where α = [ ln ( √1 + m2 + m / √1 + m2 - m ) + m. ln ( √1 + m2 + 1 / √1 + m2 - 1 )
m = B/L
B = width of foundation
L = length of foundation
1
p
Es
Bqo
Es
Bqo

## Slide 5
By: Kamal Tawfiq, Ph.D., P.E.
3.0
2.5
2.0
1.5
1.0
L / B
3.0
2
8
4
3
5
6
7
10
9
1
α, αav, αr
α
αav
αr
For circular foundation
α = 1
αav = 0.85
αr = 0.88
Values of α, αav, and αr
Bqo (1 - μs) α
Es
Se =

## Slide 7
DH =
Cc H
1 + eO
P0
Po + DP
log ( )
Dp
Dp
Dp
Dp
Dp
Dp

## Slide 8
Dp
Dp
Dp2
Dp2
Dp2
Dp
Dp
DH = log ( ) +
CS H
1 + eO
PC
Po
C C H
1 + eO
PC
Po + DP
log ( )
2
2

## Slide 9
Dp
Dp2
Dp2
Dp2
Dp2
DH = log
CS H
1 + eO
Po
Po + DP
( )
2

## Slide 11
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
G.S.
gsand = 96 pcf
gclay = 110 pcf
wc = 0.3
3 ft
4 ft
16 ft
Po
Sand
Clay
Po
Soil sample was obtained from the clay layer
Conduct consolidation test [9 load increments ]
Plot e vs. log (p) (Figure 2)
Determine Compression Index (Cc ) & Swelling Index (Cs)
Example:
Figure 2
Figure 1
Soil Sample
Cc
Cs
Dp
Dp7
Dp
Dp1
Dp9
In the lab and after removing
the soil sample from the ground,
the stresses on the soil sample = 0
In the lab the stresses are
added to the soil sample
Dp1
Dp9
5. Determine Po = 3.(96) + 4.(96-62.4) + 8.(110-62.4) = 803.2 lb/ft2
Stress
Increments
eo = 0.795
Dp2
In the ground, the sample was subjected to geostatic stresses.
In the lab and before the consolidation test the stresses on the sample = 0.
During testing, the geostatic stress is gradually recovered
Cc = 0.72
Cs = 0.1
Dr. Kamal Tawfiq - 2010

## Slide 12
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
G.S.
gsand = 96 pcf
gclay = 110 pcf
wc = 0.3
3 ft
4 ft
16 ft
Po
Sand
Clay
X
X
Po = Pc
6. Using Casagrande’s Method to determine Pc
Pc = 800 lb/ft2
Overconsolidation Ratio
OCR = = 1
The soil is
Normally Consolidated
N.C. soil
Example:
Dp1
Pc
Po
1
2
3
4
5
6
Point of
maximum curvature
Tangent to point 1
Tangent to point 1
7
Dr. Kamal Tawfiq - 2010

## Slide 13
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
X
X
Po = Pc
1
2 Horizontal line
3
4 divide the angle between 2 & 3
Extend the straight line
6 Intersection of 4 & 5
Point of
maximum curvature
Tangent to point 1
Overconsolidation Ratio OCR = = 1
The soil is Normally Consolidated (N.C.) soil
Pc
Po
7
1
Normally Consolidated Soil
Casagrande’s Method to Determine Preconsolidation Pressure (Pc)
Dr. Kamal Tawfiq - 2010

## Slide 14
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
X
X
Pc
1
2 Horizontal line
3
4 divide the angle between 2 & 3
5 Extend the stright line
6 Intersection of 4 & 5
Point of
maximum curvature
Tangent to point 1
Overconsolidation Ratio OCR = > 1
The soil is oversonsolidated (O.C.) soil
Pc
Po
7
Po
2
Overconsolidated Soil
Casagrande’s Method to Determine Pc
Dr. Kamal Tawfiq - 2010

## Slide 15
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Po
Sand
Clay
Po
A 150’ x 100’ building will be constructed at the site.
The vertical stress due to the addition of the building
qdesign =1000 lb/ft2
The weight of the building Qdesign will be transferred
to the mid height of the clay layer
Qdesign = 15,000,000 lb
The added stress at 15’ from
the ground surface is
Dp =
Example:
Dp1
Building
qdesign
Po
DP1
G.S.
(150+15) x (100+15)
15,000,000 lb
DP = 790.51 lb/ft2
DP + Po =
790.51 + 803 = 1593.51 lb/ft2
Dr. Kamal Tawfiq - 2010

## Slide 16
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Po
Sand
Clay
Po
Example:
Dp1
Building
qdesign
Po
DP1
G.S.
Consolidation Settlement
DH = log ( )
Cc H
1 + eO
Po + DP
Po
Po + DP
DP1
DP + Po = 790.51 + 803 = 1593.51 lb/ft2
DH = log ( )
0.72 x 16
1 + 0.795
1593.51
803
DH = 1.9 ft
Dr. Kamal Tawfiq - 2010

## Slide 17
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Po
Sand
Clay
Po
Dp1
qdesign
Po
G.S.
Po + DP
DP1
When the building was removed, the soil has become
an overconsolidated clay.
The rebound has taken place through
swelling from pint 1 to point 2
2
1
Demolished
Dr. Kamal Tawfiq - 2010

## Slide 18
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Po
Sand
Clay
Po
Dp1
qdesign
Po
G.S.
Po + DP
DP2
New Building
CS
CC
DH = log ( ) +
CS H
1 + eO
PC
Po
C C H
1 + eO
PC
Po + DP
log ( )
Scenario #1
The soil now is overconsolidated Soil:
The new building is heavier in weight
Pc
Constructing a new building
DP2
DP1
eo = 0.61
Assume Po + Dp2 = 2100 psf
DH =
0.1 x 16
1 + 0.61
1593.51
803
log
( )
+
0.72 x 16
1 + 0.61
1593.51
log
( )
2100
=
Dr. Kamal Tawfiq - 2010

## Slide 19
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
W.T.
gsand = 96 pcf
eo = wc . Gs = 0.3 x 2.65 = 0.795
3 ft
4 ft
16 ft
Po
Sand
Clay
Po
Scenario # 2
The soil now is overconsolidated Soil:
The new building is lighter in weight
Dp1
qdesign
Po
G.S.
DH =
CS H
1 + eO
Po + DP
New Building
P0
Po + DP
log ( )
CS
DP2
Constructing a new building
DP2
DP1
eo = 0.61
Assume Po + Dp2 = 1600 psf
DH =
0.1 x 16
1 + 0.61
1600
1593.51
log
( )
=
Dr. Kamal Tawfiq - 2010

## Slide 20
Chart: 
| 1 | 1
 | 1000 | 1000
Example of Semi-log Scale
Dr. Kamal Tawfiq - 2010