## Slide 1
Soil Settlement
By
Kamal Tawfiq, Ph.D., P.E., F.ASCE
Spring 2019

## Slide 2
Soil Settlement:
Total Soil Settlement = Elastic Settlement + Consolidation Settlement
Stotal = Se + Sc
Load Type (Rigid; Flexible)
Elastic Settlement or Immediate Settlement depends on
Settlement Location (Center or Corner)
{
Theory of Elasticity
Elastic Settlement
Time Depended Elastic Settlement (Schmertman & Hartman Method (1978)
{
By: Kamal Tawfiq, Ph.D., P.E.
Elastic settlement occurs in sandy, silty, and clayey soils.

## Slide 3
Water
Water Table (W.T.)
Voids
Solids
Expulsion of the water
Consolidation Settlement (Time Dependent Settlement)
By: Kamal Tawfiq, Ph.D., P.E.
* Consolidation settlement occurs in cohesive soils due to the expulsion of the water from the voids.
* Because of the soil permeability the rate of settlement may varied from soil to another.
* Also the variation in the rate of consolidation settlement depends on the boundary conditions.
SConsolidation = Sprimary + Ssecondary
Primary Consolidation Volume change is due to reduction in pore water pressure
Secondary Consolidation Volume change is due to the rearrangement of the soil particles
(No pore water pressure change, Δu = 0, occurs after the primary consolidation)
When the water in the voids starts to flow out of the soil matrix due to consolidation of the clay layer. Consequently, the excess pore water pressure (Du) will reduce, and the void ratio (e) of the soil matrix will reduce too.
Settlement DH
Log Time
Primary Consolidation
Secondary Consolidation

## Slide 4
Elastic Settlement
Se = (1 - μs) α
2
2
(corner of the flexible foundation)
Se = (1 - μs) α
2
(center of the flexible foundation)
By: Kamal Tawfiq, Ph.D., P.E.
Where α = [ ln ( √1 + m2 + m / √1 + m2 - m ) + m. ln ( √1 + m2 + 1 / √1 + m2 - 1 )
m = B/L
B = width of foundation
L = length of foundation
1
p
Es
Bqo
Es
Bqo

## Slide 5
By: Kamal Tawfiq, Ph.D., P.E.
3.0
2.5
2.0
1.5
1.0
L / B
0.0
2
8
4
3
5
6
7
10
9
1
α, αav, αr
α
αav
αr
For circular foundation
α = 1
αav = 0.85
αr = 0.88
Values of α, αav, and αr
Bqo (1 - μs) α
Es
Se =

## Slide 6
Laboratory Consolidation Test
- One Dimensional Consolidation
Soil Sample
Depth of Sampling
H
De
1
e
1st Load Increment
2st Load Increment
4st Load
Increment
Plot all
De vs. Load increments
De1 vs. DP1
De2 vs. DP2
De1
DP2
Cc
Cc
Cs

## Slide 7
Consolidation Settlement
Two way
drainage path
H
H/2
Assume a fully saturated Sponge
Seepage
Ds
DP
P

## Slide 9
How do you know if the clay layer at the site is
normally consolidated or
Over-consolidated ???
Question
G.S.
Sand
Today
Case 1
Past
Case 2
Past
Po
Clay
Normally Consolidated and Overconsolidated Clay
Use Casagrande Graphical Method to determine Pc
If Pc = Po .. Soil is NC
If Pc > Po .. Soil is OC
Po = Vertical effective stress at the mid of the clay layer,
It is known

## Slide 10
Chart: 
| 1 | 1
 | 1000 | 1000
Log (p)
Void Ratio (e)
Pc = Po
Dp1
Po + DP
DP1
Normally Consolidated
Stress of the building at the mid height of the clay layer
Case 1

## Slide 11
Chart: 
| 1 | 1
 | 1000 | 1000
Void Ratio (e)
Po
Dp1
Po + DP
DP2
CS
CC
Pc
DP1
Stress of the building at the mid height of the clay layer
Over-consolidated
Case 2-1

## Slide 12
Chart: 
| 1 | 1
 | 1000 | 1000
Void Ratio (e)
Po
Dp1
Po + DP
CS
CC
Pc
DP2
Stress of the building at the mid height of the clay layer
Over-consolidated
Case 2-2

## Slide 14
DH =
CS H
1 + eO
P0
Po + DP
log ( )
Dp
Dp
Dp
Dp
Dp
Dp

## Slide 15
Dp
Dp
Dp2
Dp2
Dp2
Dp
Dp
DH = log ( ) +
CS H
1 + eO
PC
Po
C C H
1 + eO
PC
Po + DP
log ( )

## Slide 16
Dp
Dp2
Dp2
Dp2
Dp2
DH = log
CS H
1 + eO
Po
Po + DP
( )
2