## Slide 1
Slope Stability Analysis
for Landfills and Embankments
Geotechnical Design
CGN 4801
By
Kamal Tawfiq, Ph.D., P.E.

## Slide 3
Slope stability analysis is performed to assess the safe design of a human-made or natural slopes (e.g. embankments, road cuts, open-pit mining, excavations, landfills etc.) and the equilibrium conditions.
The main objectives of slope stability analysis are finding endangered areas, investigation of potential failure mechanisms, determination of the slope sensitivity to different triggering mechanisms, designing of optimal slopes with regard to safety, reliability and economics, designing possible remedial measures, e.g. barriers and stabilization.
Slope Stability Analysis and Design

## Slide 4
FACTORS AFFECTING SLOPE STABILITY
1- Soil Type
2- Geometry of the cross section (Height, slope angle, etc.)
3- Moisture Content
4- Pore water pressure
5- Additional loads
6- Shear Strength reduction
7- Vibrations and Earthquake
By Kamal Tawfiq, Ph.D., P.E.

## Slide 5
To Analyze and Design Slopes, We use the Following Categories

## Slide 6
W
T
N
Friction = N tan d
Driving Force = T = W . sinb
b
Resisting Force = F = N tand = (W.cosb) tand
F.S. = Fresisting/Fdriving
W
T
N
Friction = N tan d
b

## Slide 7
W
T
N
Friction = N tan ddeveloped
Driving Force = T = W . sinb
b
Resisting Force = F = N tand = (W.cosb) tand
F.S. = Fresisting/Fdriving
W
T
N
Friction = N tan d
b
The Concept of Developed Friction
Developed Friction
F.S. = 1 =
Resisting Force
Driving Force
F.S. = 2.5 =
Resisting Force
Driving Force
On the verge of failure

## Slide 8
FACTOR OF SAFETY
1- For Shear Strength
tdeveloped = t / F.S.
tdeveloped = (c + σ tanϕ) / F.S.
2- For Shear Parameters
cd = c / F.S.
tanϕd = tanϕ / F.S.
3- For Height of the Slope
Hdesign = Hc / F.S.
Developed angle of friction
Developed cohesion or
Mobilized cohesion

## Slide 9
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, FV = W cos β
Weight = W
β
τ = N tanϕ
N = Fv = W cos β
INFINITE SLOPE
I. PLANAR FAILURE or Transitional Failure
H
1
b = 1 cosβ
A- Dry Soil (ϕ soil)
W = g H cosβ
b = 1 cosβ
By Kamal Tawfiq, Ph.D., P.E.
Shear Resistance

## Slide 10
G.S.
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, FV = W cos β
Weight = W
β
τ = N tanϕ
N = Fv = W cos β
1
b = 1 cosβ
A- Dry Soil (ϕ soil)
W = g H cosβ
b = 1 cosβ
Driving Force = FD = g H cos β sinβ
Resisting Force = FR = g H cos β cosβ tanϕ
FS = FR/FD
g H cos β sinβ
g H cos β cosβ tanϕ
FS =
tanϕ
FS =
tanβ
By Kamal Tawfiq, Ph.D., P.E.
β

## Slide 11
G.S.
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, FV = W cos β
Weight = W
β
τ = N tanϕ
N = Fv = W cos β
1
b = 1 cosβ
B- Submarged Soil (ϕ soil)
W = g H cosβ
Driving Force = FD = g H cos β sinβ
Resisting Force = FR = g H cos β cosβ tanϕ
FS = FR / FD
g H cos β sinβ
g H cos β cosβ tanϕ
FS =
tanϕ
FS =
tanβ
W.T
_
_
_
_

## Slide 12
C- Seepage Parallel to Slope (ϕ soil)
G.S.
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, Neff = (W – u) cos β
Weight = W
β
τ = Neff tanϕ
Neff = (W-u) cos β
1
b = 1 cosβ
Seepage
tanϕ
FS =
tanβ
gw Z
gsoilH cos2β
(1-
)
By Kamal Tawfiq, Ph.D., P.E.
Pore Water Pressure (u)
Z = Pressure Head
What is Pressure Head?
What is Total Head?
What is Elevation Head?
Total Head = Elevation Head+ Pressure Head
Go to Next Page

## Slide 13
Pressure
Head
Elevation
Head
Datum
Pressure
Head
Elevation
Head
Datum
Ground Surface
Failure Surface
Flow Line
Flow Line
Flow Line
Equipotential Line
Elevation
Head
Elevation
Head
Pressure
Head
phreatic line
Atmospheric Pressure Line
Pore Water Pressure (u)
=
Pressure head *( gwater )
=
g z
Total Head, Elevation Head and Pressure Head
Total Head = Elevation Head+ Pressure Head
Head Loss

## Slide 14
d
dw
b
W
T
N’
U
b/cos a
a
dwcos a
Soil Surface
Water Table
Assumed failure surface
For the infinite slope shown below, what is the pore water pressure at point A ?
A
a
Z
Z = dw cos a (cos a)
B
Z
Pore Water Pressure (u) = gwater * g z
Z = Pressure Head

## Slide 15
G.S.
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, FV = W cos β
Weight = W
β
t = C + N tanϕ
N = Fv = W cos β
1
b = 1 cosβ
D- Infinite Slope in c - ϕ soil (with seepage)
tanϕ
tanβ
FS =
c
gsoil H cosβ sinβ
gsoil H cos2β
(1-
u
)
If no seepage:
u = 0
If Submerged Slope:
u = 0 g = g’
By Kamal Tawfiq, Ph.D., P.E.
+

## Slide 16
Stability Number Ns
tanϕ
tanβ
FS =
c
gsoil H cosβ sinβ
gsoil H cos2β
(1-
u
)
= 1
Critical Height Hc at FS = 1
Ns =
c
gHc
ru =
u
gH
= pore water pressure ratio
Hc =
c
gsoil [sinβ cosβ - tanϕ (cos2β - ru)]
Hc =
c
gsoil cos2β (tanβ - tanϕ)
- u tanϕ
General Equation:
By Kamal Tawfiq, Ph.D., P.E.
+
H =
cdev
gsoil [sinβ cosβ - tanϕdev (cos2β - ru)]
Or
cdev =
c
FSc
tanfdev =
tanf
FSf
fdev = tan-1 ( )
tanf
FSf
(with seepage)
H
β
Weight = W
β
N = Fv = W cos β
W sinb
W cosb
t = C + N tanϕ
seepage

## Slide 17
γH
cd
= sinβ cosβ - tanϕd (cos2β - ru)
Ns =
Hc =
c
γsoil [sinβ cosβ - tanϕ (cos2β - ru)]
γHc
c
= sinβ cosβ - tanϕ (cos2β - ru)
Ns =
General Equation:
tanϕd =
tanϕ
FSf
cd =
c
FSc
H
β
β
seepage
ϕ = 45o
ϕ = 35o
ϕ = 25o
ϕ = 15o
Ns =
c
gHc
β
γH
cd
= sinβ cosβ - tanϕd (cos2β - ru)
Ns =

## Slide 18
To Analyze and Design Slopes, We use the Following Categories

## Slide 19
Finite Failure Planar Failure
Cd =
γH
4
1- cos (β -ϕd)
Sin β cos ϕd
Hcr =
4c
g
Sin β cos ϕ
1- cos (β - ϕ)
Driving Force = Fd = W sinβ
N = W cos β
W
β
τ = c + σ tanϕ
θ
β
γ = ✓
ϕ = ✓
c = ✓
H
A
B
C
H =
4cd
g
Sin β cos ϕd
1- cos (β - ϕd)
or

## Slide 20
Example:
Given:
b= 30o
H = 10 ft
= 32o
c = 180 psf
Find:
F.S. of the Slope
H =
4cd
g
Sin β cos ϕd
1- cos (β - ϕd)

## Slide 21
Center
R
a2
c . L
W1
θ
R
A
R
B
R
C
W2
F.S. =
Mdriving
Mresisting
Circular Failure Surface (Cohesive Soil)
Determinate Problem
Number of Unknowns = Number of Equilibrium Equations
Mresisting = c . L + W2 . a2 = c . (R.θ) R + W2 . a2
Mdriving = W1 . a1
W1 = Area (BCDE) . γsoil
By Kamal Tawfiq, Ph.D., P.E.
D
E
a1

## Slide 22
Circuler Failure Surface in C - f Soil
Indeterminate Problem
Number of Unknowns ≠ Number of Equilibrium Equations
W varies from point to point. Therefore, N & F will vary from point to point
Center
R
W1
W2

## Slide 23
Circuler Failure Surface in C - f Soil
Indeterminate Problem
Number of Unknowns ≠ Number of Equilibrium Equations
W varies from point to point. Therefore, N & F will vary from point to point
Center
R
f
N
t
F
W
W sinq
W cosq
q
q

## Slide 24
A variety of charted solutions exist for the simple geometry considered above.
For the undrained (total stress) analysis of slopes charts produced by Taylor are often used.
The charts are based on the analysis of circular failure surfaces, and assume that soil strength is given by a Mohr-Coulomb analysis
Tension cracks are not considered
Stability Number

## Slide 25
αi
H
nH
DH
Taylor’s Method
By Kamal Tawfiq, Ph.D., P.E.

## Slide 26
Taylor’s Chart

## Slide 28
Taylor’s Chart
H = ?
30
o
cu = 20 kN/m2
fu = 10o
gbulk = 15 kN/m3
F.S. = 1.5
Since the factor of safety is given, then the problem indicates a design of a new slope
Solution:
Use the chart with i = 30o, and fmob = tan-1 (
tan 10o
1.5
)
= 6.7o
fmob
SN = 0.1 =
20/1.5
15 x Hdesign
Hdesign = = 8.88 m
20/1.5
15 x 0.1
SN = 0.1
Example - 1
fmobilized = fdeveloped

## Slide 29
Taylor’s Chart
H = 7 m
30
o
cu = 20 kN/m2
fu = 10o
gbulk = 15 kN/m3
F.S. = ????
Since the factor of safety is not given, then the problem indicates an existing slope that we need
to analyze its safety.
Solution:
2- Use the chart with i = 30o, and fmob = tan-1 (
tan 10o
1.0
)
= 10o
fmob
SN = 0.075 =
cmob
15 x 7
4- cmob = 15 x 7 x 0.075 = 7.87 kN/m2
5- FSc = c / cmob = 20/7.87 = 2.5
Therefore the Assumed FSf = the calculated FSc
SN = 0.075
Example - 2
1- Assume FSf = 1
3- Go to the chart and find SN for fmob = 10o
Trial # 1
fmobilized = fdeveloped

## Slide 30
This means the assumed factor of safety was not the right one. So we need
to assume another FSf and solve the problem again for FSc.
2- Use the chart with i = 30o, and fmob = tan-1 (
tan 10o
1.5
)
= 6.7o
SN = 0.1 =
cmob
15 x 7
4- cmob = 15 x 7 x 0.10 = 10.5 kN/m2
5- FSc = c / cmob = 20/10.5 = 1.9
Therefore the Assumed FSf = the calculated FSc
1- Assume FSf = 1.5
3- Go to the chart and find SN for fmob = 6.7o
Trial # 2
fmob
SN = 0.1
This means the assumed factor of safety was not the right one. So we need
to assume another FSf and solve the problem again for FSc.

## Slide 31
2- Use the chart with i = 30o, and fmob = tan-1 (
tan 10o
1.8
)
= 5.5o
SN = 0.11 =
cmob
15 x 7
4- cmob = 15 x 7 x 0.11 = 11.55 kN/m2
5- FSc = c / cmob = 20/11.55 = 1.73
Therefore the Assumed FSf = the calculated FSc
1- Assume FSf = 1.8
3- Go to the chart and find SN for fmob = 5.5o
Trial # 3
fmob
SN = 0.11
This means the assumed factor of safety was not the right one. So we need
to assume another FSf and solve the problem again for FSc.

## Slide 32
Since we complied three different trials, we are ready to find the right
factor of safety by using the 45o line method
Assumed FSf Calculated FSc
1.0 2.5
1.5 1.9
1.8 1.73
Chart: 
| 1 | 1.5 | 1.8
 | 2.5 | 1.9 | 1.73
1.75
1.75
So the correct FS is 1.75

## Slide 33
Zones are marked on the chart indicating whether the failure mode will be shallow or deep-seated.
If a deep-seated failure is indicated the soil layer must be sufficiently deep to enable this mechanism to occur.
There is a second chart due to Taylor which can be used when the depth of soil below the base of the slope is limited
This chart is only valid for f = 0
Taylor’s Chart - example

## Slide 35
Taylor’s Chart - example with finite depth
8 m
30
o
2 m
Rock
Calculate the Depth Factor D

## Slide 36
Taylor’s Chart - example with finite depth
8 m
30
o
2 m
Rock
DH
Calculate the Depth Factor D
DH = 10 m

## Slide 37
Taylor’s Chart - example with finite depth
8 m
30
o
2 m
Rock
DH
Calculate the Depth Factor D
DH = 10 m, H = 8m
D = 1.25

## Slide 39
Taylor’s Chart - example with finite depth
8 m
30
o
2 m
Rock
DH
D = 1.25
Cdev
15 x 8
= 0.165
Cdev = 0.165 x 15 x 8 = 19.8 kN/m2 FS = 1.01

## Slide 40
STATICALLY INDETERMINATE PROBLEMS
METHOD OF SLICES
αi
Center
1
2
3
4
5
6
7
8
9
10
11
αi
Resultant
Δx
Si
L
Wi
S + ΔS
Xi
R
Center
Ei
E + ΔE
Ti = c.L + Neffi tan ϕ
ϕ
Ni = Neffi + ui L
αi
αi
Ni = Neff + ui L
Ti = c.L + Neff tan ϕ
Wi
Wi cos α
Wi sin α
By Kamal Tawfiq, Ph.D., P.E
ϕ

## Slide 41
αi
Resultant
Δxi
Si
Li
Wi
S + ΔS
Xi
R
Center
Ei
Ei + ΔE
Ti = c.Li + Neffi tan ϕ
ϕ
Ni = Neffi + ui Li
αi
bi
αi
θi
ai
αi
Unknowns Associated with Force Equilibrium
n = Resultant normal forces Ni on the base of each slice or wedge
1 = Safety factor, which permits the shear forces Ti on the base of each
slice to be expressed in terms of Ni
n-1 = Resultant normal forces Ei on each interface between slices or wedges
n-1 = Angles αi which express the relationships between the shear force Si
and the normal force Ei on each interface
By Kamal Tawfiq, Ph.D., P.E

## Slide 42
FELLENIUS METHOD (ORDINARY METHOD, SWEDISH METHOD)
αi
Resultant
Δxi
Si
Li
Wi
S + ΔS
Xi
R
Center
Ei
Ei + ΔE
Ti = c.Li + Neffi tan ϕ
ϕ
Ni = Neffi + ui Li
αi
bi
αi
αi
ai
αi
Ni = Neffi + ui L
Ti = c.L + Neffi tan ϕ
Wi
Wi cos α
Wi sin α
MR ∑CLi +(wicosθi -uiLi)tanϕ
MD ∑wi sinθi
=
=
F
By Kamal Tawfiq, Ph.D., P.E

## Slide 45
1.5
1.0
Stiff Layer
Drain
= 125 lb/ft3
c = 90 lb/ft2
f = 32o
20 ft
Center of failure Surface
R = 30 ft
1
2
3
4
5
6
7
8
9
hw6
This example is from Lambe and Whitman (1969), John Wiley & Sons Publisher
Kamal Tawfiq, Ph.D., P.E.
Pore Water Pressure = u6 = hw6 x g water
hw7

## Slide 46
Slice | Width Dx (ft) | Ave Height (ft) | Weight (Kips) | qi | Wi sin qi | Wi cos qi | ui | Dli | Ui = ui Dli | Ni = Wi cosqi - Ui
1 | 4.5 | 1.6 | 0.9 | -1.7 | 0 | 0.9 | 0 | 4.4 | 0 | 0.9
2 | 3.2 | 4.2 | 1.7 | 2.9 | 0.1 | 1.7 | 0 | 3.2 | 0 | 1.7
3 | 1.8 | 5.8 | 1.3 | 8.05 | 0.2 | 1.3 | 0.03 | 1.9 | 0.05 | 1.25
4 | 5.0 | 7.4 | 4.6 | 14.5 | 1.2 | 4.5 | 0.21 | 5.3 | 1.1 | 3.4
5 | 5.0 | 9.0 | 5.6 | 24.8 | 2.3 | 5.1 | 0.29 | 5.6 | 1.6 | 3.5
6 | 5.0 | 9.3 | 5.8 | 35.4 | 3.4 | 4.7 | 0.25 | 6.2 | 1.55 | 3.15
7 | 4.4 | 8.4 | 4.6 | 47.7 | 3.4 | 3.1 | 0.11 | 6.7 | 0.7 | 2.4
8 | 0.6 | 6.7 | 0.5 | 55.1 | 0.4 | 0.3 | 0 | 1.2 | 0 | 0.3
9 | 3.2 | 3.8 | 1.5 | 60.4 | 1.3 | 0.7 | 0 | 7.3 | 0 | 0.7
 |  |  |  |  | 12.3 |  |  | 41.8 |  | 17.3
1- Using Ordinary Method of Slices (Swedish Method)
Kamal Tawfiq, Ph.D., P.E.

## Slide 47
(1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) |  | (9) | 
 |  |  |  |  |  |  | Mi |  | (7)/(8) | 
Slice | Width Dx (ft) | C Dxi (kips) | ui Dxi (Kips) | Wi-ui Dxi (Kips) | (5).(tan f) (Kips) | (3)+(6) (Kips) | Assume F=1.25 | Assume F=1.35 | F=1.25 | F=1.35
1 | 4.5 | 0.4 | 0 | 0.9 | 0.55 | 0.95 | 0.97 | 0.97 | 1.0 | 1.0
2 | 3.2 | 0.29 | 0 | 1.7 | 1.05 | 1.35 | 1.02 | 1.02 | 1.3 | 1.3
3 | 1.8 | 0.16 | 0.05 | 1.25 | 0.8 | 0.95 | 1.06 | 1.05 | 0.9 | 0.9
4 | 5.0 | 0.45 | 1.05 | 3.55 | 2.25 | 2.7 | 1.09 | 1.08 | 2.5 | 2.5
5 | 5.0 | 0.45 | 1.45 | 4.15 | 2.55 | 3.00 | 1.12 | 1.10 | 2.7 | 2.75
6 | 5.0 | 0.45 | 1.25 | 4.55 | 2.7 | 3.15 | 1.1 | 1.08 | 2.85 | 2.9
7 | 4.4 | 0.4 | 0.5 | 4.1 | 2.65 | 3.05 | 1.05 | 1.02 | 2.9 | 2.95
8 | 0.6 | 0.05 | 0 | 0.5 | 0.3 | 0.35 | 0.98 | 0.95 | 0.35 | 0.4
9 | 3.2 | 0.29 | 0 | 1.5 | 0.95 | 1.25 | 0.93 | 0.92 | 1.3 | 1.35
 |  |  |  |  |  |  |  |  | 15.8 | 16.09
2- Using Simplified Bishop Method
From the previous solution
Kamal Tawfiq, Ph.D., P.E.

## Slide 48
R = 30 ft
1.5
1.0
Stiff Layer
Drain
= 125 lb/ft3
c = 90 lb/ft2
f = 32o
20 ft
Center of failure Surface
A
What is the pore water pressure at point A?
Name:__________ ID:________
CEG 4801 Geotechnical Design
Spring 2018