## Slide 1
Slope Stability Analysis
for Landfills and Embankments
Geotechnical Design
CGN 4801
By
Kamal Tawfiq, Ph.D., P.E.

## Slide 2
Slope stability analysis is performed to assess the safe design of a human-made or natural slopes (e.g. embankments, road cuts, open-pit mining, excavations, landfills etc.) and the equilibrium conditions.
The main objectives of slope stability analysis are finding endangered areas, investigation of potential failure mechanisms, determination of the slope sensitivity to different triggering mechanisms, designing of optimal slopes with regard to safety, reliability and economics, designing possible remedial measures, e.g. barriers and stabilization.
Slope Stability Analysis and Design

## Slide 3
FACTORS AFFECTING SLOPE STABILITY
1- Soil Type
2- Geometry of the cross section (Height, slope angle, etc.)
3- Moisture Content
4- Pore water pressure
5- Additional loads
6- Shear Strength reduction
7- Vibrations and Earthquake
By Kamal Tawfiq, Ph.D., P.E.

## Slide 4
To Analyze and Design Slopes:
1- Planar Failures (Determinate Problems)
Infinite Failures Small depth, Long failure surface
Finite Slope Failures Simple wedge
Depth
b
H
2- Circular Failures (Determinate & Indeterminate Problems)
Above Toe
Through Toe
Deep seated
3- Wedge Failures Multiple Planer Failure
4- Complex Failures Combination of Planar & Circular
H
b

## Slide 5
W
T
N
Friction = N tan ddeveloped
Driving Force = T = W . sinb
b
Resisting Force = F = N tand = (W.cosb) tand
F.S. = Fresisting/Fdriving
The Concept of Developed Friction
Developed Friction
F.S. = 1 =
Resisting Force
Driving Force
F.S. = 2.5 =
Resisting Force
Driving Force
On the verge of failure
1. Planar Failures

## Slide 6
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, FV = W cos β
Weight = W
β
τ = N tanϕ
N = Fv = W cos β
INFINITE SLOPE
I. PLANAR FAILURE or Transitional Failure
H
1
b = 1 cosβ
A- Dry Soil (ϕ soil)
W = g H cosβ
b = 1 cosβ
By Kamal Tawfiq, Ph.D., P.E.
Shear Resistance

## Slide 7
G.S.
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, FV = W cos β
Weight = W
β
τ = N tanϕ
N = Fv = W cos β
1
b = 1 cosβ
A- Dry Soil (ϕ soil)
W = g H cosβ
b = 1 cosβ
Driving Force = FD = g H cos β sinβ
Resisting Force = FR = g H cos β cosβ tanϕ
FS = FR/FD
g H cos β sinβ
g H cos β cosβ tanϕ
FS =
tanϕ
FS =
tanβ
By Kamal Tawfiq, Ph.D., P.E.
β

## Slide 8
G.S.
Failure
Surface
H
β
Normal Component, FV = W cos β
Weight = W
β
τ = N tanϕ
N = Fv = W cos β
1
b = 1 cosβ
B- Submerged Soil (ϕ soil)
W = g H cosβ
Driving Force = FD = g H cos β sinβ
Resisting Force = FR = g H cos β cosβ tanϕ
FS = FR / FD
g H cos β sinβ
g H cos β cosβ tanϕ
FS =
tanϕ
FS =
tanβ
W.T
_
_
_
_
Driving Force, FD = W sin β

## Slide 9
C- Seepage Parallel to Slope (ϕ soil)
G.S.
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, Neff = (W – u) cos β
Weight = W
τ = Neff tanϕ
Neff = (W-u) cos β
1
b = 1 cosβ
Seepage
tanϕ
FS =
tanβ
gw Z
gsoilH cos2β
(1-
)
By Kamal Tawfiq, Ph.D., P.E.
Pore Water Pressure (u)
Z = Pressure Head
What is Pressure Head?
What is Total Head?
What is Elevation Head?
Total Head = Elevation Head+ Pressure Head
Go to Next Page
β

## Slide 10
Pressure
Head
Elevation
Head
Datum
Pressure
Head
Elevation
Head
Datum
Ground Surface
Failure Surface
Flow Line
Flow Line
Flow Line
Equipotential Line
Elevation
Head
Elevation
Head
Pressure
Head
phreatic line
Atmospheric Pressure Line
Pore Water Pressure (u)
=
Pressure head *( gwater )
=
g z
Total Head, Elevation Head and Pressure Head
Total Head = Elevation Head+ Pressure Head
Head Loss

## Slide 11
d
dw
b
W
T
N’
U
b/cos a
a
dwcos a
Soil Surface
Water Table
Assumed failure surface
For the infinite slope shown below, what is the pore water pressure at point A ?
A
a
Z
Z = dw cos a (cos a)
B
Z
Pore Water Pressure (u) = gwater * g z
Z = Pressure Head

## Slide 12
G.S.
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, FV = W cos β
Weight = W
β
t = C + N tanϕ
N = Fv = W cos β
1
b = 1 cosβ
D- Infinite Slope in c - ϕ soil (with seepage)
tanϕ
tanβ
FS =
c
gsoil H cosβ sinβ
gsoil H cos2β
(1-
u
)
If no seepage:
u = 0
If Submerged Slope:
u = 0 g = g’
By Kamal Tawfiq, Ph.D., P.E.
+

## Slide 13
Stability Number Ns and Pore Water Pressure Ration ru
tanϕ
tanβ
FS =
c
gsoil H cosβ sinβ
gsoil H cos2β
(1-
u
)
= 1
Critical Height Hc at FS = 1
Ns =
c
gHc
ru =
u
gH
= pore water pressure ratio
Hc =
c
gsoil [sinβ cosβ - tanϕ (cos2β - ru)]
Hc =
c
gsoil cos2β (tanβ - tanϕ)
- u tanϕ
General Equation:
By Kamal Tawfiq, Ph.D., P.E.
+
H =
cd
gsoil [sinβ cosβ - tanϕd (cos2β - ru)]
Or
cdev =
c
FSc
tanfdev =
tanf
FSf
fdev = tan-1 ( )
tanf
FSf
(with seepage)
H
β
Weight = W
β
N = Fv = W cos β
W sinb
W cosb
t = C + N tanϕ
seepage
Developed (d)
or
Mobilized (m)
Planar Slope Failure
Infinite Slope
1
2
3

## Slide 14
Planar Slope Failure
Finite Slope
Ta = W.sinq
W
q
b
A
H
B
C
c =
Na = W.cosq
Tr
Na = Nr
Na = normal component =
Ta = tangential component =

## Slide 15
Na = normal component =
Ta = tangential component =
…… Driving Shear Stress
Planar Slope Failure
Finite Slope
Ta = W.sinq
W
q
b
A
H
B
C
c =
Na = W.cosq
Tr
Na = Nr

## Slide 16
Solved Example:
Given:
g = 112 pcf
b= 55o
= 26o
q = 35o
c = 520 psf
F.S = 1.5
Find:
Safe Height:
Solution:
Since we know the safety factor, then
cd =
…….
Ta = W.sinq
W
q
b
A
H
B
C
c =
Na = W.cosq
Tr
Na = Nr

## Slide 17
Solved Example:
Given:
g = 112 pcf
b= 55o
= 26o
q = 35o
c = 520 psf
H = 8’
Find:
If the slope is safe or not.
Solution:
Since we don’t know the F.S of the slope (F.Sc = F.Sf), then
1- Assume F.Sf = 1 …..
2- Find F.Sc
3- Assume F.Sf= 2
4- Find F.Sc
Fd = W.sinq
N = W.cosq
W
q
b
A
H
B
C
c =

## Slide 18
Center
R
a2
c . L
W1
θ
R
A
R
B
R
C
W2
F.S. =
Mdriving
Mresisting
Circular Failure Surface (Cohesive Soil)
Determinate Problem
Number of Unknowns = Number of Equilibrium Equations
Mresisting = c . L + W2 . a2 = c . (R.θ) R + W2 . a2
Mdriving = W1 . a1
W1 = Area (BCDE) . γsoil
By Kamal Tawfiq, Ph.D., P.E.
D
E
a1

## Slide 19
Circular Method in Clayey Soil (f = 0)
center
center
Radius = R
Radius = R
Shear Resistance = C = c L
W1
W2
a1
a2
Factor of Safety =
Resisting Moment (MR)
Driving Moment (MD)
Resisting Moment (MR) = W2 x a2 + C x R
q
R.q
Driving Moment (MD) = W1 x a1
CG1
CG2
Green Area x Soil Unit Weigh
Yellow Area x Soil Unit Weigh
How to find W1, W2 , CG1 and CG2 ?
Refer to your Eng. Mechanics course
Case 1
Case 2

## Slide 20
Factor of Safety =
Resisting Moment (MR)
Driving Moment (MD)
center
Radius = R
a3
a4
q
CG1
A1
A2
A3
A4
W1
W3
W2
W4
CG3
CG2
CG4
a1
a2
C = c L
Resisting Moment (MR) = W4 x a4 + C x R
Driving Moment (MD)=W1xa1+W2xa2++W3xa3

## Slide 21
Circuler Failure Surface in C - f Soil
Indeterminate Problem
Number of Unknowns ≠ Number of Equilibrium Equations
W varies from point to point. Therefore, N & F will vary from point to point
Center
R
W1
W2

## Slide 22
Circuler Failure Surface in C - f Soil
Indeterminate Problem
Number of Unknowns ≠ Number of Equilibrium Equations
W varies from point to point. Therefore, N & F will vary from point to point
Center
R
f
N
tr
F
W
W sinq
W cosq
q
q

## Slide 23
A variety of charted solutions exist for the simple geometry considered above.
For the undrained (total stress) analysis of slopes charts produced by Taylor are often used.
The charts are based on the analysis of circular failure surfaces, and assume that soil strength is given by a Mohr-Coulomb analysis
Tension cracks are not considered
Stability Number

## Slide 24
αi
H
nH
DH
Taylor’s Method
By Kamal Tawfiq, Ph.D., P.E.

## Slide 25
Taylor’s Chart

## Slide 27
Solution:
Use the chart with i = 30o, and fdev = tan-1 (
tan 10o
1.5
)
= 6.7o
SN = 0.1 =
20/1.5
15 x Hdesign
Hdesign = = 8.88 m
20/1.5
15 x 0.1
Example 1:
Given:
cu = 20 kN/m2
fu = 10o
gbulk = 15 kN/m3
F.S. = 1.5
Find:
Safe Height (H)
Hdesign=?
b=30o
or b=30o
Stability Number (c / gH)
Slope Angle b (deg)
SN = 0.1

## Slide 28
Solution:
2- Use the chart with b = 30o, and fdev = tan-1 (
tan 10o
1.0
SN = 0.075 =
cdev
15 x 7
4- cdev = 15 x 7 x 0.075 = 7.87 kN/m2
5- FSc = c / cdev = 20 / 7.87 = 2.5
Therefore the Assumed FSf = the calculated FSc
1- Assume FSf = 1
3- Go to the chart and find SN for fdev = 10o
Trial # 1
Given:
cu = 20 kN/m2
fu = 10o
gbulk = 15 kN/m3
H = 7 m
b= 30o
Find:
F.S.
Example 2:
)
= 10o
H= 7m
b=30o
Stability Number (c / gH)
Slope Angle b (deg)
SN=0.075

## Slide 29
This means the assumed factor of safety was not the right one. So we need
to assume another FSf and solve the problem again for FSc.
2- Use the chart with i = 30o, and fdev = tan-1 (
tan 10o
1.5
)
= 6.7o
SN = 0.1 =
cdev
15 x 7
4- cdev = 15 x 7 x 0.10 = 10.5 kN/m2
5- FSc = c / cdev = 20/10.5 = 1.9
Therefore the Assumed FSf = the calculated FSc
1- Assume FSf = 1.5
3- Go to the chart and find SN for fdev = 6.7o
Trial # 2
This means the assumed factor of safety was not the right one. So we need to assume another FSf and solve the problem again for FSc.
Stability Number (c / gH)
Slope Angle b (deg)

## Slide 30
2- Use the chart with i = 30o, and fdev = tan-1 (
tan 10o
1.8
)
= 5.5o
SN = 0.11 =
cdev
15 x 7
4- cdev = 15 x 7 x 0.11 = 11.55 kN/m2
5- FSc = c / cdev = 20/11.55 = 1.73
Therefore the Assumed FSf = the calculated FSc
1- Assume FSf = 1.8
3- Go to the chart and find SN for fdev = 5.5o
Trial # 3
This means the assumed factor of safety was not the right one. So we need to assume another FSf and solve the problem again for FSc.
Stability Number (c / gH)
Slope Angle b (deg)

## Slide 31
Since we complied three different trials, we are ready to find the right
factor of safety by using the 45o line method
Assumed FSf Calculated FSc
1.0 2.5
1.5 1.9
1.8 1.73
Chart: 
| 1 | 1.5 | 1.8
 | 2.5 | 1.9 | 1.73
1.75
1.75
So the correct FS is 1.75

## Slide 32
Zones are marked on the chart indicating whether the failure mode will be shallow or deep-seated.
If a deep-seated failure is indicated the soil layer must be sufficiently deep to enable this mechanism to occur.
There is a second chart due to Taylor which can be used when the depth of soil below the base of the slope is limited
This chart is only valid for f = 0
Taylor’s Chart - example

## Slide 33
Stability Number (c / gH)

## Slide 34
H= 8m
b=30o
Rock
Example 3:
Given:
cu = 20 kN/m2
fu = 0
gbulk = 15 kN/m3
F.S. = 1.5
Find:
Calculate the depth factor D
Solution
DH = 8+2 = 10 m
D= 1.25
H= 2m

## Slide 35
H= 8m
b=30o
Rock
Example 3:
Given:
cu = 20 kN/m2
fu = 0
gbulk = 15 kN/m3
DH = 10 m
Find:
Factor of Safety
Solution
D = 10/8 = 1.25
FSc = 1.01
H= 2m

## Slide 36
STATICALLY INDETERMINATE PROBLEMS
By Kamal Tawfiq, Ph.D., P.E
αi
Center
1
2
3
4
5
6
7
8
9
10
11
ϕ
αi
Resultant
Δxi
Si
Li
Wi
S + ΔS
Xi
R
Center
Ei
Ei + ΔE
Ti = c.Li + Neffi tan ϕ
ϕ
Ni = Neffi + ui Li
αi
bi
αi
θi
ai
αi
METHOD OF SLICES

## Slide 37
αi
Resultant
Δxi
Si
Li
Wi
S + ΔS
Xi
R
Center
Ei
Ei + ΔE
Ti = c.Li + Neffi tan ϕ
ϕ
Ni = Neffi + ui Li
αi
bi
αi
θi
ai
αi
Unknowns Associated with Force Equilibrium
n = Resultant normal forces Ni on the base of each slice or wedge
1 = Safety factor, which permits the shear forces Ti on the base of each
slice to be expressed in terms of Ni
n-1 = Resultant normal forces Ei on each interface between slices or wedges
n-1 = Angles αi which express the relationships between the shear force Si
and the normal force Ei on each interface
By Kamal Tawfiq, Ph.D., P.E

## Slide 38
FELLENIUS METHOD (ORDINARY METHOD, SWEDISH METHOD)
MR ∑CLi +(wicosθi -uiLi)tanϕ
MD ∑wi sinθi
=
=
F
By Kamal Tawfiq, Ph.D., P.E
αi
Resultant
Δx
L
Wi
Xi
R
Center
Ni = Neffi + ui L
αi
ϕ
Ti = c.L + Neff tan ϕ
αi
Ni = Neff + ui L
Ti = c.L + Neff tan ϕ
Wi
Wi cos α
Wi sin α
Effective Normal Stress
METHOD OF SLICES
αi
Center
1
2
3
4
5
6
7
8
9
10
11
ϕ

## Slide 40
1.5
1.0
Stiff Layer
Drain
= 125 lb/ft3
c = 90 lb/ft2
f = 32o
20 ft
Center of failure Surface
R = 30 ft
1
2
3
4
5
6
7
8
9
hw6
This example is from Lambe and Whitman (1969), John Wiley & Sons Publisher
Kamal Tawfiq, Ph.D., P.E.
Pore Water Pressure = u6 = hw6 x g water
hw7

## Slide 41
Slice | Width Dx (ft) | Ave Height (ft) | Weight (Kips) | qi | Wi sin qi | Wi cos qi | ui | Dli | Ui = ui Dli | Ni = Wi cosqi - Ui
1 | 4.5 | 1.6 | 0.9 | -1.7 | 0 | 0.9 | 0 | 4.4 | 0 | 0.9
2 | 3.2 | 4.2 | 1.7 | 2.9 | 0.1 | 1.7 | 0 | 3.2 | 0 | 1.7
3 | 1.8 | 5.8 | 1.3 | 8.05 | 0.2 | 1.3 | 0.03 | 1.9 | 0.05 | 1.25
4 | 5.0 | 7.4 | 4.6 | 14.5 | 1.2 | 4.5 | 0.21 | 5.3 | 1.1 | 3.4
5 | 5.0 | 9.0 | 5.6 | 24.8 | 2.3 | 5.1 | 0.29 | 5.6 | 1.6 | 3.5
6 | 5.0 | 9.3 | 5.8 | 35.4 | 3.4 | 4.7 | 0.25 | 6.2 | 1.55 | 3.15
7 | 4.4 | 8.4 | 4.6 | 47.7 | 3.4 | 3.1 | 0.11 | 6.7 | 0.7 | 2.4
8 | 0.6 | 6.7 | 0.5 | 55.1 | 0.4 | 0.3 | 0 | 1.2 | 0 | 0.3
9 | 3.2 | 3.8 | 1.5 | 60.4 | 1.3 | 0.7 | 0 | 7.3 | 0 | 0.7
 |  |  |  |  | 12.3 |  |  | 41.8 |  | 17.3
1- Using Ordinary Method of Slices (Swedish Method)
Kamal Tawfiq, Ph.D., P.E.
D
ksf

## Slide 42
(1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) |  | (9) | 
 |  |  |  |  |  |  | Mi |  | (7)/(8) | 
Slice | Width Dx (ft) | C Dxi (kips) | ui Dxi (Kips) | Wi-ui Dxi (Kips) | (5).(tan f) (Kips) | (3)+(6) (Kips) | Assume F=1.25 | Assume F=1.35 | F=1.25 | F=1.35
1 | 4.5 | 0.4 | 0 | 0.9 | 0.55 | 0.95 | 0.97 | 0.97 | 1.0 | 1.0
2 | 3.2 | 0.29 | 0 | 1.7 | 1.05 | 1.35 | 1.02 | 1.02 | 1.3 | 1.3
3 | 1.8 | 0.16 | 0.05 | 1.25 | 0.8 | 0.95 | 1.06 | 1.05 | 0.9 | 0.9
4 | 5.0 | 0.45 | 1.05 | 3.55 | 2.25 | 2.7 | 1.09 | 1.08 | 2.5 | 2.5
5 | 5.0 | 0.45 | 1.45 | 4.15 | 2.55 | 3.00 | 1.12 | 1.10 | 2.7 | 2.75
6 | 5.0 | 0.45 | 1.25 | 4.55 | 2.7 | 3.15 | 1.1 | 1.08 | 2.85 | 2.9
7 | 4.4 | 0.4 | 0.5 | 4.1 | 2.65 | 3.05 | 1.05 | 1.02 | 2.9 | 2.95
8 | 0.6 | 0.05 | 0 | 0.5 | 0.3 | 0.35 | 0.98 | 0.95 | 0.35 | 0.4
9 | 3.2 | 0.29 | 0 | 1.5 | 0.95 | 1.25 | 0.93 | 0.92 | 1.3 | 1.35
 |  |  |  |  |  |  |  |  | 15.8 | 16.09
2- Using Simplified Bishop Method
From the previous solution
Kamal Tawfiq, Ph.D., P.E.

## Slide 44
R
C

## Slide 45
R = 30 ft
1.5
1.0
Stiff Layer
Drain
= 125 lb/ft3
c = 90 lb/ft2
f = 32o
20 ft
Center of failure Surface
A
What is the pore water pressure at points A and B?
Name:__________ ID:________
CEG 4801 Geotechnical Design
Spring 2019
B