## Slide 1
Slope Stability
Analysis & Design

## Slide 2
Slope stability analysis is performed to assess the safe design of a human-made or natural slopes (e.g. embankments, road cuts, open-pit mining, excavations, landfills etc.) and the equilibrium conditions.
The main objectives of slope stability analysis are finding endangered areas, investigation of potential failure mechanisms, determination of the slope sensitivity to different triggering mechanisms, designing of optimal slopes with regard to safety, reliability and economics, designing possible remedial measures, e.g. barriers and stabilization.
Slope Stability Analysis and Design

## Slide 3
FACTORS AFFECTING SLOPE STABILITY
1- Soil Type
2- Geometry of the cross section (Height, slope angle, etc.)
3- Moisture Content
4- Pore water pressure
5- Additional loads
6- Shear Strength reduction
7- Vibrations and Earthquake
By Kamal Tawfiq, Ph.D., P.E.

## Slide 4
To Analyze and Design Slopes:
1- Planar Failures (Determinate Problems)
Infinite Failures Small depth, Long failure surface
Finite Slope Failures Simple wedge
Depth
b
H
2- Circular Failures (Determinate & Indeterminate Problems)
Above Toe
Through Toe
Deep seated
3- Wedge Failures Multiple Planer Failure
4- Complex Failures Combination of Planar & Circular
H
b

## Slide 5
W
T
N
Friction = N tan ddeveloped
Driving Force = T = W . sinb
b
Resisting Force = F = N tand = (W.cosb) tand
F.S. = Fresisting/Fdriving
The Concept of Developed Friction
Developed Friction
F.S. = 1 =
Resisting Force
Driving Force
F.S. = 2.5 =
Resisting Force
Driving Force
On the verge of failure
1. Planar Failures

## Slide 6
FACTOR OF SAFETY
1- For Shear Strength
tdeveloped = t / F.S.
tdeveloped = (c + σ tanϕ) / F.S.
2- For Shear Parameters
cd = c / F.S.
tanϕd = tanϕ / F.S.
3- For Height of the Slope
Hdesign = Hc / F.S.
Developed angle of friction
Developed cohesion or
Mobilized cohesion

## Slide 7
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, FV = W cos β
Weight = W
β
τ = N tanϕ
N = Fv = W cos β
INFINITE SLOPE
I. PLANAR FAILURE or Transitional Failure
H
1
b = 1 cosβ
A- Dry Soil (ϕ soil)
W = g H cosβ
b = 1 cosβ
By Kamal Tawfiq, Ph.D., P.E.
Shear Resistance

## Slide 8
G.S.
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, FV = W cos β
Weight = W
β
τ = N tanϕ
N = Fv = W cos β
1
b = 1 cosβ
A- Dry Soil (ϕ soil)
W = g H cosβ
b = 1 cosβ
Driving Force = FD = g H cos β sinβ
Resisting Force = FR = g H cos β cosβ tanϕ
FS = FR/FD
g H cos β sinβ
g H cos β cosβ tanϕ
FS =
tanϕ
FS =
tanβ
By Kamal Tawfiq, Ph.D., P.E.
β

## Slide 9
G.S.
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, FV = W cos β
Weight = W
β
τ = N tanϕ
N = Fv = W cos β
1
b = 1 cosβ
B- Submerged Soil (ϕ soil)
W = g H cosβ
Driving Force = FD = g H cos β sinβ
Resisting Force = FR = g H cos β cosβ tanϕ
FS = FR / FD
g H cos β sinβ
g H cos β cosβ tanϕ
FS =
tanϕ
FS =
tanβ
W.T
_
_
_
_

## Slide 10
C- Seepage Parallel to Slope (ϕ soil)
G.S.
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, Neff = (W – u) cos β
Weight = W
β
τ = Neff tanϕ
Neff = (W-u) cos β
1
b = 1 cosβ
Seepage
tanϕ
FS =
tanβ
gw Z
gsoilH cos2β
(1-
)
By Kamal Tawfiq, Ph.D., P.E.
Pore Water Pressure (u)
Z = Pressure Head
What is Pressure Head?
What is Total Head?
What is Elevation Head?
Total Head = Elevation Head+ Pressure Head
Go to Next Page

## Slide 11
Pressure
Head
Elevation
Head
Datum
Pressure
Head
Elevation
Head
Datum
Ground Surface
Failure Surface
Flow Line
Flow Line
Flow Line
Equipotential Line
Elevation
Head
Elevation
Head
Pressure
Head
phreatic line
Atmospheric Pressure Line
Pore Water Pressure (u)
=
Pressure head *( gwater )
=
g z
Total Head, Elevation Head and Pressure Head
Total Head = Elevation Head+ Pressure Head
Head Loss

## Slide 12
d
dw
b
W
T
N’
U
b/cos a
a
dwcos a
Soil Surface
Water Table
Assumed failure surface
For the infinite slope shown below, what is the pore water pressure at point A ?
A
a
Z
Z = dw cos a (cos a)
B
Z
Pore Water Pressure (u) = gwater * g z
Z = Pressure Head

## Slide 13
G.S.
Failure
Surface
H
β
Driving Force, FD = W sin β
Normal Component, FV = W cos β
Weight = W
β
t = C + N tanϕ
N = Fv = W cos β
1
b = 1 cosβ
D- Infinite Slope in c - ϕ soil (with seepage)
tanϕ
tanβ
FS =
c
gsoil H cosβ sinβ
gsoil H cos2β
(1-
u
)
If no seepage:
u = 0
If Submerged Slope:
u = 0 g = g’
By Kamal Tawfiq, Ph.D., P.E.
+

## Slide 14
Stability Number Ns
tanϕ
tanβ
FS =
c
gsoil H cosβ sinβ
gsoil H cos2β
(1-
u
)
= 1
Critical Height Hc at FS = 1
Ns =
c
gHc
ru =
u
gH
= pore water pressure ratio
Hc =
c
gsoil [sinβ cosβ - tanϕ (cos2β - ru)]
Hc =
c
gsoil cos2β (tanβ - tanϕ)
- u tanϕ
General Equation:
By Kamal Tawfiq, Ph.D., P.E.
+
H =
cdev
gsoil [sinβ cosβ - tanϕdev (cos2β - ru)]
Or
cdev =
c
FSc
tanfdev =
tanf
FSf
fdev = tan-1 ( )
tanf
FSf
(with seepage)
H
β
Weight = W
β
N = Fv = W cos β
W sinb
W cosb
t = C + N tanϕ
seepage

## Slide 15
γH
cd
= sinβ cosβ - tanϕd (cos2β - ru)
Ns =
Hc =
c
γsoil [sinβ cosβ - tanϕ (cos2β - ru)]
γHc
c
= sinβ cosβ - tanϕ (cos2β - ru)
Ns =
General Equation:
tanϕd =
tanϕ
FSf
cd =
c
FSc
H
β
β
seepage
ϕ = 45o
ϕ = 35o
ϕ = 25o
ϕ = 15o
Ns =
c
gHc
β
γH
cd
= sinβ cosβ - tanϕd (cos2β - ru)
Ns =

## Slide 16
Planar Slope Failure
Finite Slope
Fd = W.sinb
N = W.cosb
W
q
b
A
H
B
C
c =

## Slide 17
Example:
Given:
b= 30o
H = 10 ft
= 32o
c = 180 psf
Find:
F.S. of the Slope
Fd = W.sinb
N = W.cosb
W
q
b
A
H
B
C
c =