## Slide 1
A variety of charted solutions exist for the simple geometry considered above.
For the undrained (total stress) analysis of slopes charts produced by Taylor are often used.
The charts are based on the analysis of circular failure surfaces, and assume that soil strength is given by a Mohr-Coulomb analysis
Tension cracks are not considered
Stability Number

## Slide 2
Taylor’s Chart

## Slide 3
Taylor’s Chart
H = ?
30
o
cu = 20 kN/m2
fu = 10o
gbulk = 15 kN/m3
F.S. = 1.5
Since the factor of safety is given, then the problem indicates a design of a new slope
Solution:
Use the chart with i = 30o, and fmob = tan-1 (
tan 10o
1.5
)
= 6.7o
fmob
SN = 0.1 =
20/1.5
15 x Hdesign
Hdesign = = 8.88 m
20/1.5
15 x 0.1
SN = 0.1
Example - 1
fmobilized = fdeveloped

## Slide 4
Taylor’s Chart
H = 7 m
30
o
cu = 20 kN/m2
fu = 10o
gbulk = 15 kN/m3
F.S. = ????
Since the factor of safety is not given, then the problem indicates an existing slope which we need
to analyze it for its stability.
Solution:
2- Use the chart with i = 30o, and fmob = tan-1 (
tan 10o
1.0
)
= 10o
fmob
SN = 0.075 =
cmob
15 x 7
4- cmob = 15 x 7 x 0.075 = 7.87 kN/m2
5- FSc = c / cmob = 20/7.87 = 2.5
Therefore the Assumed FSf = the calculated FSc
SN = 0.075
Example - 2
1- Assume FSf = 1
3- Go to the chart and find SN for fmob = 10o
Trial # 1
fmobilized = fdeveloped

## Slide 5
This means the assumed factor of safety was not the right one. So we need
to assume another FSf and solve the problem again for FSc.
2- Use the chart with i = 30o, and fmob = tan-1 (
tan 10o
1.5
)
= 6.7o
SN = 0.1 =
cmob
15 x 7
4- cmob = 15 x 7 x 0.10 = 10.5 kN/m2
5- FSc = c / cmob = 20/10.5 = 1.9
Therefore the Assumed FSf = the calculated FSc
1- Assume FSf = 1.5
3- Go to the chart and find SN for fmob = 6.7o
Trial # 2
fmob
SN = 0.1
This means the assumed factor of safety was not the right one. So we need
to assume another FSf and solve the problem again for FSc.

## Slide 6
2- Use the chart with i = 30o, and fmob = tan-1 (
tan 10o
1.8
)
= 5.5o
SN = 0.11 =
cmob
15 x 7
4- cmob = 15 x 7 x 0.11 = 11.55 kN/m2
5- FSc = c / cmob = 20/11.55 = 1.73
Therefore the Assumed FSf = the calculated FSc
1- Assume FSf = 1.8
3- Go to the chart and find SN for fmob = 5.5o
Trial # 3
fmob
SN = 0.11
This means the assumed factor of safety was not the right one. So we need
to assume another FSf and solve the problem again for FSc.

## Slide 7
Since we complied three different trials, we are ready to find the right
factor of safety by using the 45o line method
Assumed FSf Calculated FSc
1.0 2.5
1.5 1.9
1.8 1.73
Chart: 
| 1 | 1.5 | 1.8
 | 2.5 | 1.9 | 1.73
1.75
1.75
So the correct FS is 1.75

## Slide 8
Zones are marked on the chart indicating whether the failure mode will be shallow or deep-seated.
If a deep-seated failure is indicated the soil layer must be sufficiently deep to enable this mechanism to occur.
There is a second chart due to Taylor which can be used when the depth of soil below the base of the slope is limited
This chart is only valid for f = 0
Taylor’s Chart - example

## Slide 10
Taylor’s Chart - example with finite depth
8 m
30
o
2 m
Rock
Calculate the Depth Factor D

## Slide 11
Taylor’s Chart - example with finite depth
8 m
30
o
2 m
Rock
DH
Calculate the Depth Factor D
DH = 10 m

## Slide 12
Taylor’s Chart - example with finite depth
8 m
30
o
2 m
Rock
DH
Calculate the Depth Factor D
DH = 10 m, H = 8m
D = 1.25

## Slide 14
Taylor’s Chart - example with finite depth
8 m
30
o
2 m
Rock
DH
D = 1.25
Cdev
15 x 8
= 0.165
Cdev = 0.165 x 15 x 8 = 19.8 kN/m2 FS = 1.01