## Slide 1: Geotechnical Investigation For Civil and Environmental Engineering projects
By
Kamal Tawfiq, Ph.D., P.E, F.ASCE
FLORIDA A&M UNIVERISTY – FLORIDA STATE UNIVERSITY
COLLEGE Of ENGINEERING
DEPARTMENT OF CIVIL & ENVIRONMENTAL ENGINEERING

## Slide 2
Lecture 1
Session 1
Introduction to Geotechnical Investigation
INTRODUCTION
Objectives:
To learn how to conduct geotechnical investigation for foundation projects
To review soil and rock properties needed for foundation analysis and design
Outcomes:
To apply fundamental knowledge of soil mechanics and geotechnical engineering to geotechnical investigation
Learning Tasks:
Assignments
Online quizzes

## Slide 3
Before we investigate the feasibility of any foundation project one should understand
the interaction between the human activities & the geologic environment
INTRODUCTION

## Slide 4
INTRODUCTION
Human Activities
&
Geologic Environment
Geometrical Changes
External Stresses
Altering Stresses in Soil Layers
Active Impact
Building Construction
Dams
Embankments
Roadways/ Railways
Underground Construction
Waterways
Earth Retaining Structures
Dewatering Facilities
Airports
Hydraulic Structures
Towers/Silos
Pipelines
Bridges
Passive Impact
Slope Failure
Flow / Landslides
Erosion
Flooding
Ground Subsidence
Settlement
Ground Failure
Piping
Heave
Earthquake

## Slide 5
Altering Stresses in Soil Layers
sv
sv
sh
sh
txy
txy
txy
txy
sv
sv
sh
sh
txy
txy
txy
txy
sv
sv
sh
sh
txy
txy
txy
txy

## Slide 6
An adequate assessment of the site should be done through
Geotechnical Investigation
INTRODUCTION

## Slide 7
INTRODUCTION
2. Conduct a thorough geotechnical investigation
This requires the skill and the knowledge to
Identify and describe rock & soil formations
Identify geologic hazards
Identify and describe rock & soil types
Define groundwater conditions
Procure samples
Perform field and laboratory testing
Samples
Continental United States Physiographic regions

## Slide 8
Primary processes in the geologic cycle
Igneous
Rock
Sedimentary
Rock
Metamorphic
Rock
Induration
Pyroclastic Ejection
Weathering
Physical or Chemical
Metamorphosis
Melting
Cooling
Magma
Weathering
Physical or Chemical
Metamorphosis
Melting
Pyroclastic Ejection
Weathering
SOIL
Identify and describe rock & soil formations
1/6

## Slide 9
Soil Formation
* Soil material is the product of rock
* The geological process that produce soil is WEATHERING Chemical and Physical
* Variation in Particle size and shape depends on:
1 - Weathering Process
2 - Transportation Process
* Variation in Soil structure depends on:
1 - Soil Minerals
2 - Deposition Process
flocculated
bookhouse
turbostratic
natural structure
Identify and describe rock & soil formations
2/6

## Slide 10
Soil Formation
* Transportation and Deposition
Four forces are usually cause the transportation (water, wind, ice, gravity) and deposition of soils
1-Water Alluvial Soil
1- Fluvial
2- Estuarine
3- Lacustrine
4- Coastal
5- Marine
Identify and describe rock & soil formations
3/6

## Slide 11
2- Ice Glacial Soils
Hard Pan
Terminal Moraine
Esker
Kettles
Identify and describe rock & soil formations
4/6

## Slide 12
3- Wind Aeolian Soils
4- Gravity Colluvial Soil
1-Talus
Sand Dunes
Loess
5/6
Identify and describe rock & soil formations

## Slide 13
Identify and describe rock & soil formations
Continental United States Physiographic Regions Include
8 regions,
25 provinces, and
85 sections
6/6

## Slide 14
Identify and describe rock & soil types
Rock Type
Soil Type
Igneous Rock
Sedimentary Rock
Metamorphic Rock
Residual Soil
Transported Soil

## Slide 15
Question
What type of soils are usually produced in nature by the different weathering & Transportation processes?
- Boulders
- Gravel
- Sand
- Silt
- Clay
* These soils can be - Dry
- Saturated -Fully
- Partially
Also they have different shapes , textures , structures
Shapes ....... Elongated
Rounded
Plated
Angular
Texture ......... Coarse
Medium
Fine
Structures..... Loose
Dense
Honeycombed
Dispersed
Flocculated

## Slide 16
Geotechnical Investigation
Steps of Geotechnical Investigation
Data Collection
Terrain Analysis
Site Exploration
Subsurface Sectioning
Sample Recovery
Soil Testing

## Slide 17
1. Data Collection
1.1 Type of structure
1.2 General use of the structure
1.3 Column load
1.4 Column spacing
1.5 Building code
1.6 Basement requirements
1.7 Topography maps
1.8 Geological maps
1.9 Soil Maps
1.10 Groundwater maps
1.11 Report, Ariel photographs, satellite images, etc.
Geotechnical Investigation

## Slide 18
2 Terrain Analysis
Using remote sensing and landform interpretation techniques to determine:
2.1 Geomorphic characteristics on the site (Landform)
2.2 Relief amplitudes
2.3 Drainage basins
2.4 Vegetation
2.5 Climate conditions, weathering, frost action, erosion, and mass wasting
Geotechnical Investigation

## Slide 19
3. Site Exploration
It is a field trip to inspect:
3.1 General topography, existing drainage, ditches, etc.
3.2 General conditions of the soil
3.3 Type of vegetation
3.4 Surface water condition
3.5 Accessibility of the site
Geotechnical Investigation

## Slide 20
4. Subsurface Sectioning
This includes the following
4.1 Test Pits (for shallow depths)
4.2 Auger Boring (Manual, Mechanical)
4.3 Wash Boring
4.4 Core boring
4.5 Special Methods - Seismic refraction
GPR
Electric Resistivity
Geotechnical Investigation
The depth and the interval of the subsurface sectioning is governed by:
Type of construction
Column Load
Column spacing
Test boring is the most usable method.
In planning and executing the test boring
you need to know:
Equipment Selection
Boring Spacing
Boring Depths
Boring Spacing:
Depending on the area under study, a grid systems may be appropriate in uniform conditions.
The spacing usually ranges from 30 ft to 1600 ft. The following spacing may be adopted for wide range of construction:
1- Multistory Buildings 30 ft to 100 ft
2- Residential Subdivision 800 ft to 1600 ft
3- Warehouses, Industrial plants 60 ft to 200 ft
4- Dams and Dikes 130 ft to 260 ft
5- Highways and Railways 800 ft to 1600 ft
** In general spacing may vary depending on the irregularity of the site geology.
Depth of Boring:
1- Boring should be extended through any unsuitable foundation strata (unconsolidated fill, organic soils, compressible layers until soil of acceptable bearing capacity is reached.
2- In general, boring should be extended to at least 1.5 to 2 times the minimum width of the loaded area.
3- In the case of very heavy structures (bridges), boring in most cases are extended to bedrock, or at least one boring should be extended to bedrock.
4- The following empirical equations can be used to estimate the minimum depth of borings in office buildings:
Db = 3 S0.7 (for light steel or narrow concrete buildings)
Db = 6 S0.7 (for heavy steel or wide concrete buildings)
Where S = number of stories in meters
Equipment Selection for Subsurface Sectioning
This depends on:
1- Terrain features
2- Accessibility
3- Geological conditions
4- Boring Depths
5- Sample types
6- Nature of the project

## Slide 21
4. Subsurface Sectioning
Geotechnical Investigation
Areas of investigation | Boring depth
Large structure with separate closely space footings | Extend to depth where increase in vertical stress for combined foundations is less than 10 percent of effective overburden stress. Generally all boring should extend to no less than 9 m (30 ft) below lowest part of foundation unless rock is encountered at shallower depth.
Isolated rigid foundations | Extend to depth where vertical stress decreases to 10 percent of bearing pressure. Generally all borings should extend no less than 9 m (30 ft) below lowest part of foundation unless rock is encountered at shallower depth.
Long bulkhead or wharf wall | Extend to depth below dredge line between 0.75 and 1.5 times unbalanced height of wall. Where stratification indicates possible deep stability problem, selected borings should reach top of hard stratum.
Deep cuts | Extend to depth between 0.75 and 1 times base width of narrow cuts. Where cut is above groundwater in stable materials, depth of 1.2 to 2.4 m (4 to 8 ft) below base may suffice. Where base is below groundwater, determine extent of previous strata below base.
Dams and water retention structures | Extend to depth of 0.5 base width of earth dams or 1 to 1.5 times height of small concrete dams in relatively homogeneous foundations. Borings may terminate after penetration of 3 to 6 m (10 to 20 ft) in hard and impervious stratum if continuity of this stratum is known from reconnaissance.
High embankments | Extend to depth between 0.5 to 1.25 times horizontal length of side slope in relatively homogeneous foundation. Where soft strata are encountered, borings should reach hard materials.
From NAVFAC DM-7.1, 1982.

## Slide 22
Boussinesq’s Equation for Vertical Stress Caused by a Rectangularly Loaded Area
4. Subsurface Sectioning
Dsc = q Ic
0.1 q = q Ic
q
0.1 q
m = B/Z n = L/Z
′
′
Z

## Slide 23
4. Subsurface Sectioning
Boring depth using Richard et al. 1979 Chart
Boring Depth Using Boussinesq’s Equation for Square loading
(RICHARD D. BARKSDALE AND MILTON O. SCHREIBER, 1979)

## Slide 24
EXAMPLE
Given
7 ft square footing
Contact pressure of 5000 lb/ft2
Wet unit weight of the soil = 115 lb/ft3. Water table is estimated to be 40 ft beneath the footing.
Find
The minimum depth of test boring
Db
4. Subsurface Sectioning
Boring depth
7 ft
Contact pressure of 5000 lb/ft2
gwet= 115 lb/ft3

## Slide 25
EXAMPLE
Solution
Since the water table is estimated to be 40 ft beneath the footing and the footing's width is 7 ft, the soil's wet unit weight should be used
Using gwet =115 lb/ft3,
Contact pressure = 5000 lb/ft2, and Width of footing =7 ft,
Db ~ 21.5 ft. use 22 ft.
4. Subsurface Sectioning
Boring depth
7 ft
Contact pressure of 5000 lb/ft2
gwet= 115 lb/ft3

## Slide 26
Δqs
Z
X
R
X/R
Z/R
1
2
3
4
1
2
3
0
0.90
0.80
0.70
0.30
0.50
0.40
0.10
0.20
Δqs
ΔPz/qs
0.60
Circular Load: (Vertical Stress)/(Surface Stress)
0.05
σz = σ1
σz = σ1
σx = σ2
σx = σ2
0.15
R = Radius
4. Subsurface Sectioning

## Slide 27
5. Sample Recovery
5.1 Methods of Sample Recovery
  Hand auger
  Split spoon
  Backhoe
  Thin wall tube (Shelby tube)
5.2 Soil samples obtained during sectioning are either:
  Disturbed
  Undisturbed
Geotechnical Investigation
Disturbed soil samples are used for
  Grain size analysis
  Determination of index properties
  Organic content
  Specific gravity
Undisturbed samples are used for
  As for disturbed sample
  Determining mechanical properties
  Determining hydraulic properties

## Slide 28
Geotechnical Investigation
Methods of Sample Recovery
  Hand auger
The practical depth of investigation using a hand auger
depends upon the soil properties and depth of investigation.
Test pit

## Slide 29
Geotechnical Investigation
Methods of Sample Recovery
  Split spoon
Split spoon sampling methods are used primarily to collect shallow and deep subsurface soil samples.
All split spoon samplers, regardless of size, are basically split cylindrical barrels that are threaded on each end.
Split spoon sampling method is used to obtain disturbed and undisturbed samples.
- The sampler is driven in into the soil by a hammer
- The weight of the hammer is 140 lb
- The number of blows (N) required to penetrate the spoon of three 6 in. intervals are added and recorded.
This procedure is called the Standard Penetration Test (SPT)
Actually, the Standard Penetration Number N is the number of blows of the last two intervals (12 in.) The first interval (6 in.) is usually discarded (why??????????)
18 to 30 in

## Slide 30
Geotechnical Investigation
THE STANDARD PENETRATION TEST (SPT) ASTM D1586
- The SPT is one of the most popular and economical means to obtain subsurface information.
- The testing method was standardized in 1958 as ASTM D1568
The test consists of:
* A 140 lb driving mass falling from a height of 30 in.
* Drive the standard split spoon sampler a distance of 18 in. into the soil
* Counting the number of blows (N) to drive the sampler 12 in.
(6 in. + 6 in.)
* The boring log should show "refusal" and should be halted if:
a- 50 blows are required for any 150 mm increment
b- 100 blows are obtained
c- 10 successful blows produce no advance
* N should be corrected for the increase of the overburden pressure
Hollow Stem Auger

## Slide 31
THE STANDARD PENETRATION TEST (SPT) ASTM D1586
See attached SPT video

## Slide 32
Amount of
removed sv
Example
Nfield = 40
Corrections for SPT Field Blow-count (NField)
1- Peck & Bazaraa (1969) suggested
Ncor = For (sv < 1.5 kips/ft2)
Ncor = For (sv > 1.5 kips/ft2)
2- Peck, Hanson, and Thornburn (1974) proposed
Ncor = ( ) (Nf) For (sv in tons/ft2)
4 Nf
1 + 2 sv
4 Nf
3.25 + 0.5 sv
0.77 log
20
sv
sv = Vertical effective stress at the sampling depth (kips/ft2)
1 kip = kilopound = 1000 lb = 4448.2216 Newtons (N) = 4.4482216 kilonewtons (kN)
1 US ton = 2000 lb

## Slide 33
Corrections for SPT Field Blow-count (NField)
Amount of
removed sv
Example
Nfield = 40
Example 1:
Given:
SPT = 40 at 20’ in sand
gsand = 115 lb/ft3
Find:
Ncor = ??
Solution:
Using Peck, Hanson, and Thornburn (1974) equation
CN = 0.77 log (20/sv)
sv = (20) (115 )/ 2000(lb/ton) = 1.15 tons/ft2
CN = 0.77 log (20/1.15) = 0.955
Ncor = (0.955) (40) = 38
0.77 log
20
sv
Ncor = ( ) (Nf) For (sv in tons/ft2)

## Slide 34
Corrections for SPT Field Blow-count (NField)
Amount of
removed sv
Example
Nfield = 40
Example 2:
Given:
SPT = 40 at 20’ in sand
gsand = 115 lb/ft3
Find:
Ncor = ??
Solution:
Using Peck & Bazaraa (1969) equation
sv = [(20)(115) / 1000 (lb/kip)] = 2.3 kips/ft2
Since sv is > 1.5 kips/ft2 use
Ncor = 4 (40) / [3.25+(0.5)(2.3)] = 36
4 Nf
3.25 + 0.5 sv
Ncor =
For (sv > 1.5 kips/ft2)

## Slide 35
Corrections for SPT Field Blow-count (NField)
Skempton (1986) suggested the following correction for the SPT field blow-count Nf
N60 =
Where:
Em = Hammer efficiency (for U.S. equipment, Em= 0.6 for a safety hammer,
and 0.45 for a doughnut hammer). For automatic systems that lift the
hammer and allow it to drop unimpeded can deliver higher energy to the drill rods
with values of Em as high as 95 percent (ASTM D 6066-96, 2004).
Cb = Borehole diameter correction (Cb = 1.0 for borehole = 65 to 115 mm diameter, 1.05 for 150 mm diameter, and 1.15 for 200 mm diameter)
Cr = Rod length correction (Cr = 0.75 for up to 4 m for drill rods, 0.85 for 4 to 6 m drill rods, 0.95 for 6 to 10 m drill rods, and 1.00 for rods in excess of 10 m)
As an average value N60 = 0.5 to 0.67Nf
Em Cb Cr Nf
60
Assuming 60% hammer efficiency
doughnut hammer
safety hammer
Automatic hammer

## Slide 36
Correction of N Value for foundations in an earthquake zone
engineering, such as liquefaction analyses, the standard penetration test N60 value is corrected for the overburden soil pressure, also known as the effective overburden pressure or the vertical effective stress (sv).
Where:
(N1)60 = standard penetration test N value corrected for both field testing procedures and overburden pressure
CN = correction factor to account for the overburden pressure, and it is approximately equal to (100/sv)0.5 where sv is the vertical effective stress, in kPa.
Suggested maximum values of CN range from 1.7 to 2.0 (Youd and Idriss, 1997, 2001).
N60 = standard penetration test N value corrected for field testing procedures.
The N60 is calculated by using Skempton’s equation.
(N1)60 = CN N60 =
100
sv
0.5
N60
Em Cb Cr Nf
60
N60 =

## Slide 37
Curves showing the relationship between bearing capacity factors and f, as determined by theory, and rough empirical relationship between bearing capacity factors or f and values of standard penetration resistance N.
Peck et al. (1974)
Relationship between bearing capacity factors, f, and SPT
Example
Given:
Nf =40
Water Table = 5’
gsoil = 120 pcf
Find:
Nq, Ng and f
Solution:
sv = {(5)(120)+[15(120-62.4)]}/2000 lb/ton =
= ton/ft2
Ncor = CN Nf = 0.77 log (20/ ) =
Nq, = Ng = f =
W.T.
5 ft
15 ft
Nf =40
gsoil = 120 pcf
Angle of Internal Friction, f (degrees)
Bearing Capacity Factor, N g & N q
Standard Penetration Resistance, N ( Blows/ft)
Nq
Ng

## Slide 38
Cone Penetration Test (CPT )
The most common type of mechanical penetrometer is the Dutch
mantle cone and is abbreviated CPT.
The cone is pushed into the soil to the desired depth (initial position) and then force is applied to the inner rod, which moves the cone downward into the extended position.
The cone is pushed into the soil at a rate of about 2 to 4 ft/min (10 to 20 mm/sec). The required force to move the cone into the extended position divided by the horizontally projected area (10 cm2) of the cone is defined as the cone resistance qc , also known as the cone bearing or the end bearing resistance.
By continually repeating the two-step process
shown in the figure, the cone resistance qc is
obtained at increments that ordinarily
do not exceed 8 in. (20 cm).
Geotechnical Investigation
2 to
4 ft/min

## Slide 39
Cone Penetration Test (CPT )
Standard
Piezocone
Type 1
Piezocone
Friction
CPT
Type 2
Piezocone

## Slide 40
Cone Penetration Test (CPT )
Special features of the cone penetration test are as follows:
Cone resistance versus depth.
A considerable amount of work has been performed in correlating cone resistance qc with subsurface conditions. Figure1 presents four examples, where the cone resistance qc has been plotted versus depth below ground surface. The shape of the cone resistance qc plots versus depth can be used to identify sands, clays, cavities, or rock.
Figure1: Simplified examples of CPT cone resistance qc versus depth, showing possible interpretations of soil types and conditions. (From Schmertmann, 1977.)
NC Clay
Sand
NC Clay
NC Clay
Sand
Dense
Sand

## Slide 41
Cone Penetration Test (CPT )
Special features of the cone penetration test are as follows:
2. Friction ratio.
The figure below illustrates the two-step process that can be used to obtain the soil friction along a side sleeve fs.
1- In the first step, the cone resistance is obtained (qc) = 1000 psi
2- in the second step, the cone plus sleeve friction is determined (qc + fs) = 1440 psi
3- Subtraction gives the sleeve friction (fs) = 440 psi
The friction ratio (FR) can then be calculated, defined as FR = sleeve friction (fs) divided by cone resistance = (fs/qc )x100. By knowing the friction ratio (FR) and cone resistance qc, the type of soil can be estimated by using Fig. 2.
Test sequence for obtaining the sleeve friction from the Dutch cone penetrometer and an example of the test data plotted versus depth.
Cone Resistance
Friction Resistance
Friction Ratio

## Slide 42
Cone Penetration Test (CPT )
Figure 2: Guide for estimating soil type from Dutch mantle cone
Steps:
1- Enter chart with cone resistance qc and friction ratio
2- FR = sleeve friction divided by cone resistance = (fs / qc)x100.
(From Schmertmann, 1977)
Figure 2:
qc
FR

## Slide 43
Cone Penetration Test (CPT )
Other Cone Penetrometers.
Besides the mechanical cone, there are other types of cone penetrometers, such as:
Electric cone. A cone penetrometer that
uses electric-force transducers built into the apparatus for measuring cone resistance
and friction resistance.
Piezocone. A cone penetrometer with the additional capability of measuring pore water pressure generated during the penetration of the cone.
Special devices. The cone can even be
equipped with a video camera to enable
the type of soil to be viewed during the
test (Raschke and Hryciw, 1997).

## Slide 44
Because of these factors, in the United States, the CPT is used less frequently than the SPT.
Cone Penetration Test (CPT )
A major advantage of the cone penetration test (CPT)
- It provides almost a continuous subsurface record of the cone resistance qc and fs
This is in contrast to the SPT, which obtains data at much larger intervals in the soil deposit.
Disadvantages of the CPT are that soil samples cannot be recovered and special equipment is required to produce a steady and slow penetration of the cone.
Unlike the SPT, the ability to obtain a steady and slow penetration of the cone is not included as part of conventional drilling rigs.

## Slide 45
Seismic refraction (for large areas)

## Slide 46
Ground Penetration Radar (GPR)

## Slide 47
Ground Penetration Radar (GPR)

## Slide 48
Geo-electrical Profiling using Electrical resistivity or D.C. Resistivity Method
Schematic Illustrating Basic Concept of
D.C. Resistivity Crew In Operation Electrical Resistivity Measurement
Good for sensing buried wastes and waste migration

## Slide 49
Geotechnical Investigation
top
bottom
bottom
top

## Slide 50
Rotary core barrel
Coring bits are commonly 1.75 to 5.25 inches in diameter.
Diamond or Tungsten carbide insets on rotary coring bit.

## Slide 51
Core recovery parameters describe the quality of core recovered from a borehole.
Total core recovery (TCR)
TCR is the borehole core recovery percentage.
TCR is defined as the quotient:
% TCR = ( ) x 100
Lsum of pieces = Sum of length of core pieces
Ltotal core run = Total length of core run
∑ Lsum of pieces
Ltotal core run

## Slide 52
Core recovery parameters describe the quality of core recovered from a borehole.
Solid core recovery (SCR)
Solid core recovery (SCR) is the borehole core recovery percentage of solid, cylindrical, pieces of rock core.
SCR is defined as the quotient:
SCR = ( ) x 100
Lsum of solid core pieces
Ltotal core run

## Slide 53
RQD | Rock mass quality
<25% | very poor
25-50% | poor
50-75% | fair
75-90% | good
90-100% | excellent
Rock Quality Designation (RQD) Factor
Developed in 1964 by Deere
Rock-Quality Designation (RQD) is a rough measure of the degree of jointing or fracture in a rock mass, measured as a percentage of the drill core in lengths of 10 cm or more.
∑ Lsum of 10cm
Ltotal core run
RQD = x 100
Lsum of 10cm = Sum of length of core sticks longer than
10 cm measured along the center line of the core
From the RQD index the rock mass can be classified as follows:

## Slide 54
Rock Quality
Length, L
0.8 ft
0.7 ft
0.8 ft
0.6 ft
0.2 ft
0.7 ft
Sound
Not sound, highly weathered
Not sound, centerline pieces < 4 inches, highly weathered
Sound
Not sound
Sound
Core Run
Total = 4 ft
CR = 95% RQD = 53%

## Slide 55
NEW SECTION

## Slide 56
Geotechnical Investigation
MEASUREMENTS OF MATERIAL PROPERTIES
Soil Properties
Physical properties
Index Properties
Hydraulic Properties
Mechanical Properties

## Slide 57
MEASUREMENTS OF MATERIAL PROPERTIES
Methods of Measurement
1- Laboratory Testing Methods
2- In-Situ Testing Methods
3- Empirical Correlation's
Terzaghi & Peck (1948): Cc = 0.009 (wc – 10%)
Skempton (1944): Cc 0.007 (wc – 7%)

## Slide 58
MEASUREMENTS OF MATERIAL PROPERTIES
Methods of Measurement
1- Laboratory Testing Methods
- Provide better control over the boundary conditions
- Different parameters can be determined individually or in
combination
- Results can be produced

## Slide 59
MEASUREMENTS OF MATERIAL PROPERTIES
Methods of Measurement
2- In-Situ Testing Methods
Measurements of properties for large soil masses
Less disturbance
Measurements under real field conditions
Can be performed during site exploration (SPT & CPT)
In-Situ testing methods are used to determine:
1- Hydraulic properties (Wells)
2- Mechanical properties (SPT, CPT, Vane Shear Test,
Pressuremeters, CBR) (See Table 3.20)

## Slide 60
MEASUREMENTS OF MATERIAL PROPERTIES
Soil Properties
1- Physical properties: Used to describe the soil. These properties are incorporated with the soil classification systems, and in some cases they are related to the mechanical properties
- Specific gravity
- Grain size
- Density (Saturated, Partially saturated, submerged, minimum,
maximum, relative, optimum moisture content)
- Porosity
- Degree of saturation
- Void ratio
- Moisture content
- Hardness (for rocks)
- Durability (for rocks)
- Reactivity (for rocks)

## Slide 61
MEASUREMENTS OF MATERIAL PROPERTIES
Soil Properties
2- Index Properties: Used to classify the soil or to correlate with the mechanical properties.
- Atterberg Limits or Consistency Limits (LL, PL SL) - Moisture Content vs. Unit Weight Relationship (Compaction) - Grain Size Distribution
- Relative Density Dr
Relative Density Dr
PL
LL
Proctor Test
Grain Size Distribution

## Slide 62
MEASUREMENTS OF MATERIAL PROPERTIES
Soil Properties
3- Hydraulic Properties
- Permeability or Hydraulic Conductivity (k)
Infiltration Rate
Double Ring Infiltrometer

## Slide 63
Direct Shear
MEASUREMENTS OF MATERIAL PROPERTIES
Soil Properties
4- Mechanical Properties: To describe the behavior of the soil under different types of stresses
-Deformation Moduli – Young's Modulus (E) & Shear Modulus (G)
Consolidation (Cc, Cs, Cv, Pc, mv, K)
Strength (c, f) Unconfined Compression
Direct Shear,
Triaxial Compression
California Bearing Ratio (CBR) or
Lime Rock Bearing Ration (LBR)
used for pavement design
Unconfined
Compression
Triaxial Compression
Consolidation Test

## Slide 64
MEASUREMENTS OF MATERIAL PROPERTIES
Methods of Measurement
3- Empirical Correlations
- Correlations are usually based on basic or index properties
- These properties are correlated with the mechanical & hydraulic properties
- Used to provide basis for all engineering analysis
- Reduce the cost of geotechnical investigation
- Presented as ----- Tables, Charts, and Equations
For example Beyer formula for coefficient of permeability (k)
K = C . (d10)2
Where :
C = 4.5x10-3 log
U = Uniformity coefficient = d60/d10
d10 = Effective diameter (mm)
d10
10%
Passing
500
U

## Slide 65
Reporting Geotechnical Investigation
Both an adequate geotechnical investigation and a comprehensive geotechnical report are necessary to construct a safe, cost-effective project.
While the geotechnical report content and format will vary by project size and highway agency, all geotechnical reports should contain certain basic essential information, including:
Cover letter and Executive summery
Scope of the Project
Site Description
Proposed Construction
Summary of all subsurface exploration data, including subsurface soil profile, exploration logs, laboratory or in situ test results, and ground water information;
Interpretation and analysis of the subsurface data; Specific engineering recommendations for design;
Discussion of conditions for solution of anticipated problems; and Recommended geotechnical special provisions.

## Slide 66
Geotechnical Report Production

## Slide 67
Geotechnical Report Production

## Slide 68
Geotechnical Report Production
1- Map of the Project Location

## Slide 69
Geotechnical Report Production
2- Boring Locations

## Slide 70
Geotechnical Report Production

## Slide 71
3- Boring Log:
Soil description and classification
Sample depth
SPT field value
Water Table
Geotechnical Report Production

## Slide 72
Soil description and classification
Sample
SPT field value
(5+5+8)
13
3- Boring Log:

## Slide 73
4- Profile of Soil Layers:

## Slide 74
Geotechnical Report Production
4- Profile of Soil Layers:

## Slide 75
4- Profile of Soil Layers:

## Slide 76
6- Soil Testing Results

## Slide 77
5- Soil Testing Summery