## Slide 1
FAMU-FSU College of Engineering
Department of Civil and Environmental Engineering
CEG 3011
Soil Mechanics
Fall 2019
Homework # 8
Soil Strength
Solved the Following Problems
The following are the results of four direct shear tests on sandy soil. If the size of each specimen is 44 mm x 44 mm, draw a graph for the shear stress at failure against the normal stress, and determine the shear strength parameter of the soil.
Test No. | Normal Force (N) | Shear Force at Failure (N)
1 | 200 | 82
2 | 300 | 120
3 | 400 | 160
4 | 550 | 220

## Slide 2
Solution

## Slide 6
Triaxial Shear Test
s1 = s3+ Dp
s1 = s3+ Dp
c=Soil Cohesion
f = Angle of Friction of the Soil (Friction between soil particles)
f
c and f = soil strength parameters
t = c + sn tanf
s3
s3
s3
s3
Dp
Dp
Dp = Deviator Stress
s3= Confining Stress
s1= Vertical Stress
s1 =s3+Dp

## Slide 7
1.44
1.44+5.76
2.88+6.85
2.88
4.32+7.50
4.32
t = c + sn tanf